## Slide 1: Passive Scanning Improvement
Date: 2011-09-20
Authors:

## Slide 2: Abstract
This presentation addresses how to improve passive scanning in the context of TGai providing Fast Initial Link Set-Up

## Slide 3: Conformance w/ Tgai PAR & 5C
Conformance Question | Response
Does the proposal degrade the security offered by Robust Security Network Association (RSNA) already defined in 802.11? | No
Does the proposal change the MAC SAP interface? | No
Does the proposal require or introduce a change to the 802.1 architecture? | No
Does the proposal introduce a change in the channel access mechanism? | No
Does the proposal introduce a change in the PHY? | No
Which of the following link set-up phases is addressed by the proposal? (1) AP Discovery (2) Network Discovery (3) Link (re-)establishment / exchange of security related messages (4) Higher layer aspects, e.g. IP address assignment | 1
Marc Emmelmann, FOKUS

## Slide 4: AP vs. Network Discovery
AP Discovery:
  Find APs (any or specific SSIDs)  criteria for selection within .11 / no need to query for information of offered network service (e.g. does this AP provide access to T-Mobile customers etc.)
  Sufficient for enterprise, home, and industrial scenarios where AP selection can be based on SSID
Network Discovery:
  Currently required AP discovery beforehand (as AQNP msg. Exchange is unicast)
  Retrieve information on services “behind the AP”
Combination of phases:
  Today: AP Discovery + (optional) AP Discovery
  TGai solution space different approaches to suite different scenarios
    Optimize AP Discovery  covers enterprise, industry, home scenarios; usually no extra Network Discovery
    Optimize Network Discovery  might yield to solutions where we do not need a separate AP discovery any more, i.e. intelligently combine both phases
Focus of this talk

## Slide 5: State of the Art Passive Scanning
Scan through all available channels
STA “shall listen to each channel scanned for no longer than a maximum duration defined by the MaxChannelTime“ [11REVmb-D4, Cls 11.1.3.1]

## Slide 6: Main Idea – Stop after having found the 1st “suitable” AP
Only possible in vendor specific implementations:
  “shall listen to each channel scanned for no longer than a maximum duration defined by the MaxChannelTime“ [11REVmb-D4, Cls 11.1.3.1]  does not prohibit a STA to quit before MaxChannelTime
  Still have to go through all channels
  BUT: currently, there is not option to the MLME-SCAN.request primitive forcing this behavior.
Idea: If a MIB variable is set (e.g.: dot11FILSscanFor1stApOnly is set to 1), the scanning returns after having detected the 1st suitable AP.
  Remaining channels to be scanned are ignored
We currently have methods of selecting to look only for specific APs via [11Revmb-D9, 6.3.3.2.2]
  SSID List (11k)
  AccessNetworkType (11u)
  HESSID (11u)

## Slide 7: Straw Polls
Are you interested in seeing additional presentations, and proposed draft amending text, addressing how to optimize passive scanning (assuming enterprise scenarios where network discovery is not necessary)?
  Yes:
  No:
Are you interested in seeing additional presentations, and proposed draft amending text, addressing how to optimize passive scanning in combination with network discovery (e.g. for Hotspot 2.0 scenarios)?
  Yes
  No

## Slide 8: References
11-10/922r2: Achievable gains in AP discovery (Marc Emmelmann, Fraunhofer FOKUS)
11-10/965r1: Potential performance improvement with fast initial link set-up (Marc Emmelmann, Fraunhofer FOKUS & Root Inc.)
11-11/1237: TGai Key Technical Ideas (M. Emmelmann, Fraunhofer FOKUS)