## Slide 1: TGai Key Technical Ideas
Date: 2011-09-19
Authors:

## Slide 2: Abstract
Accompanying slide set for the TGai Tutorial on Monday, September 19, 2011, Okinawa Interim Meeting.
Main concepts and initial evaluation based on material presented in the SG Phase. TGai will see first technical presentations (with more details) this week.

## Slide 3: Focus of TGai
TGai focuses on reducing the time spent in any phase of the initial link set-up
Phase |  |  |  | Auth. & Assoc. | 
FIA has analyzed the performance of all link set-up phases (as imposed by IEEE 802.11-2007) and identified potentials for performance improvement
The following summary of this analyzes illustrates some initial technical approaches on how to reduce the time spent in the initial link set-up phase
Phase | AP Discovery | Network Discovery | TSF Sync. (1 additional scan) | Auth. & Assoc. | Higher Layer (DHCP / IP)

## Slide 4: Access Point Discovery: Today
Note:
  Qi & Walker (11-10/853r1) provide worst case approximations of up to 3400ms.
  11-10/922r2 contains details how the assumptions behind the expected mean calculation for the values presented herein
Passive scanning
Active scanning
No Assumptions (scan all channels), find all APs
2.4 GHz
5 GHz
1100 ms
Expected Mean of time spent in scanning for
2300 ms
102 ms
n/a
Potentials for improvement:
  Return from scanning procedure after having found the 1st AP
  Use “external” knowledge on which channels to scan
  What about 5GHz operation—really only passive scanning or are there potential alternatives for faster AP discovery?
  Source: 11-10/922r2

## Slide 5: AP Discovery: Return after 1st AP is found
Passive scanning
Active scanning
No Assumptions (scan all channels), find all APs
2.4 GHz
5 GHz
1100 ms
Expected Mean of time spent in scanning for
2300 ms
102 ms
n/a
No Assumptions (scan all channels), stop after 1st APs is found
2.4 GHz
5 GHz
550 ms
1150 ms
22 ms
n/a
Amendment required
Passive scanning
  Theoretically, this is possible: “shall listen to each channel scanned for no longer than a maximum duration defined by the MaxChannelTime“ [11REVmb-D4, Cls 11.1.3.1]
  BUT: currently, there is not option to the MLME-SCAN.request primitive forcing this behavior.
Active scanning:
  Not possible right now: “…. [scan until] ProbeTimer reaches MaxChannelTime, process all received probe responses“ [11REVmb-D4, Cls 11.1.3.2.2]
  Source: 11-10/922r2

## Slide 6: AP Discovery: Reduction of number of channels to scan
Passive scanning
Active scanning
No Assumptions (scan all channels), find all APs
2.4 GHz
5 GHz
Reduce number of channels (to 1) where APs are known to operate
2.4 GHz
5 GHz
2.4 GHz
5 GHz
1100 ms
Expected Mean of time spent in scanning for
2300 ms
102 ms
n/a
17 ms
n/a
100 ms
100 ms
Return after 1st AP Responses (scan 1 channel)
50ms
50ms
2 ms
No Assumptions (scan all channels), stop after 1st APs is found
2.4 GHz
5 GHz
550 ms
1150 ms
22 ms
n/a
11k may work, but not for initial link set-up
Amendment required
Combine both: Amendment required
Amendment required
Moving from one BSS to another (note: not in scope of FIA SG, but mentioned for completeness)
  11k neighbor report can provide information on which channels APs operate
Initial link-set up
  Not possible right now (STA is not within a BSS in order to query a neighbor report)
  Possible approach: allow input via management plane
  Source: 11-10/922r2

## Slide 7: AP Discovery: Enablement of 5GHz active scanning via 2.4 GHz
APs with simultaneous dual-band operation are common (esp. in commercial environments)
AP has knowledge on the 5GHz channels it is operating on
Provide information on 5GHz operation / channels via 2.4GHz channel to STA  STA can immediately synchronize via active scan on 5GHz channel (if legislation permits)
Passive scanning
Active scanning
No Assumptions (scan all channels), find all APs
2.4 GHz
5 GHz
Reduce number of channels (to 1) where APs are known to operate
Enablement at 5GHz via 2.4 GHz
2.4 GHz
5 GHz
2.4 GHz
5 GHz
1100 ms
Expected Mean of time spent in scanning for
2300 ms
102 ms
n/a
17 ms
n/a
100 ms
100 ms
Return after 1st AP Responses (scan 1 channel)
50ms
50ms
2 ms
n/a
2.4 GHz
5 GHz
50ms
50ms
2 ms
2 + ε ms
No Assumptions (scan all channels), stop after 1st APs is found
2.4 GHz
5 GHz
550 ms
1150 ms
22 ms
n/a
Amendment required
11k may work, but not for initial link set-up
Amendment required
Combine both: Amendment required
Amendment required
  Source: 11-10/922r2

## Slide 8: AP Discovery: Summary
Information on accessibility can be increasingly obtained from external sources in addition to the existing 802.11 schemes (e.g.: Offline WiFi Database for iPhone, location information in mobile devices, coverage maps, etc.)
Such information can reduce the time spent in AP discovery, but as of today …
802.11 does not provide all means to fully exploit this potential
Even without external information, scanning in 5GHz can be reduced from 2300ms down to 104ms (enablement via 2.4GHz; active scan of all channels at 2.4GHz, active scan of known channel w/ immediate return after 1st probe response on 5GHz channel)
Passive scanning
Active scanning
No Assumptions (scan all channels), find all APs
2.4 GHz
5 GHz
Reduce number of channels (to 1) where APs are known to operate
Enablement at 5GHz via 2.4 GHz
2.4 GHz
5 GHz
2.4 GHz
5 GHz
1100 ms
Expected Mean of time spent in scanning for
2300 ms
102 ms
n/a
17 ms
n/a
100 ms
100 ms
Return after 1st AP Responses (scan 1 channel)
50ms
50ms
2 ms
n/a
2.4 GHz
5 GHz
50ms
50ms
2 ms
2 + ε ms
No Assumptions (scan all channels), stop after 1st APs is found
2.4 GHz
5 GHz
550 ms
1150 ms
22 ms
n/a
Amendment required
11k may work, but not for initial link set-up
Amendment required
Combine both: Amendment required
Amendment required
Increase in (externally available) knowledge

## Slide 9: Fast Initial Link Set-Up
Phase | AP Discovery |  | Network Discovery | TSF Sync. (1 additional scan) | Auth. & Assoc. | Higher Layer (DHCP / IP)
 | Active | passive |  |  |  | 
Today | 102 ms (not @ 5GHz) | 1100 to 2300 ms |  |  |  | 
Possible achievement (w/ knowledge) | 2 ms (possible at 5GHz) | 50 ms |  |  |  | 
Rel. document | 10/0922r2 |  | 802.11u |  |  | 
Next Slides

## Slide 10: Network Discovery
Originally not further discussed during the SG phase.
Well covered by 11u
Ongoing presentations in TGai show potential for improving network discovery for a large number of STAs simultaneously attempting a network discovery
SSID1
SSID2
Network Selection (SSID2)
- ANQP is unicast
- Each SSID is queried until a suitable network is found.
SSID3
Beacon
SSID1
SSID2
Network Selection (SSID2)
Association Request
SSID3
- ANQP to be sent to the broadcast address
AP answers if it can satisfy the condition in the request
ANQP responses are sent unicast
Association Request
Beacon

## Slide 11: Fast Initial Link Set-Up
Phase | AP Discovery |  | Network Discovery | TSF Sync. (1 additional scan) | Auth. & Assoc. | Higher Layer (DHCP / IP)
 | Active | passive |  |  |  | 
Today | 102 ms (not @ 5GHz) | 1100 to 2300 ms |  |  |  | 
Possible achievement (w/ knowledge) | 2 ms (possible at 5GHz) | 50 ms | Optimizations for large number of users simultaneously entering a network |  |  | 
Rel. document | 10/0922r2 |  | 802.11u |  |  | 
Next Slides

## Slide 12: Main Idea: Parallelization of Tasks
Start (parts of) the message exchange required for IP address assignment during the Auth. & Assoc. Phase
AP Discovery | Network Discovery | TSF Sync. (1 additional scan) | Auth. & Assoc. | Higher Layer (DHCP / IP)
AP Discovery | Network Discovery | TSF Sync. (1 additional scan) | Auth. & Assoc.
 |  |  | Higher Layer (DHCP / IP)

## Slide 13: Fast Initial Authentication & Higher Layer Set-Up: Reduction of messages
Evaluation considers:
  Sync via Active Scanning
  Authentication as described
  DHCP messages to obtain IP and router information
  Processing time (1ms) and Transfer Time (3ms) for messages being sent to server (DHCP server or authentication server). Pls. see 11-10/988r0 for details.
Keep EAP-GPSK to assure consistent comparison of achievable improvements while upholding security level
Optimizes EAP-GPSK:
  As discussed during Beijing meeting: No security concerns risen during meeting
  Remove Auth-Req. / Auth-Res.
  AP immediately starts with EAP-GPSK-1 (remove EAPOL Start, EAP-Req.ID, EAP-Res.ID)
  Source: 11-10/0988r0
Method | Message Exchange | Connecting Duration |  |  | Airtime Consumption |  | 
 |  | DS1 | OFDM6 | OFDM54 | DS1 | OFDM6 | OFDM54
IEEE802.11i (EAP-GPSK) | 12 | 108,664μS | 76,989μS | 72,092μS | 49,232μS | 9,257μS | 3,962μS
Optimize EAP-GPSK | 9 | 94,752μS | 66,409μS | 61,921μS | 42,428μS | 7,860μS | 3,073μS
Next optimization: Picky Backing  parallel exchange of DHCP-messages with authentication message transfer

## Slide 14: Piggybacking of DHCP: one possible approach (*)
STA
AP
AS
DHCP/Default Gateway
DHCP Discovery
DHCP Offer
DHCP Request
DHCP ACK
ARP Request to Default Gateway
ARP Reply from Default Gateway
EAP-GPSK
EAPOL-Key
EAPOL-Start
EAPOL-Success
Association Request with:
AS Selector
DHCP Discovery
Association Response with:
DHCP ACK
Gratuitous ARP for Default Gateway
Parallel Processing for EAP and IP
AP waits for finishing both processes for EAP and IP.
Piggyback
Any packet can be used to transfer DHCP packets
Piggyback
Piggyback
Piggyback
  Source: 11-10/1008r2
  (*) refers to “Plan B”

## Slide 15: Performance Gains with Piggybacking
  Source: 11-10/0988r0 & 11-10/980r1
Use OFDM6 numbers for evaluation of overall performance gain
Reduced number of messages account mostly for performance gain (less overhead due to 802.11 header)
Further improvements might be possible: General security comments by Bob Moskowitz regarding FIA:
  Secure fast authentication can be achieved by 4 message exchanges
  Example to prove technical feasibility: HIP
Method | Message Exchange | Connecting Duration |  |  | Airtime Consumption |  | 
 |  | DS1 | OFDM6 | OFDM54 | DS1 | OFDM6 | OFDM54
IEEE802.11i (EAP-GPSK) | 12 | 108,664μS | 76,989μS | 72,092μS | 49,232μS | 9,257μS | 3,962μS
Optimize EAP-GPSK | 9 | 97,160μS | 69,323μS | 64,894μS | 41,836μS | 7,774μS | 3,046μS
Optimize EAP-GPSK w/piggyback B | 6 | 65,488μS | 39,937μS | 35,762μS | 36,272μS | 6,571μS | 2,197μS
Next part of the tutorial will highlight Security Requirements

## Slide 16: Fast Initial Link Set-Up
Total time for Link Set-Up for shown technical feasible solutions:
  Today per 802.11-2007: 179ms – 2377 ms
  With Fast Initial Link-Set Up: 38ms – 86ms
Considering all link set-up phases simultaneously results in largest performance improvement
 Modified Scope to include all phases of initial link set-up  Required security level of RSNA in Scope  Review by security experts before letter ballot
Phase | AP Discovery |  | Network Discovery | TSF Sync. (1 additional scan) | Auth. & Assoc. | Higher Layer (DHCP / IP)
 | Active | passive |  |  |  | 
Today | 102 ms (not @ 5GHz) | 1100 to 2300 ms | Optimizations for large number of users simultaneously entering a network | EAP-GPSK @ OFDM6: 6ms + 71ms processing time |  | 
Possible achievement (w/ knowledge) | 2 ms (possible at 5GHz) | 50 ms |  | EAP-GPSK w/ Piggyback@ OFDM6: 5ms + 35ms processing time (reduced number of messages require less processing time, further optimization might be possible) |  | 
Rel. document | 10/0922r2 |  | 802.11u | 10/988r0 & 10/1008r2 & 11-10/980r0 |  | 

## Slide 17: References
11-10/853r1: Some concerns about FIA (Emily Qi and Jesse Walker, Intel)
11-10/922r2: Achievable gains in AP discovery (Marc Emmelmann, Fraunhofer FOKUS)
11-10/965r1: Potential performance improvement with fast initial link set-up (Marc Emmelmann, Fraunhofer FOKUS & Root Inc.)
11-10/988r1: Protocol comparison (Hitoshi Morioka, Root Inc.)
11-10/1008r2: Parallel processing for upper layer (Hiroki Nakano, TNT Inc.)
11-10/980r0: FIA Security Analysis Bob Moskowitz
11-10/832r0: Comments to PAR & 5C (M. Emmelmann, Fraunhofer FOKUS & Root Inc.)
11-10/1106: Transition from FIA to FILS (M. Emmelmann, Fraunhofer FOKUS)
11-11/1015: Optimized network selection (Gabor Bajko, Nokia, Necati Canpolat, Intel)