## Slide 1: Simulation Study of the Performance of DCF Under Heavy Traffics for 802.11ah
Date: 2011-09-15
Authors:

## Slide 2: Abstract
In this report, we present simulation results that show the performance of DCF in “802.11ah Environmental and Agriculture Use Cases” [1] under heavy bursty traffics.

## Slide 3: Simulation Scenarios
Num of AP: 1
Num of Stations:100, 200, 300, 400
Topology:
  Disk with a 1000 meter radius
  AP at the center of the disk
  Stations uniformly within the disk

## Slide 4: Simulation Parameters 1
Channel Bandwidth | 20MHz
Symbol Duration | 4µs
Bursty Data Rate | 50kbps/station (uplink)
TX Power | 30dBm
Antenna Gains | 3dB
MCS | BPSK, 1 over 2
Max Communication Range | 1012 Meters (-88dBm)
Max Carrier Sensing Range | 1293 Meters (-92dBm)
Packet Size | 1250Bytes
DIFS | 34µs
SIFS | 16µs
Slot Time | 9µs
CWmin | 15
CWmax | 1023

## Slide 5: Simulation Parameters 2
Pathloss model
  Outdoor Macro [2]: PL(d) =8+37.6log10(d)
  Station to Station model [3]: PL(d)=16.90 + 42.4*log10(d)
Traffic Model
  For each station
    Bursty-Window = 16 Seconds
    #Packets = Busty-Window * Data Rate / Packet Size
    TX time for each packet is randomly selected in the Bursty-Window
Bursty-Window

## Slide 6: Simulation Result: Uplink Outage
For 200-400 stations, 15% of stations have almost 0 throughput and about 5% of
stations achieved a throughput of 40-47kbps

## Slide 7: Discussion
With DCF, heavy bursty traffics may cause
  Increased energy consumption
  Unfairness in terms of throughput
Compare performance to non-contention based MACs such as PCF
  Further study

## Slide 8: References
[1] Potential Compromise for 802.11ah Use Case Document, IEEE802.11-11/0457r0
[2] TGah channel model – proposed text, IEEE802.11-11/0968r1
[3] STA-STA Pathloss Model, IEEE802.11-11/1263r0