## Slide 1: Spatial stream support in TGah specification
Date: 2011-9-21
Authors:

## Slide 2: Abstract
The following presentation recommends the maximum number of spatial streams the TGah specification could support.

## Slide 3: TGah PAR and 5C [1]
5.2 Scope of Proposed Standard:
This amendment defines an Orthogonal Frequency Division Multiplexing (OFDM) Physical layer (PHY) operating in the license-exempt bands below 1 GHz, e.g., 868-868.6 MHz (Europe), 950 MHz -958 MHz (Japan), 314-316 MHz, 430-434 MHz, 470-510 MHz, and 779-787 MHz (China), 917 – 923.5 MHz (Korea) and 902-928 MHz (USA), and enhancements to the IEEE 802.11 Medium Access Control (MAC) to support this PHY, and provides mechanisms that enable coexistence with other systems in the bands including IEEE 802.15.4 and IEEE P802.15.4g.
The data rates defined in this amendment optimize the rate vs range performance of the specific channelization in a given band.
This amendment also adds support for:
transmission range up to 1 km
data rates > 100 kbit/s
while maintaining the 802.11 WLAN user experience for fixed, outdoor, point to multi point applications.

## Slide 4: Use Cases
Use Case 1 : Sensors and meters
Use Case 2 : Backhaul Sensor and meter data
Use Case 3 : Extended range Wi-Fi

## Slide 5: Antenna Dimension at sub 1GHz
Wavelength at 900 MHz is 12.48”
A ½ wavelength antenna would be 6.24”
A ¼ wavelength antenna would be 3.12”
The TGah PAR also specifies other frequencies of operation including 868-868.6 MHz (Europe), 950 MHz -958 MHz (Japan), 314-316 MHz, 430-434 MHz, 470-510 MHz, and 779-787 MHz (China), 917 – 923.5 MHz (Korea) and 902-928 MHz (USA)

## Slide 6: Discussion
The TGah PAR and 5C criterion does not have requirements for high data rates. It calls out requirements for long range 1km and > 100 kbps throughput.
Sensor’s don’t have high throughput requirements. They however have low power and small form factor requirements
Extended range WiFi has high throughput requirements which could be met with a maximum of 4 Spatial Streams.

## Slide 7: Discussion (Cont.)
Antennas have larger dimensions when operating in the Sub 1 GHz band.
It may not be feasible to have greater than 4 antennas in a device operating in sub 1 GHz band.

## Slide 8: Conclusion
Based on the PAR, Use Cases and the larger antenna dimensions in the sub 1 GHz band, it is recommended that the TGah specification support a maximum of 4 spatial streams.

## Slide 9: References
https://mentor.ieee.org/802.11/dcn/10/11-10-0001-13-0wng-900mhz-par-and-5c.doc
https://mentor.ieee.org/802.11/dcn/11/11-11-0457-00-00ah-potential-compromise-of-802-11ah-use-case-document.pptx