## Slide 1: Potential Channelization for 802.11ah
Date: 2011-9-18
Authors:

## Slide 2: Abstract
In this document we introduce an initial proposal for transmission channelization for 802.11ah
  Channelization refers to the process of breaking down the available spectrum in different regions into ‘channels’
    Mainly impacts sections analogous to Annex J of Std-802.11-2007
This document is a follow up to document: 11/1238r0 ‘Channelization and Bandwidth Modes for 802.11ah’
Notes: doc.: IEEE 802.11-yy/xxxxr0

## Slide 3: Context: Sub 1GHz Spectrum Availability in Key Geographies
902
928 MHz
917
923.5
929.7
779
787
863
868.6
8 MHz
5.6 MHz
26 MHz
6.5 MHz
China
(max erp <= 10 mW)
EU
US (max erp <=1 W)
Korea
Japan
(Max BW = 1MHz)
Region | Tx power regulations
US | Max e.r.p. <= 1 W
EU | max erp <=14 dBm PSD <= -4.5 dBm/100KHz (863~868.6MHz) PSD <= 6.2 dBm/100KHz (865~868MHz)
Korea | 3 mW or 10 mW (920.6~923.5MHz and six 200 KHz channels below 920.6 MHz)
China | Max e.r.p. <= 10 mW
Japan | 1mW , 20 mW or 250 mW (915.9~929.7MHz) Max BW <= 1 MHz
915.9
928 MHz
13.8 MHz

## Slide 4: US Channelization (902 – 928MHz)
902 MHz
928 MHz
1 MHz
2 MHz
4 MHz
8 MHz
16 MHz
Note: Devices operating in the 1 MHz PHY mode are expected to operate in the lower 1 MHz of each 2 MHz wide channel .

## Slide 5: South Korea 917- 923.5 Channelization (6.5 MHz)*
917 MHz
923 MHz
1 MHz
2 MHz
* Assumes 500 KHz , 923 – 923.5 as guard band
4 MHz

## Slide 6: Japan 915.9- 929.7 Channelization (13.8 MHz)*
916 MHz
929 MHz
1 MHz
2 MHz
* Assumes 100 KHz , 915.9 – 916 MHz and – 929 – 929.7 as guard bands
4 MHz
Note: Current understanding of the Japan regulations is that there is a 1 MHz max bandwidth limitation

## Slide 7: China 779- 787 Channelization (8 MHz)
779 MHz
787 MHz
1 MHz
2 MHz
4 MHz
8 MHz

## Slide 8: Europe 863- 868.6 Channelization (5.6 MHz)*
863 MHz
868 MHz
1 MHz
2 MHz
* Assumes 600 KHz , 868 - 868.6 as guard band

## Slide 9
Back Up

## Slide 10: Prospective Spec Framework Text Regarding Bandwidth Modes:
The draft specification shall include support for 1 MHz, 2 MHz, 4 MHz, 8 MHz, and 16 MHz PHY transmissions.
An 802.11ah STA shall support reception of 1 MHz and 2 MHz PHY transmissions.