## Slide 1: Considerations for Cellular-Offloading Use Case
Date: 2011-09-xx
Authors:

## Slide 2: Abstract
This presentation provides some consideration for the use case of Cellular offloading

## Slide 3: Use Case 3b: 802.11ah Outdoor Wi-Fi for cellular traffic offloading Use Case [1]
Traffic offloading by 802.11 WLAN is considered as good solution of mobile traffic explosion
However, current 802.11(a, g, n, ac) WLAN have short coverage and assume indoor environment
TGah has large coverage (~1km), so it can be used for mobile traffic offloading in outdoor environment

## Slide 4: 802.11 Uplink/Downlink Performance
Reference: Novarum Inc. Report, 2010 “Guidelines for Successful Large Scale Outdoor Wi-Fi Networks”
“smartphones have much more limited coverage and performance due to their lower transmitter power and minimal antennas”
Tested 175 wireless networks in 36 North American Cities
Clients:
  11g laptop client 30mW o/p power, high power 11g laptop – 200mW o/p power, 2x2 MIMO 11n client – 30mW o/p power, iPhone WIFI – 11g
Difference could be due to uplink signalling
Mismatch in UL/DL throughput

## Slide 5: Observation
Based on previous slide, TGah should consider carefully design of uplink transmission for more power challenged device like mobile phones
  Uplink MAC layer DATA transmission (during uplink traffic)
  Uplink signalling, e.g. CTS/ACK (during downlink traffic)
Unlike cellular networks, each 802.11 downlink MAC data transmission requires uplink signalling (e.g. CTS/ACK)
Even if we provide a long range downlink, uplink range will be shorter in power challenged devices
  especially when there’s a mismatch in output power between BS and STA

## Slide 6: Link budget example (handphones)
Difference in UL and DL power budget

## Slide 7: Current Use Case
3G base station
STA
3G UL/DL
TGah UL/DL
STA
802.11 AP

## Slide 8: Observations
3G coverage is good & longer than 11ah and can be used as a candidate uplink transmission
We should not exclude the case where more than 1 connection are up (e.g Cellular and 802.11ah operating simultaneously)

## Slide 9: Traffic Asymmetry
Reference: Plum Consulting, June 2011 “Economic study of the benefits from use of 1452-1492 MHz for a supplemental mobile downlink for enhanced multimedia and broadband services”

## Slide 10: Other sub-Use Case
STA
3G UL/DL
STA
TGah DL
3G UL
3G base station
802.11ah AP
3G base station
88%
12%

## Slide 11: Observation
No modification to cellular networks signalling required
Traffic routing done at IP layer
Only enhancement of UL signaling for TGah DL traffic required

## Slide 12: Other sub-Use Case
STA
3G UL/DL
STA
TGah (UL Traffic
& TGg/n DL signalling)
11g/n DL
3G base station
802.11g/n AP
802.11ah AP
Co-located APs

## Slide 13: Observation
UL/DL Traffic routing done at IP layer
TGah bands maybe be BW limited and we can benefit from still using the 2.4GHz band for offloading
Use of TGah for TGg/n signaling design required

## Slide 14: Conclusion
Current use case of the Cellular offloading should consider concurrent operation of multiple bearers and clever use of TGah for enhanced performance

## Slide 15: References
[1] Rolf de Vegt, “Potential Compromise for 802.11ah Use Case Document,” 11-11/457r0.
[2] Novarum Inc. Report, 2010 “Guidelines for Successful Large Scale Outdoor Wi-Fi Networks”
[3] Plum Consulting, June 2011 “Economic study of the benefits from use of 1452-1492 MHz for a supplemental mobile downlink for enhanced multimedia and broadband services”