## Slide 1: Performance Evaluation of 802.11ah Network with Multi-floor Indoor Propagation Models
Date: 2011-09-22
Authors:

## Slide 2: Abstract
Study the Performance of IEEE 802.11ah Network due to Floor Attenuation in Indoor Scenarios

## Slide 3: Simulation Scenario
10m
5mm
10m
5mm
4 floors with corresponding FAFs
1 AP and 1 connected STA per room
Compare cumulative uplink throughput when APs and STAs are on same floor and on different floors

## Slide 4: Simulation Parameters
Channel Bandwidth | 20MHz
Data Rate | 100kbps
TX Power | 30dBm
Antenna Gains | 3dB
Max Communication Range | -82dBm
FAF (dB) | 0, 12.9, 18.7, 24.4, 27.7
Packet Size | 1500 Bytes
DIFS | 34µs
SIFS | 16µs
Slot Time | 9µs
CWmin | 15
CWmax | 1023

## Slide 5: Preliminary Results for Uplink Data Transmissions
Aggregate Throughput Ratio
Break point distance = 5 m
1 Floor
3 Floors
Chart: 
 | 0.8221 | 0.99

## Slide 6: Conclusion
Floor attenuation has a significant impact on aggregate throughput of 802.11ah network
  Multi-floor attenuation must be considered for indoor 802.11ah networks

## Slide 7: Reference
[1] Ron Porat et. al., “TGah channel model – proposed text,” 11-11/0968r1.