## Slide 1: Motions and Strawpoll on Channelization for 11ah
Date: 2011-9-21
Authors:

## Slide 2: Abstract
This document we includes the text for Motions and Strawpolls regarding transmission channelization for 802.11ah
  Channelization refers to the process of breaking down the available spectrum in different regions into ‘channels’
    Mainly impacts sections analogous to Annex J of Std-802.11-2007
This document is a follow up to documents:
  11/1238r0 ‘Channelization and Bandwidth Modes for 802.11ah’
  11/1269r3 ‘Potential Channelization for 802.11ah’
This document references:
  11/1318r0 ‘Japanese Channelization for 11ah’
  11/1320r0 ’11ah Channelization of China’
Notes: doc.: IEEE 802.11-yy/xxxxr0

## Slide 3: Motion 1: Channelization for South Korea
Motion: Adopt into the Spec Framework the following text and graphic regarding channelization for South Korea:
Yes, No, Abstain
917 MHz
923 MHz
1 MHz
2 MHz
Assumes 500 KHz , 923 – 923.5 as guard band
4 MHz

## Slide 4: Motion 2: Channelization for Europe
Motion: Adopt into the Spec Framework the following text and graphic regarding channelization for Europe:
Yes, No, Abstain
863 MHz
868 MHz
1 MHz
2 MHz
* Assumes 600 KHz , 868 - 868.6 as guard band

## Slide 5: Motion 3: Channelization for Japan
Adopt into the Spec Framework the channelization proposal contained in slide 3 of document 11/1318r0 for Japan

## Slide 6: Motion 4: Channelization for China
Adopt into the Spec Framework the channelization proposal contained in slide 4 of document 11/1320r0 for China

## Slide 7: Strawpoll 1: Channelization for US
Strawpoll: Do you agree with the following channelization for the US:
Yes, No, Abstain

## Slide 8
Back Up

## Slide 9: Context: Sub 1GHz Spectrum Availability in Key Geographies
902
928 MHz
917
923.5
929.7
779
787
863
868.6
8 MHz
5.6 MHz
26 MHz
6.5 MHz
China
(max erp <= 10 mW)
EU
US (max erp <=1 W)
Korea
Japan
(Max BW = 1MHz)
Region | Tx power regulations
US | Max e.r.p. <= 1 W
EU | max erp <=14 dBm PSD <= -4.5 dBm/100KHz (863~868.6MHz) PSD <= 6.2 dBm/100KHz (865~868MHz)
Korea | 3 mW or 10 mW (920.6~923.5MHz and six 200 KHz channels below 920.6 MHz)
China | Max e.r.p. <= 10 mW
Japan | 1mW , 20 mW or 250 mW (915.9~929.7MHz) Max BW <= 1 MHz
915.9
928 MHz
13.8 MHz