IEEE P802.11
Wireless LANs

| Frame Size Corrections |
| --- |
| Date: 2011-09-22 |
| Author(s): |
| Name | Affiliation | Address | Phone | email |
| Mark Rison | CSR plc | Cowley Road Cambridge, CB4 0WZ, UK | +44 1223 692000 | mark dod rison et csr dod com |
| Kazuyuki Sakoda | Sony Corporation | 5-1-12 Kita-Shinagawa, Shinagawa-ku, Tokyo, 141-0001 Japan | +81-3-5448-4018 | KazuyukiA.Sakoda(at)jp.sony.com |
| Michael Bahr | Siemens AG, Corporate Technology | Otto-Hahn-Ring 6 80200 München, Germany |  | bahr et siemens dod com |

All changes are based on IEEE 802.11 REVmb D10.0.

This submission resolves comments CID

Editor instruction: In clause 8.2.3 General frame format, delete the note on page 430 lines 1-4 as indicated by the Winword track changes in the text below:

Note, the information contained in this note is repeated in similar notes in the clauses on the specific frame types.

Editor instruction: In clause 8.3.2.1 Data frame format, change the note on page 464 lines 13-16 as indicated by the Winword track changes in the text below:

NOTE—The maximum frame body size shown in Figure 8-30 (Data frame) is for CCMP encryption of a maximum-size A-MSDU (note that TKIP encryption is not allowed in this case and any Mesh Control fields are part of the A-MSDU subframes). The maximum frame body size if A-MSDUs are not used is 2338 octets for CCMP encryption of a maximum-size MSDU and 2342 octets for TKIP encryption of a maximum-size MSDU, including in both cases an 18-octet Mesh Control field. The frame body size might in all cases be greater if a vendor-specific cipher suite is used.

Editor instruction: In clause 8.3.3.1 Format of management frames, change the note on page 468 lines 24-27 as indicated by the Winword track changes in the text below:

NOTE 1—The maximum frame body size shown in Figure 8-34 (Management frame format) is for CCMP encryption with a maximum-size MMPDU (note TKIP encryption is not allowed and any Mesh Control field is held within the MMPDU, not as a separate header). The frame body size might be greater if a vendor-specific cipher suite is used.

Editor instruction: In clause W.1 Clarification of Mesh Data frame format, change the text of the clause and the heading of Figure W-1 as indicated by the Winword track changes in the text below. Replace Figure W-1 with the one provided below.

W.1 Clarification of Mesh Data frame format

The Mesh Data frame consists of MAC Header, Frame Body, and the FCS. The fields in the MAC Header

are described in 8.2.3 (General frame format).

In a Mesh Data frame containing a single MSDU, the Mesh Control field is placed as the first element in the encrypted Frame Body. The Frame Body contains also the LLC/SNAP headers and the higher layer data. This is shown in the example frame format for an encrypted Mesh Data frame in Figure W-1 (Format of a CCMP-encrypted Mesh Data frame containing a single MSDU).

When the Mesh Data frame is fragmented, only the first fragment contains the Mesh Control field.

| Octets: 2 | 2 | 6 | 6 | 6 | 2 | 6 | 2 | 4 | 8 | 18 | up to 2304 | 8 | 4 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Frame Control | Duration/ ID | Address 1 | Address 2 | Address 3 | Sequence Control | Address 4 | QoS Control | HT Control | Frame Body | FCS |
|  |  |  |  |  |  |  |  |  | CCMP Header | Mesh Control | LLC/SNAP headers | Layer 3 datagram | MIC |  |
| MAC Header, Not encrypted | Frame Body |  |
|  | Encrypted using CCMP |  |

Figure W-1—Format of a CCMP-encrypted Mesh Data frame containing a single MSDU

Note to editor: All changes to Figure W-1 are in the area of the Frame Body.

References:

IEEE 802.11 REVmb D10.0, August 2011

# Comments

First or second element?

What about this? “In a Mesh Data frame containing a single MSDU, the Mesh Control field is placed as the first element in the Frame Body or as the first element in the encrypted portion of the Frame body.

How about “placed immediately before the MSDU, in the encrypted Frame Body”?

Ah, that’s much better. I am for Mark’s proposal “placed immediately before the MSDU, in the encrypted Frame Body”?

Why did you change the wording here? I prefer the previous wording.

I thought we had agreed on “The format of a CCMP-encrypted Mesh Data frame containing a single MSDU is shown in …”?

Combine those to: up to 2338?

I would prefer having them in this form.

I’m OK with either.  The Frame Body arrow needs to clearly include the MIC, however

# Text boxes

Abstract

The submission provides text changes to IEEE 802.11 REVmb D10.0 in order to correct the frame sizes. Problems with the Frame Size where indicated in comments of the Sponsor Ballot on IEEE 802.11 REVmb D10.0. This submission intends to resolve these comments.