IEEE P802.11
Wireless LANs

| An RSN in an MBSS |
| --- |
| Date: 2011-09-22 |
| Author(s): |
| Name | Affiliation | Address | Phone | email |
| Dan Harkins | Aruba Networks | 1322 Crossman ave, Sunnyvale, CA | +1 408 227 4500 | dharkins at arubanetworks dot com |

Instruct the editor to create a new section entitled “11.5.1.3.4 Security association in an MBSS”, to move the content of 11.3.3 Mesh authentication into this new section, and to create text in the now empty 11.3.3 referring interested readers back to 11.5.1.3.4.

Instruct the editor to create a new 11.5.7 and increment the existing 11.5.7 and all subsequent subsections under 11.5.

11.5.7 RSNA policy selection in an MBSS

RSNA policy is advertised in Beacon frames and Probe Response frames. A mesh STA identifies a candidate peer by parsing its neigbor STA’s Beacon frames and Probe Response frames (see section 13.2).

All mesh STAs in an MBSS use the same group cipher suite. Mesh STAs establish authenticated peerings with each other using the AMPE protocol (see section 13.5). In AMPE, mesh STAs negotiate a pairwise cipher suite, and establish a pairwise MTKSA, to protect individually addressed frames and state a group cipher suite and establish an MGTKSA to process incoming group addressed frames from a peer.

The AMPE performs key confirmation of a secret, authenticated, and shared PMK derived by an authenticated key management protocol (see section 11.3) and derives pairwise symmetric keys.

Instruct the editor to create a new 11.5.11 (which will go after the existing 11.5.9 that was incremeneted above to become 11.5.10) and increment all subsequent sections under 11.5

11.5.11 RSNA authentication in an MBSS

When establishing an RSNA in an MBSS, a mesh STA shall use IEEE 802.11 SAE authentication (see section 11.3), or optionally IEEE 802.1X authentication, prior to establishment of an authenticated peering. An RSNA security association, called a Mesh PMKSA, is created upon successful completion of authentication.

Authentication using IEEE 802.11 SAE authentication is based on a password. A password is required to be shared between two mesh STAs in order to successfully complete authentication. This password can be pairwise—each pair of mesh STAs in an MBSS has a unique password—or it can be shared—all mesh STAs in the MBSS share the same password.

Due to the security properties of IEEE 802.11 SAE authentication, an adversary has no greater possibility in determining a shared password than in determining a pairwise password. The potential for misuse, though, is greater if a shared password becomes known to an adversary because an unlimited number of mesh STAs under the control of the adversary can be added to the MBSS.

Instruct the editor to create a new 11.5.14 (which will go after the existing 11.5.11 that was incremented twice above to become 11.5.13) and increment all subsequent sections under 11.5

11.5.14 RSNA key management in an MBSS

Upon successful completion of the AMPE, a secure mesh peering is established between two mesh STAs. This secure mesh peering includes a mesh PMKSA and a mesh TKSA. Multiple mesh TKSAs may be created using a single mesh PMKSA (a limit to that number is a policy decision outside the scope of this standard).

A mesh TKSA is logically a child of the mesh PMKSA. A mesh TKSA shall be destroyed if the corresponding mesh PMKSA, which was used by the AMPE to create it, is destroyed. Mesh PMKSAs are limited by their lifetime (section 11.6.1.3).

References:

# Text boxes

Abstract

This document addresses CIDs 14064, 14065, 14066, 14067 from the Sponsor Ballot against Draft P802.11REVmb_D10.0