IEEE P802.11
Wireless LANs

| LB171 Some comment resolutions for enabling |
| --- |
| Date: 2011-10-24 |
| Author(s): |
| Name | Affiliation | Address | Phone | email |
| Peter Ecclesine | Cisco Systems | 170 W. Tasman Dr.,MS SJ-14-4, San Jose, CA 95134-1706 | +1-408-527-0815 | pecclesi@cisco.com |

Interpretation of a Motion to Adopt

A motion to approve this submission means that the editing instructions and any changed or added material are actioned in the TGaf Draft.  This introduction is not part of the adopted material.

Editing instructions formatted like this are intended to be copied into the TGaf Draft (i.e. they are instructions to the 802.11 editor on how to merge the text with the baseline documents).

TGaf Editor: Editing instructions preceded by “TGaf Editor” are instructions to the TGaf editor to modify existing material in the TGaf draft.  As a result of adopting the changes, the TGaf editor will execute the instructions rather than copy them to the TGaf Draft.

Enabling comments

LB171 CIDs 42, 340, 684, 712 and 827:

| 42 | 8.4.2.af5 36.22 | Why burn an IE just to signal a capability, when there is a perfectly good extended capability element? | Remove the "Geodatabase Inband Enabling Signal element" and create a "Geodatabase Inband Enabling Signal" field in the extended capabilities IE |
| --- | --- | --- | --- |
| 340 | 8.4.2.af5 36.21 | Wouldn't it be more efficient to define a bit in the Extended Capabilities element to indicate enablement is possible? | As per comment. |
| 684 | 8.4.2.af5 36.22 | Geodatabase Inband Enabling signal element is defined as an IE with zero length and this IE is not marked extensible in Table 8-51. This looks like an inefficient way of conveying 1-bit information. Wouldn't a single bit reserved from Extended Capabilities provide the same functionality without having to allocate a new element id and add two octets to the Beacon frames? | Delete 8.4.2.af5 and replace all references to it with a reference to a new Extended Capabilities subfield. Add the new subfield into the Extended Capabilities element in 8.4.2.29 for this purpose. |
| 712 | 8.4.2.af5 36.24 | The use of an empty 2 octet information Element to signal this capability seems rather inefficient. | Why not define a new bit in the extended capabilities field to signal the same information? |
| 827 | 8.4.2.af5 36.24 | Using up an element ID, and sending 8 bytes in every beacon and probe response, is very inefficient for something that should only require 1 bit. | Delete Geodatabase Inband Enabling Signal element, and use a bit in the extended capabilities instead. |

Discussion:

LB 171 CIDs 42, 340, 684, 712 and 827 say that since Extended Capabilities field is in every beacon, a single bit there can convey the information. CID 42 proposes to name the bit Geodatabase Inband Enabling Signal.

Propose Accepted for CIDs 42, 340, 684, 712 and 827, per discussion and editing instructions in 11-11/1386r2.

LB171 CID 646:

| 646 | 8.4.2.af5 36.22 | Unnecessary field - combine with single element for WS | Remove and combine with other fields |
| --- | --- | --- | --- |

Discussion:

LB 171 CID 646 says the Geodatabase Inband Enabling Signal element is unnecessary, and to combine with other fields for WS. We note the field is necessary, but it does not to be an element.

Propose Revised for CID 646 because the field is necessary for GDC operation, but it can be a bit in Extended Capabilities, per discussion and editing instructions in 11-11/1386r2.

LB171 CIDs 545, 614 and 905:

| 545 | 10.12 56.35 | Is an enabling STA always an AP STA? If it is not, what is a non-AP enabling STA? Is there may exist that an enabling STA only providing enablement, WSM and CVS transmission? Then, it should be signaled that the enabling STA can only provide these functionalities. | Provide a clear behavior of an enabling STA and define signalings of an enabling STA that only provides enablement, WSM and CVS transmission in order that STAs know that what the enabling STA can provide. Include these signaling in extended capability element. See forthcoming document 11-11/xxxxr0. |
| --- | --- | --- | --- |
| 614 | 10.12 56.35 | Is an enabling STA always an AP STA? If it is not, what is a non-AP enabling STA? Is there may exist that an enabling STA only providing enablement, WSM and CVS transmission? Then, it should be signaled that the enabling STA can only provide these functionalities. | Provide a clear behavior of an enabling STA and define signalings of an enabling STA that only provides enablement, WSM and CVS transmission in order that STAs know that what the enabling STA can provide. Include these signaling in extended capability element. See forthcoming document 11-11/xxxxr0. |
| 905 | 10.12 56.35 | Is an enabling STA always an AP STA? If it is not, what is a non-AP enabling STA? Is there may exist that an enabling STA only providing enablement, WSM and CVS transmission? Then, it should be signaled that the enabling STA can only provide these functionalities. | Provide a clear behavior of an enabling STA and define signalings of an enabling STA that only provides enablement, WSM and CVS transmission in order that STAs know that what the enabling STA can provide. Include these signaling in extended capability element. See forthcoming document 11-11/xxxxr0. |

Discussion:

LB 171 duplicate CIDs 545, 614 and 905 say that if the enabling STA is an AP, then it should provide enablement, WSM and CVS transmission and to include signalings of these capabilities in the Extended Capabilities element. We propose that in an infrastructure BSS an enabling STA is always an AP. The WSM is available from every AP, so WSM available is not necessary to be signaled in the Extended Capabilities element. The CVS must be securely communicated to client devices, and that is not possible in the Extended Capabilities element.

Propose Revised for CIDs 545, 614 and 905, per the discussion and editing instructions in 11-11/1386r2. We propose that in an infrastructure BSS, an enabling STA is always an AP.

LB171 CID 981:

| 981 | 8.4.2.af5 36.21 | The enabling signal defined in clause 8.4.2.af5 only allows the advertisement for the enablement on the channel, which is the target of the enablement. However, allowing that advertisement to be possible on a different band should be possible. For example, an enabling STA, which provides the enablement on the TVWS band, should be able to advertise its capability over 2.4 GHz band channel (assuming the enabling STA supports dual band operation). Also, the enabling signal should be able to identify which channel that the enabling STA is operating in the band that the STA is providing the enablement. | Add octets to identify the band to which the STA is providing the enablement and to identify the channel that the STA is operating in that particular band. |
| --- | --- | --- | --- |

Discussion:

LB 171 CID 981 requests a definition of multiband enablement with an enabling signal advertisement on a different band. FCC rules for TVBD operation define radios operating in TV bands. There is no multiband operation operation defined in FCC rules. The FCC rules require secure communication between client devices and master devices regarding available channels, so that the geodatabase can deny channels to any devices based on their FCC IDs. Defining the enabling signal as a TV band on-channel signal is the least insecure method known, as it can proven to work at time of device certification.

Propose Rejected for CID 981, per discussion and editing instructions in 11-11/1386r2. The FCC rules require secure communication between client devices and master devices regarding available channels, so that the geodatabase can deny channels to any devices based on their FCC IDs. Defining the enabling signal as a TV band on-channel signal is the least insecure method known, as it can be proven to work at time of device certification.

LB171 CID 1182:

| 1182 | 8.4.2.af6 36.42 | The client devices listen enabling signal in the TV band and can contact the enabling STA and obtain the list of available channels in other frequency band. | Add additional field to indicate through which frequency band the client devices are allowed to contact the enabling STA and obtain the list of available channels. |
| --- | --- | --- | --- |

Discussion:

LB 171 CID 1182 requests a definition of multiband enablement/operation with an enabling signal advertisement of available channels from another band. FCC rules for TVBD operation define radios operating in TV bands. There is no multiband operation operation defined in FCC rules. The FCC rules require secure communication between client devices and master devices regarding available channels, so that the geodatabase can deny channels to any devices based on their FCC IDs. Defining the communication of available channels as a TV band on-channel protocol is the least insecure method known, as it can be proven to work at time of device certification.

Propose Rejected for CID 1182, per discussion and editing instructions in 11-11/1386r2. The FCC rules require secure communication between client devices and master devices regarding available channels, so that the geodatabase can deny channels to any devices based on their FCC IDs. Defining the communication of available channels as a TV band on-channel protocol is the least insecure method known, as it can be proven to work at time of device certification.

Proposed Resolution:

Accept changes to P802.11af draft based on discussion and editing instructions in 11-11/1386r2:

TGaf Editor: Change text in section 6.3.3.3.2 as follows:

### 6.3.3 Scan

### 6.3.3.3 MLME-SCAN.confirm

### 6.3.3.3.2 Semantics of the service primitive

Editor: Insert threefour new entries at the end of BSSDescription table as follows:

| Name | Type | Valid range | Description | IBSS adoption |
| --- | --- | --- | --- | --- |
| White Space Map | White Space Map element | As defined in 8.4.2.160 (White Space Map element) | The values from the White Space Map element if such an element was present in the probe response or Beacon frame, else null. | Adopt |
| DSE Link Identifier | DSE Link Identifier element | As defined in 8.4.2.161 (DSE Link Identifier element) | The values from the DSE Link Identifier element if such an element was present in the probe response or Beacon frame, else null. | Adopt |
| Channel Power Management Announcement | Channel Power Management Announcement element | As defined in 8.4.2.162 (Channel Power Management Announcement element) | The values from the Channel Power Management Announcement element if such an element was present in the probe response or Beacon frame, else null. | Adopt |
| Geodatabase Inband Enabling Signal | Geodatabase Inband Enabling Signal element | As defined in 8.4.2.164 (Geodatabase Inband Enabling Signal element) | The values from the Geodatabase Inband Enabling Signal element if such an element was present in the Probe Response or Beacon frame, else null. | Adopt |

### 8.3.3.2 Beacon frame format

TGaf Editor: Change editing instruction in section 8.3.3.2 Beacon frame format as follows:

Insert the following threefour rows (ignoring the header row) before the last order in Table 8-20:

TGaf Editor: Change the last row of Table 8-20 Beacon frame body in section 8.3.3.2 as follows:

| <ANA> | Geodatabase Inband Enabling Signal | The Geodatabase inband enabling signal is optionally present if dot11GDCActivated is true. |
| --- | --- | --- |

### 8.3.3.10 Probe Response frame format

TGaf Editor: Change editing instructions in 8.3.3.10 Probe Response frame format as follows:

Insert the following three four rows (ignoring the header row) before the last two rows in Table 8-27 Probe Response frame body in the correct position to preserve ordering by the "Order" column:

TGaf Editor: Change the last row of Table 8-26 Probe Response frame body in section 8.3.3.10 as follows:

| <ANA> | Geodatabase Inband Enabling Signal | The Geodatabase inband enabling signal is optionally present if dot11GDCActivated is true. |
| --- | --- | --- |

### 8.4.2 Information elements

### 8.4.2.1 General

TGaf Editor: Change editing instructions in 8.4.2.1 General as follows:

Insert the following fivesix rows (ignoring the header row) in Table 8-54 Element IDs in the correct position to preserve ordering by the "Element ID" column.

TGaf Editor: change the next to last row in Table 8-54 Element IDs for the Geodatabase Inband Enabling Signal row as follows:

| Element | Element ID | Length of indicated element (in octets) | Extensible |
| --- | --- | --- | --- |
| Geodatabase Inband Enabling Signal (see 8.4.2.164 (Geodatabase Inband Enabling Signal element)) | <ANA> | 2 | Yes |

### 8.4.2.29 Extended Capabilities element

TGaf Editor: Change editing instructions in 8.4.2.29 Extended Capabilities element as follows:

Insert the following six three rows (ignoring the header row) into Table 8-103 in the correct position to preserve ordering by the "Bit" column and renumber the reserved values accordingly:

TGaf Editor: Insert new last row in Table 8-103 Capabilities field as follows:

| <ANA> | Geodatabase Inband Enabling Signal | The STA sets the Geodatabase inband enabling signal to 1 when dot11GDCActivated is true and the STA permits GDC dependent STAs to operate, see 10.38.2 (GDC enabling STA operation). |
| --- | --- | --- |

### 8.4.2.164 Geodatabase Inband Enabling Signal element

TGaf Editor: Delete heading and all text in 8.4.2.164 Geodatabase Inband Enabling Signal element

### 10.38.2 GDC enabling STA operation

TGaf Editor: Change the second sentence as follows:

The GDC enabling signal is a beacon frame containing a Geodatabase Inband Enabling Signal field in the Extended Capabilities element set to 1.

# Text boxes

Abstract

Proposed resolutions to some LB 171 CIDs in Comment Group MAC enabling (CIDs 42, 340, 545, 614, 646, 684, 712, 827, 905, 981 and 1182).

Editing instructions are based on P802.11af speculative Draft 1.04.

The resolutions are coordinated with resolutions for DSE comments in 11-11/1150, 11-11/1151 and 11-11/1153, as discussed in November 1, 2011 teleconference.