IEEE P802.11
Wireless LANs

| MAC Comment Resolution – CID 2157, 2158, 3047 |
| --- |
| Date: Oct 21, 2011 |
| Author(s): |
| Name | Affiliation | Address | Phone | email |
| Liwen | STMicroelectronics |  |  | Liwen.chu@st.com |

| CommentID | Subclause | Page | Line | CommentType | Comment | SuggestedRemedy |
| --- | --- | --- | --- | --- | --- | --- |
| 3047 | 8.5.8.16 | 60 | 60 | T | Adding a non-IE field (Association ID) in the middle of IE fields makes it more complex to parse the frame. While it is possible to parse the frame here because the immediately preceding IE is a mandatory one, it would be good to avoid this type of construction to keep implementation simpler. | Consider definition a new element in the IE format (element ID + length fields) for Source/Destination Association ID and use it instead of the Association ID field (7.3.1.8) in the frames. This applies to all the frames to which the Destination/Source Association ID was added. |

Discussion: This comment is already resolved by 11-11/931r1 by adding an AID IE.

Proposed Resolution:

Principle - See 11-11-0931r1

| CommentID | Subclause | Page | Line | CommentType | Comment | SuggestedRemedy |
| --- | --- | --- | --- | --- | --- | --- |
| 2157 | 8.2.5.2 | 25 | 12 | TR | This Duration setting rule may create more collision. | Fix the problem. |
| 2158 | 8.2.5.2 | 25 | 15 | TR | This Duration setting rule may create more collision. | Fix the problem. |

Discussion:

In 8.2.5.2, for an NDPA frame, the Duration/ID field is set to the estimated time required to transmit the

subsequent NDP and VHT Compressed Beamforming frame response plus two SIFS intervals (Bullet 7). And for a Beamforming Report Poll frame, the Duration/ID field is set to the estimated time required to transmit the VHT Compressed Beamforming frame response plus one SIFS interval (Bullet 8). The TXOP holder may send data frames after beamforming during the same TXOP as VHT beamforming. The Duration in NDPA needs to cover the following data frame and related acknowledge. When the TXOP holder starts the TXOP with Beamforming Report Poll, it may also send data frames during the same TXOP as beamforming poll. The Duration in Beamforming Report Poll needs to cover the following data frame and related acknowledge.

When TXOP limit value is 0, MSDU/MMPDU may be fragmented, and multiple PPDUs (for multiple fragments) may be transmitted. Frame exchange sequence in 9. 19.2.2 should be changed accordingly.

Two editorial changes are proposed about frame transmission sequence when TXOP limit is 0.

The changes are based on 802.11ac D1.2 and 802.11REVmb12.0.

Proposed Resolution: Principle, See 11-11/1387r4.

Proposed Resolution Text:

8.2.5.2 Setting for single and multiple protection under enhanced distributed channel access (EDCA)

a) Single protection settings.

Change Bullet 7) and 8)  as following:

7) For an NDPA frame, the Duration/ID field is set to the estimated time ,  required to transmit the subsequent NDP and VHT Compressed Beamforming frame response plus two SIFS intervals, plus the pending frame and its acknowledgement if required (including appropriate IFS values) when any pending frames are to be transmitted within the same TXOP as the NDPA frame.

8) For a Beamforming Report Poll frame, the Duration/ID field is set to the estimated time

required to transmit the VHT Compressed Beamforming frame response plus one SIFS interval, plus the pending frame and its acknowledgement if required (including appropriate IFS values) when any pending frames are to be transmitted within the same TXOP as the Beamforming Report Poll frame

Change b) as following:

b) Multiple protection settings. The Duration/ID field is set to a value D as follows:

1) If TTXOP = 0 and TEND_NAV = 0, then D = TSINGLE-MSDU – TPPDU

2) Else if TTXOP = 0 and TEND_NAV > 0, then D = TEND-NAV –TPPDU

3) Else if TEND-NAV = 0, then

4) Else TEND – NAV – TPPDU ≤D ≤TTXOP – REMAINING – TPPDU

where

TSINGLE-MSDU is the estimated time required for the transmission of the allowed frame

exchange sequence defined in 9.19.2.2 (EDCA TXOPs)

(for a TXOP limit value of 0), including applicable IFS durations

TPENDING is the estimated time required for the transmission of

— Pending MPDUs of the same AC

— Any associated immediate response frames

— Any NDP transmissions and explicit feedback response frames

— Applicable IFS durations

— Any RDG

TTXOP is the value of dot11EDCATableTXOPLimit (dot11EDCAQAPTableTXOPLimit

for the AP) for that AC

TTXOP-REMAINING is TTXOP less the time already used time within the TXOP

TEND-NAV is the remaining duration of any NAV set by the TXOP holder, or 0 if no

NAV has been established

TPPDU is the time required for transmission of the current PPDU

9.19.2.2 EDCA TXOPs

Change the 3rd paragraph of 9.19.2.2  as following:

A TXOP limit value of 0 indicates that the TXOP holder may transmit or cause to be transmitted (as responses)

the following within the current TXOP:

a) One of the following at any rate, subject to the rules in 9.7:

1) SU PPDUs carrying fragments of a single MSDU or MMPDU,

2) An SU PPDU carrying aA single MSDU, MMPDU, A-MSDU, or A-MPDU

, or

3) An MU PPDU carrying A-MPDUs to different users

)(#2107)

b) Any required acknowledgments

c) Any frames required for protection, including one of the following:

1) An RTS/CTS exchange

2) CTS to itself

3) Dual CTS as specified in 9.3.2.8 (Dual CTS protection)

d) Any frames required for beamforming as specified in 9.26 (Sounding PPDUs) and in 9.31.5 (VHT

sounding protocol)(#3090)

e) Any frames required for link adaptation as specified in 9.28

f) Any number of BlockAckReq frames

# Text boxes

Abstract

This document provides resolution for the following CIDs on TGac D1.0:

CID 2157, 2158, 3047