## Slide 1: Proposal for Ping Pang Handoff Count with External Networks
Date: 2011-10-27
Authors:

## Slide 2: Background
As WIFI is pretty popular, if a traditional operator wants to provide a continuous and satisfied service to its users holding wifi-inside phones, the support for the handoff between WIFI and mobile networks is becoming necessary more and more
  Because of the complexity of the multi-access networks coverage, ping-pang handoff will be a normal thing such as in the buildings of a campus.

## Slide 3: Problem
The ping-pang handoff is bothersome, bring meaningless overload to the both-sides networks.
The frequency of the ping-pang handoff is a very important factor to optimize the radio boundary and adjust the handoff policy.
Traditionally, if a staff wants to optimize the both-side networks to decrease the possibility of the ping-pang handoff, he has to do DT with real muli-modes devices in the areas with higher user complaints.
  To make sure of whether the ping-pang handoff is just the reason
  It always takes a long time with much cost

## Slide 4: Proposal
A judgment can be made remotely, depending on the number of ping-pang handoffs:
  Which can save much time to optimize the networks boundaries or expand the network.
  Which can help adjust the handoff policy.
The way of decreasing the ping-pang handoffs is different from that of decreasing or stabling other kind of handoffs

## Slide 5: Proposal
A new counter with two additional objects is proposed to add into MIB, called dot11PingPangHandoffCount
dot11PingPangHandoffCount OBJECT-TYPE
SYNTAX Counter32
MAX-ACCESS read-only
STATUS current
DESPRITION
"This counter, only available at a WNM AP, shall increment only when a terminal MAC Address joining or leaving again in a dot11HandOffTimer cycle, only if the MAC Address was in the dot11HandoffTable ."
::= { xxxx ? }

## Slide 6: Proposal
The first Additional Object along with dot11PingPangHandoffCount is called dot11HandOffTimer
  Default value is 300 seconds?
dot11HandOffTimer OBJECT-TYPE
SYNTAX Timer
MAX-ACCESS read-write
STATUS current
DESPRITION
"This timer, serving for dot11PingPangHandoffCount. As it is 0, dot11PingPangHandoffCount doesn’t work; otherwise, in each timer cycle, dot11PingPangHandoffCount adds one if a ping-pang handoff happens, which depends on the dot11HandoffTable."
::= { xxxx ? }

## Slide 7: Proposal
The second additional object along with dot11PingPangHandoffCount is called dot11HandoffTable
dot11HandoffTable OBJECT-TYPE
SYNTAX dot11HandoffEntry
MAX-ACCESS not accessible
STATUS current
DESPRITION
“Each entry represents a row in the dot11HandoffTable and provides information about whether a mac address incomes and outcomes in continuous dot11HandOffTime cycles.“
Index {dot11HandoffMacAddress }
::= { xxxx ? }

## Slide 8: Proposal
dot11HandoffEntry ::=
SQUENCE {
dot11HandoffMacAddress MacAddress
dot11IsPingPang Integer{0,1}
}
dot11HandoffMacAddress OBJECT-TYPE
SYNTAX MacAddress
MAX-ACCESS read-only
STATUS current
DESPRITION
“Once a incoming or outgoing handoff happens and the dot11HandOffTimer is not 0, the dot11PingPangHandoffCount adds one if the corresponded mac address already was in the table. Otherwise add a new entry into the table.“
::= {dot11HandoffEntry 1 }

## Slide 9: Proposal
dot11IsPingPang OBJECT-TYPE
SYNTAX Integer{0,1}
MAX-ACCESS read-only
STATUS current
DESPRITION
“As a new mac address is added into the table, the default value is 0. And then if the handoff of the mac address happens again in the bi-direction and in a dot11HandOffTimer cycle, the value is 1 no matter how many times happens more. And in the next adot11HandOffTimer cylce, all the values of 1 will reset to 0 and the left entries will be deleted. “
::= {dot11HandoffEntry 2 }

## Slide 10: Straw Poll
Do you think it meaningful to put the dot11PingPangHandoffCount counter with two additional objects into the MIB to facilitate some service and network quality statistics?
- Yes
- No
- Don’t know