## Slide 1: A Protocol for FILS Authentication
Date: 2011-11-01
Authors:

## Slide 2: Abstract
This presentation describes a proposed FILS authentication protocol.

## Slide 3: Background: Otway-Rees
Classic 3-party protocol
Players:
  Alice, a client/peer with identity A
  Bob, a server/peer with identity B
  Trent, the trusted 3rd party with identity T
Assumptions:
  Alice shares a key with Trent, Kat
  Bob shares a key with Trent, Kbt
Notation:
  {X}y is wrapping message X with key y
  gx is a Diffie-Hellman exponential, generator g raised to power x
  Nx is a nonce, a random number, contributed by party x
  sess is a session identifier
  X  Y means X sends to Y

## Slide 4: Background: Otway-Rees
A  B: A, B, sess, {Na, A, B, sess} Kat
B  T: B, A, sess, {Na, A, B, sess} Kat, {Nb, B, A, sess} Kbt
B  T: sess, {Na, Kab}Kat, {Nb, Kab}Kbt
A  B: sess, {Na, Kab}Kat
Now Alice and Bob share a secret key, Kab, and a session identifier, sess.

## Slide 5: Background: Otway-Rees
Nonces provide a proof of “liveness” to the resulting shared key
If sess is reused a cut-and-paste attack could result in one party thinking protocol finished successfully and the other thinking it failed– not a good result
Trent, the trusted third party, is a key distributor
  Someone else besides Alice and Bob know their secret
  Trent is solely responsible for creating the secret
Alice and Bob really haven’t authenticated each other!
  They share a key with the other party but have not proven to each other that the other party knows it
We could add an Otway-Rees-like exchange, but….

## Slide 6: FILS Authentication Using a TTP
Use Diffie-Hellman to derive a unique session key
Use Trent to authenticate the exchange, not be a key distributor
Add a proof-of-possession upon completion of the exchange
Embed Alice’s message for/from Trent inside Bob’s to mitigate cut-and-paste issues

## Slide 7: FILS Authentication Using a TTP
A  B: A, sess, Na, {A, B, sess, ga} Kat
B  T: B, sess, {B, A, sess, gb, {A, B, sess, ga}Kat} Kbt
B  T: sess, {B, A, sess, gb, ga, {A, B, sess, ga, gb}Kat }Kbt,
A  B: sess, Nb, {A, B, sess, ga, gb}Kat
(gb)a = gab = (gb)a
Kab-mac | PMK = KDF(Na | Nb, gab)
A  B: HMAC(Kab-mac, sess | MAC-A | MAC-B)
B  A: HMAC(Kab-mac, sess | MAC-B | MAC-A)
Kab-ccm = KDF(PMK, sess, min(MACS), max(MACS))

## Slide 8: FILS Authentication Using a TTP
Diffie-Hellman exponentials in wrapped content provide the “liveness” proof to the exchange
Embedding messages from/for Alice into Bob’s messages helps thwart cut-and-paste attacks
Alice knows Bob created gb and Bob knows Alice created ga (because Trent said so), and they both know that the only entities that can know gab are themselves
Final two messages provide proof-of-possession of gab
Generation of a CCMP (GCMP!) key for initial use and a PMK for subsequent use

## Slide 9: Putting FILS Authentication Using a TTP Into 802.11
Authenticated Diffie-Hellman between Alice and Bob is four messages– two for the interaction with Trent, and two to prove possession of the resulting shared secret.
  Use 802.11 authentication frames for first two
  Use 802.11 association frames for second two
Fits in nicely with 802.11 state machine
  Discovery is through Beacons and Probe responses
  State 0 to State 1 transition is using authentication frames
  State 1 to State 2 transition is using association frames
  STA could associate with multiple APs while associated with another
Can put other things, like DHCP Request/Response, into 802.11 Association Request/Response

## Slide 10: Putting FILS Authentication Using a TTP Into 802.11
802.11 beacon/probe response
802.11 authentication request
802.11 authentication response
802.11 association request
802.11 association response
FILS-TTP authentication request
FILS-TTP authentication response
STAid, sess, {blob}sta-ttp
TTPid, APid
APid, sess, {blob}ap-ttp
sess, {blob}ap-ttp
sess, {blob}sta-ttp
H(K, sess | MAC-STA | MAC-AP)
H(K, sess | MAC-AP | MAC-STA)
STA
AP
TTP

## Slide 11: Putting FILS Authentication Using a TTP Into 802.11
Fast!
  Only operations using asymmetric cryptography invole the Diffie-Hellman key exchange
  The TTP does not do any computationally intensive action!
Use state-of-the-art crypto
  Use RFC 5297 for wrapping/unwrapping of blobs
  Use RFC 5869-style “extract-the-expand” KDF
  Works with elliptic curve as well as finite field cryptography
Communication with Trent:
  SME: this is the way 11r punted the R0-R1-AP communication issue
  ERP: could craft this req/resp into an EAP/Initiate-Reauth and EAP/Finish-Reauth, will work with RADIUS and Diameter (!)
  or other IETF?

## Slide 12: Properties of FILS Authentication Using a TTP
Perfect Forward Secrecy: Yes
Mutual Authentication: Yes
Key Generation: Yes
Identity Protection: No
Protection against DDOS attacks: No
Crypto-agility: Yes
Negotiation of crypto capabilities: Yes

## Slide 13: FILS Authentication, without Online Third Party
Uses Ephemeral Diffie-Hellmann to derive a unique session key
Uses Signatures to Authenticate Exchanged DH-exponents
Uses Message Authentication Code to provide key confirmation and complete exchange

## Slide 14: FILS Authentication Without a Third Party
Protocol Flows:
A  B: Na, xG, CertCA(IdA, aG), Idsess
A  B: Nb, yG, CertCA(IdA, bG), Idsess
K = h (xy)G = (hx)Y = (hy)X, where X:=xG, Y:=yG
Kab-mac | PMK = kdf(Na | Nb, K | IdA| IdB | Idsess)
A  B: MACkab-mac(flowAB, IdA, IdB), SigA(yG, xG, IdA, IdB, Idsess)
A  B: MACkab-mac(flowBA, IdB, IdA), SigB(xG, yG, IdB, IdA, Idsess)
Kab-ccm = KDF(PMK, Idsess, min(MACS), max(MACS))
Cryptographic Schemes:
Ephemeral Diffie-Hellmann CDH(1,1): NIST SP 800-56a
Signature Scheme ECDSA: FIPS 186-2
Key Derivation: Draft NIST SP 800-56C
Curve: P-256 h=1 (FIPS 186-2); SHA-256 (FIPS 180-2)

## Slide 15: Putting FILS Authentication Without a Third Party Into 802.11
802.11 beacon/probe response
802.11 authentication request
802.11 authentication response
802.11 association request
802.11 association response
xG, CertCA(STA, aG), Idsess
yG, CertCA(AP, bG), Idsess
STA
AP
TTP
MACka(#3, STA, AP), SigSTA(yG, xG, STA, AP, Idsess)
MACka(#4, AP, STA), SigAP(xG, yG, AP, STA, Idsess)
Possible to include AP key contribution in
Beacon/probe, at cost of loosing perfect
Forward secrecy; but does slim down #flows

## Slide 16: Properties of FILS Authentication Without a Third Party
Perfect Forward Secrecy: Yes
Mutual Authentication: Yes
Key Generation: Yes
Identity Protection: No
Protection against DDOS attacks: No, but not a threat if ECC implemented with some hardware support
Crypto-agility: Yes
Negotiation of crypto capabilities: Possible

## Slide 17: FILS Authentication Using a Simple Password (ala SAE)
A  B: Na, sess, scalara, elementa
A  B: Nb, sess, scalarb, elementb
(PWEscalarb * elementb)a = K = (PWEscalara * elementa)b
Kab-mac | PMK = KDF(Na | Nb, K)
A  B: HMAC(Kab-mac, sess | scalara | scalarb |
MAC-A | MAC-B)
B  A: HMAC(Kab-mac, sess | scalarb | scalara |
MAC-B | MAC-A)
Kab-ccm = KDF(PMK, sess, (scalara + scalarb) |
min(MACS), max(MACS))

## Slide 18: Putting FILS Authentication Using a Simple Password Into 802.11
802.11 beacon/probe response
802.11 authentication request
802.11 authentication response
802.11 association request
802.11 association response
Na, scalara, elementa, Idsess
STA
AP
Nb, scalarb, elementb, Idsess
H(K, Idsess | MAC-STA | MAC-AP)
H(K, Idsess | MAC-AP| MAC-STA)

## Slide 19: Properties of FILS Authentication Using a Simple Password (ala SAE)
Perfect Forward Secrecy: Yes
Mutual Authentication: Yes
Key Generation: Yes
Identity Protection: No
Protection against DDOS attacks: No
Crypto-agility: Yes
Negotiation of crypto capabilities: Yes

## Slide 20: FILS Authentication
Two Message Exchange supports many options
  Authentication using symmetric keys and a trusted third party
  Authentication using certificates without a trusted third party
  Authentication using passwords without a trusted third party
Many desirable security properties
  Mutual authentication
  Perfect Forward Secrecy
  Key Generation
  Crypto-agility
Use state-of-the-art cryptography

## Slide 21: Conformance with TGai PAR & 5C
Conformance Question | Response
Does the proposal degrade the security offered by Robust Security Network Association (RSNA) already defined in 802.11? | No
Does the proposal change the MAC SAP interface? | No
Does the proposal require or introduce a change to the 802.1 architecture? | No
Does the proposal introduce a change in the channel access mechanism? | No
Does the proposal introduce a change in the PHY? | No
Which of the following link set-up phases is addressed by the proposal? (1) AP Discovery (2) Network Discovery (3) Link (Re-)establishment, exchange of security related messages (4) Higher layer aspects, e.g. IP address assignment. | 3

## Slide 22: References