## Slide 1: A Protocol for FILS Authentication
Date: 2012-01-09
Authors:

## Slide 2: Abstract
This presentation describes a proposed FILS authentication protocol.

## Slide 3: Conformance with TGai PAR & 5C
Conformance Question | Response
Does the proposal degrade the security offered by Robust Security Network Association (RSNA) already defined in 802.11? | No
Does the proposal change the MAC SAP interface? | No
Does the proposal require or introduce a change to the 802.1 architecture? | No
Does the proposal introduce a change in the channel access mechanism? | No
Does the proposal introduce a change in the PHY? | No
Which of the following link set-up phases is addressed by the proposal? (1) AP Discovery (2) Network Discovery (3) Link (Re-)establishment, exchange of security related messages (4) Higher layer aspects, e.g. IP address assignment. | 3

## Slide 4: Otway-Rees: Authentication with a TTP
Classic 3-party protocol
Players:
  Alice, a client/peer with identity A
  Bob, a server/peer with identity B
  Trent, the trusted 3rd party with identity T
Assumptions:
  Alice shares a key with Trent, Kat
  Bob shares a key with Trent, Kbt
Notation:
  {X}y is wrapping message X with key y
  gx is a Diffie-Hellman exponential, generator g raised to power x
  Nx is a nonce, a random number, contributed by party x
  sess is a session identifier
  X  Y means X sends to Y

## Slide 5: “Otway-Rees” with Key Confirmation
A  B: A, B, sess, {Na, A, B, sess} Kat
B  T: B, A, sess, {Nb, B, A, sess, {Na, A, B, sess} Kat} Kbt
B  T: sess, {Nb, Na, Kab, {Na, Nb, Kab}Kat}Kbt
A  B: sess, {Na, Nb, Kab}Kat
Kab-mac | PMK = KDF(Na | Nb, Kab)
A  B: HMAC(Kab-mac, sess | MAC-A | MAC-B)
A  B: HMAC(Kab-mac, sess | MAC-B | MAC-A)
Kab-ccm = KDF(PMK, sess, min(MACS), max(MACS))

## Slide 6: “Otway-Rees” with Key Confirmation
Nonces provide a proof of “liveness” to the resulting shared key
Embedding Alice’s messages in Bob’s thwarts certain cut-and-paste attacks
Final two messages provide proof-of-possession Kab
Trent, the trusted third party, is a key distributor
  Someone else besides Alice and Bob know their secret
  Trent is solely responsible for creating the secret
If either Alice’s or Bob’s long-term secret is compromised, then all past sessions can be exposed
  Lacks Perfect Forward Secrecy (PFS)

## Slide 7: Authentication Using a TTP– Adding PFS
Use Diffie-Hellman exchange to derive a unique session key
Use Trent to authenticate the exchange, not be a key distributor
Diffie-Hellman exchange provides Perfect Forward Secrecy– if Alice’s or Bob’s long term secret is compromised, past sessions remain confidential and secure.

## Slide 8: Authentication Using a TTP– Adding PFS
A  B: A, sess, Na, {A, B, sess, ga} Kat
B  T: B, sess, {B, A, sess, gb, {A, B, sess, ga}Kat} Kbt
B  T: sess, {B, A, sess, gb, ga, {A, B, sess, ga, gb}Kat }Kbt,
A  B: sess, Nb, {A, B, sess, ga, gb}Kat
(gb)a = gab = (gb)a
Kab-mac | PMK = KDF(Na | Nb, gab)
A  B: HMAC(Kab-mac, sess | MAC-A | MAC-B)
A  B: HMAC(Kab-mac, sess | MAC-B | MAC-A)
Kab-ccm = KDF(PMK, sess, min(MACS), max(MACS))

## Slide 9: Authentication Using a TTP– Adding PFS
Diffie-Hellman exponentials in wrapped content provide the “liveness” proof to the exchange
Embedding messages from/for Alice into Bob’s messages helps thwart cut-and-paste attacks
Alice knows Bob created gb and Bob knows Alice created ga (because Trent said so), and they both know that the only entities that can know gab are themselves
Final two messages provide proof-of-possession of gab
Generation of a CCMP (GCMP!) key for initial use and a PMK for subsequent use

## Slide 10: Putting FILS Authentication Using a TTP Into 802.11
Authenticated Diffie-Hellman between Alice and Bob is four messages– two for the interaction with Trent, and two to prove possession of the resulting shared secret.
  Use 802.11 authentication frames for first two
  Use 802.11 association frames for second two
Fits in nicely with 802.11 state machine
  Discovery is through Beacons and Probe responses
  State 0 to State 1 transition is using authentication frames
  State 1 to State 2 transition is using association frames
  STA could associate with multiple APs while associated with another
Can put other things, like DHCP Request/Response, into 802.11 Association Request/Response

## Slide 11: Putting FILS Authentication Using a TTP Into 802.11
802.11 beacon/probe response
802.11 authentication request
802.11 authentication response
802.11 association request
802.11 association response
FILS-TTP authentication request
FILS-TTP authentication response
STAid, sess, {blob}sta-ttp
TTPid, APid
APid, sess, {blob}ap-ttp
sess, {blob}ap-ttp
sess, {blob}sta-ttp
H(K, sess | MAC-STA | MAC-AP)
H(K, sess | MAC-AP | MAC-STA)
STA
AP
TTP

## Slide 12: Putting FILS Authentication Using a TTP Into 802.11
Fast!
  Only operations using asymmetric cryptography invole the Diffie-Hellman key exchange
  PFS is optional!
  The TTP does not do any computationally intensive action!
Use state-of-the-art crypto
  Use RFC 5297 for wrapping/unwrapping of blobs
  Use RFC 5869-style “extract-the-expand” KDF
  Works with elliptic curve as well as finite field cryptography
Communication with Trent:
  Use existing infrastructure: RADIUS or DIAMETER.

## Slide 13: Properties of FILS Authentication Using a TTP
Perfect Forward Secrecy: Yes, optionally
Mutual Authentication: Yes
Key Generation: Yes
Identity Protection: No
Protection against DDOS attacks: No
Crypto-agility: Yes
Negotiation of crypto capabilities: Yes

## Slide 14: References