IEEE P802.11
Wireless LANs

| D1.0 Comment Resolution – Misc. CIDs 2303, 2390, 2862, 3404, 3409 |
| --- |
| Date: 2011-11-03 |
| Author(s): |
| Name | Affiliation | Address | Phone | email |
| Illsoo Sohn | LG Electronics | LG R&D Complex 533, Hogye-1dong, Dongan-Gu, Anyang-Shi, Kyungki-Do, 431-749, Korea | +82-31-450-1882 | Illsoo.sohn@lge.com |
| Yongho Seok | LG Electronics | LG R&D Complex 533, Hogye-1dong, Dongan-Gu, Anyang-Shi, Kyungki-Do, 431-749, Korea | +82-31-450-1947 | yongho.seok@lge.com |

Abstract

This document provides resolutions for the following comments to 11ac spec draft D1.0:

CIDs 2303, 2390, 2862, 3404, and 3409.

| CID | Clause | Page | Comment | Proposed Change | Owning ad-hoc |
| --- | --- | --- | --- | --- | --- |
| 2303 | 9.19.2.7 | 85.35 | When a CF-End is sent by a TXOP holding VHT STA or AP to truncate the TXOP and reset NAV on primary and secondary channels, it will reset the NAV for STAs associated with the same VHT BSS but not for OBSS STAs that had their NAV set by the TXOP holder. So the OBSS STAs for which the primary channel is the TXOP holder's secondary channel are at a disadvantage and will be unfairly denied channel access. Given that there will be dense deployment of 11ac devices such OBSS scenarios are very likely to occur and lead to poor performance. This unfairness issue needs to be resolved. | Update TXOP truncation rules for VHT with CF-End to remove this unfairness in channel access for some STAs. | MAC |

##### Proposed Resolution:

Disagree. Please see the note in 9.19.2.7 Truncation of TXOP (REVmb_10.0):

“NOTE—The transmission of a single CF-End frame by the TXOP holder resets the NAV of STAs hearing the TXOP holder. There may be STAs that could hear the TXOP responder that had set their NAV that do not hear this NAV reset. Those STAs are prevented from contending for the medium until the original NAV reservation expires.”

Even in the same BSS, a STA may not hear the CF-END. Then, the STA does not reset NAV and cannot attend contention. The AP of the BSS may make this operation more efficient by repeating CF-END after SIFS. Considering an OBSS case is not a VHT-specific issue. The operation regarding the truncation of TXOP may be further improved in the baseline spec.

| CID | Clause | Page | Comment | Proposed Change | Owning ad-hoc |
| --- | --- | --- | --- | --- | --- |
| 2390 | 22.3.6 | 130.21 | Content of note is pretty clear from the equations above; recommend adding an extra column(s) to Table 22-7 (for guard interval and for T_subfield, that contain the pre-defined variable names from Table 22-4) or a free-standing table for clarity | As in comment | PHY |

##### Proposed Resolution:

Agree. See the proposed text changes in 11/xxxxr0.

##### Editing Instructions

22. Very High Throughput (VHT) PHY specification

22.3 VHT PLCP sublayer

22.3.6 Timing-related constants

Editor: Please change Table 22-4 (Timing-related constants) as follows:

| Timing-related constants |
| --- |
| Parameter | CBW20(#1156) | CBW40 | CBW80 | CBW80+80 | CBW160 | Description(#899) |
| NSD | 52 | 108 | 234 | 234 | 468 | Number of complex data numbers per frequency segment |
| NSP | 4 | 6 | 8 | 8 | 16 | Number of pilot values per frequency segment |
| NST | 56 | 114 | 242 | 242 | 484 | Total number of subcarriers per frequency segment. See NOTE. |
| NSR | 28 | 58 | 122 | 122 | 250 | Highest data subcarrier index per frequency segment |
| NSeg | 1 | 1 | 1 | 2 | 1 | Number of frequency segments |
| ∆F | 312.5 kHz | Subcarrier frequency spacing |
| TDFT | 3.2 µs | IDFT/DFT period |
| TGI | 0.8 µs = TDFT /4 | Guard interval duration |
| TGI2 | 1.6 µs | Double guard interval |
| TGIS | 0.4 µs = TDFT /8 | Short guard interval duration |
| TSYML | 4 µs = TDFT + TGI = 1.25 x TDFT (#343) | Long GI symbol interval |
| TSYMS | 3.6 µs = TDFT + TGIS = 1.125 x TDFT (#343) | Short GI symbol interval |
| TSYM | TSYML or TSYMS depending on the GI used (SeeTable 22-7 (Tone scaling factor and guard interval duration values for PLCP fields))(#343) | Symbol interval |
| TL-STF | 8 µs = 10 x TDFT /4 | Non-HT Short Training field duration(Ed) |
| TL-LTF | 8 µs = 2 x TDFT + TGI2(#342) | Non-HT Long Training field duration(Ed) |
| TL-SIG | 4 µs = TSYML(#343) | Non-HT SIGNAL field duration(Ed) |
| TVHT-SIG-A | 8 µs = 2TSYML(#343) | VHT Signal A field duration |
| TVHT-STF | 4 µs = TSYML(#343) | VHT Short Training field duration |
| TVHT-LTF | 4 µs = TSYML(#343) | Duration of each VHT-LTF field |
| TVHT-SIG-B | 4 µs = TSYML(#343) | VHT Signal B field duration |
| Nservice | 16 | Number of bits in the SERVICE field(#421) |
| Ntail | 6 | Number of tail bits per BCC encoder(#421) |
| NOTE—NST = NSD + NSP (#343)(Ed) |

22.3.7 Mathematical description of signals

Editor: Please change Table 22-7 (Value of tone scaling factor) as follows:

| Table 22-7--Tone scaling factor and guard interval duration values for PLCP fields |
| --- |
| Field | as a function of bandwidth per frequency segment | Guard interval duration |
|  | 20 MHz | 40 MHz | 80 MHz | 160 MHz |  |
| L-STF | 12 | 24 | 48 | 96 | - |
| L-LTF | 52 | 104 | 208 | 416 | TGI2 |
| L-SIG | 52 | 104 | 208 | 416 | TGI |
| VHT-SIG-A | 52 | 104 | 208 | 416 | TGI |
| VHT-STF | 12 | 24 | 48 | 96 | - |
| VHT-LTF | 56 | 114 | 242 | 484 | TGI |
| VHT-SIG-B | 56 | 114 | 242 | 484 | TGI |
| VHT-Data | 56 | 114 | 242 | 484 | TGI or TGIS (See NOTE2) |
| NON-HT-DUP (See NOTE1) | - | 104 | 208 | 416 | TGI |
| NOTE1—NON-HT-DUP is not a field, but refers to the non-HT duplicate format PPDU. For notational convenience it is grouped here with the fields of the VHT format PPDU. NOTE2— TGI denotes guard interval duration when TXVECTOR parameter GI_TYPE equals LONG_GI, TGIS denotes short guard interval duration when TXVECTOR parameter GI_TYPE equals SHORT_GI. |

| CID | Clause | Page | Comment | Proposed Change | Owning ad-hoc |
| --- | --- | --- | --- | --- | --- |
| 2862 | 8 |  | The way HT IEs (HT Cap, HT Op, 20/40 Op, etc.) are used when VHT IEs are present needs to be clarified. Things like: are things like GF, DSSS/CCK mode, PCO, HT beamforming capabilities, antenna selection, STBC, UEQM, etc. | Clarify | MAC |

##### Proposed resolution:

Disagree. HT Capabilities and VHT Capabilities indicate STA’s capability for HT BSS and VHT BSS operations, respectively. For VHT devices, capabilities info in HT-Greenfield, DSSS/CCK Mode in 40MHz, TX Unequal Modulation Supported, PCO, Transmit Beamforming Capabilities, ASEL Capability fields, etc. can be interpreted as STA’s capabilities working as a HT STA. Thus, there should be no ambiguity in HT Capability element.

Regarding operating channel bandwidth, VHT BSS operating channel width is jointly encoded with STA Channel Width values in HT Operation element and VHT Operation element, which is clearly defined in 10.40 (VHT BSS operation). Also, other related settings can be found in 10.40.1 (Basic VHT BSS functionality).

| CID | Clause | Page | Comment | Proposed Change | Owning ad-hoc |
| --- | --- | --- | --- | --- | --- |
| 3404 | 8.2.4.5.4 | 21.39 | To avoid Ack collision in MU-MIMO, clarify that Implicit Block Ack policy shall not be set in more than one PPDU. | As in comment. | MAC |

##### Proposed resolution:

Disagree. There is already a rule for A-MPDU in Table 8-ac23 (A-MPDU contents MPDUs in MU PPDU context):

“An MU PPDU may carry at most one A-MPDU that contains one or more MPDUs soliciting an immediate response”

This statement covers the issue well. Thus, no text changes are required.

| CID | Clause | Page | Comment | Proposed Change | Owning ad-hoc |
| --- | --- | --- | --- | --- | --- |
| 3409 | 3.2 | 2.26 | "BSSBasicMCSSet: The set of modulation and coding scheme (MCS) values that are supported by all highthroughput (HT) stations (STAs) that are members of an HT basic service set (BSS)." The BSSBasicMCSSet definition should be changed for VHT stations or new definition should be defined for VHT stations. | Clarify the BSSBasicMCSSet. | MAC |

##### Proposed resolution:

Agree in principle. In 11ac D1.2, the definition of “VHTBSSBasicMCSSet” is added in 3.2 and the name of “Basic MCS Set” field of VHT Operation Element is changed to “VHT Basic MCS Set” for clarification. All the other terminologies also have been changed accordingly. Please see 11/1144r9 for detailed text changes.