IEEE P802.11
Wireless LANs

| Normative text for FILS |
| --- |
| Date: 2011-11-4 |
| Author(s): |
| Name | Company | Address | Phone | email |
| Zhiming Ding | Huawei | Bld 7, Vision Business Park, Nanshan Science Park, Shenzhen City, China | +86-755-21535837 | dingzhiming@huawei.com |
| Ping Fang | Huawei | Bld 7, Vision Business Park, Nanshan Science Park, Shenzhen City, China | +86-755-36835101 | Ping.fang@huawei.com |
| Phillip Barber | Huawei | 1700 Alma Rd, Ste 500 Plano, Texas 75075 USA | +1 972-509-5599 | pbarber@huawei.com |

Abstract

This document contains normative text for fast initial link setup protocol based on 11mb draft 12.0.

6.3.5 Authenticate

6.3.5.1 Introduction

This mechanism supports the process of establishing an authentication relationship with a peer MAC entity.

[Change subclause 6.3.5.2 as:]

6.3.5.2 MLME-AUTHENTICATE.request

6.3.5.2.1 Function

This primitive requests authentication with a specified peer MAC entity.

6.3.5.2.2 Semantics of the service primitive

The primitive parameters are as follows:

MLME-AUTHENTICATE.request(

PeerSTAAddress,

AuthenticationType,

AuthenticateFailureTimeout,

Content of FT Authentication elements,

Content of SAE Authentication Frame,

Content of FILS Authentication Frame,

VendorSpecificInfo

)

| Name | Type | Valid range | Description |
| --- | --- | --- | --- |
| PeerSTAAddress | MACAddress | Any valid individual MAC address | Specifies the address of the peer MAC entity with which to perform the authentication process. |
| AuthenticationType | Enumeration | OPEN_SYSTEM, SHARED_KEY, FAST_BSS_TRANSITION, SAE, FAST_INITIAL_LINK_SETUP | Specifies the type of authentication algorithm to use during the authentication process. |
| AuthenticationFailureTimeout | Integer | ≥1 | Specifies a time limit (in TU) after which the authentication procedure is terminated. |
| Content of FT Authentication elements | Sequence of elements | As defined in 12.8 | The set of elements to be included in the first message of the FT authentication sequence, as described in 12.8.2. Present only if dot11FastBSSTransitionActivated is true. |
| Content of SAE Authentication Frame | Sequence of elements and fields | As defined in 8.4.1.37, 8.4.1.38, 8.4.1.39, 8.4.1.40, 8.4.1.41, and 8.4.1.42 | The set of elements and fields to be included in the SAE Commit Message or SAE Confirm Message. Present only if AuthenticationType indicates SAE authentication. |
| Content of FILS Authentication Frame | Sequence of elements and fields | TBD | TBD |
| VendorSpecificInfo | A set of elements | As defined in 8.4.2.28 | Zero or more elements. |

6.3.5.4.2 Semantics of the service primitive

The primitive parameters are as follows:

MLME-AUTHENTICATE.indication(

PeerSTAAddress,

AuthenticationType,

Content of FT Authentication elements,

Content of SAE Authentication Frame,

Content of FILS Authentication Frame,

VendorSpecificInfo

)

| Name | Type | Valid range | Description |
| --- | --- | --- | --- |
| PeerSTAAddress | MACAddress | Any valid individual MAC address | Specifies the address of the peer MAC entity with which the authentication relationship was established. |
| AuthenticationType | Enumeration | OPEN_SYSTEM, SHARED_KEY, FAST_BSS_TRANSITION, SAE, FAST_INITIAL_LINK_SETUP | Specifies the type of authentication algorithm that was used during the authentication process. |
| Content of FT Authentication elements | Sequence of elements | As defined in 12.8 | The set of elements to be included in the first message of the FT authentication sequence, as described in 12.8.2. Present only if dot11FastBSSTransitionActivated is true. |
| Content of SAE Authentication Frame | Sequence of elements and fields | As defined in 8.4.1.37, 8.4.1.38, 8.4.1.39, 8.4.1.40, 8.4.1.41, and 8.4.1.42 | The set of elements to be included in the SAE Commit Message or SAE Confirm Message. Present only if AuthenticationType indicates SAE authentication. |
| Content of FILS Authentication Frame | Sequence of elements and fields | TBD | TBD |
| VendorSpecificInfo | A set of elements | As defined in 8.4.2.28 | Zero or more elements. |

6.3.5.5.2 Semantics of the service primitive

The primitive parameters are as follows:

MLME-AUTHENTICATE.response(

PeerSTAAddress,

ResultCode,

Content of FT Authentication elements,

Content of SAE Authentication Frame,

Content of FILS Authentication Frame,

VendorSpecificInfo

)

| Name | Type | Valid range | Description |
| --- | --- | --- | --- |
| PeerSTAAddress | MACAddress | Any valid individual MAC address | Specifies the address of the peer MAC entity from which the authentication request was received. |
| ResultCode | Enumeration | SUCCESS, REFUSED, ANTICLOGGING TOKEN REQUIRED, FINITE CYCLIC GROUP NOT SUPPORTED, AUTHENTICATION REJECTED | Indicates the result response to the authentication request from the peer MAC entity. |
| Content of FT Authentication elements | Sequence of elements | As defined in 12.8 | The set of elements to be included in the first message of the FT authentication sequence, as described in 12.8.2. Present only if dot11FastBSSTransitionActivated is true. |
| Content of SAE Authentication Frame | Sequence of elements and fields | As defined in 8.4.1.37, 8.4.1.38, 8.4.1.39, 8.4.1.40, 8.4.1.41, and 8.4.1.42 | The set of elements to be included in the SAE Commit Message or SAE Confirm Message. Present only if AuthenticationType indicates SAE authentication. |
| Content of FILS Authentication Frame | Sequence of elements and fields | TBD | TBD |
| VendorSpecificInfo | A set of elements | As defined in 8.4.2.28 | Zero or more elements. |

8.3.3.11 Authentication frame format

The frame body of a management frame of subtype Authentication contains the information shown in Table 8-28. FT authentication is used when FT support is advertised by the AP and dot11FastBSSTransitionActivated is true in the STA. SAE authentication is used when dot11MeshActiveAuthenticationProtocol is sae (1).

[Change Table 8-28 as:]

Table 8-28—Authentication frame body

| Order | Information | Notes |
| --- | --- | --- |
| 5 | RSN | The RSNE is present in the FT and FILS Authentication frames as defined in Table 8-29. |
| … |  |  |
| 16 | Upper Layer Message | An ULME is present in the FILS Authentication frames as defined in Table 8-29. Multiple ULMEs can be present to encapsulate a single upper layer message. Multiple upper layer messages can be encapsulated in different ULME. These upper layer messages includes EAPoL messages defined in 802.1x and EAPoL_Key frames defined in 11.6.2 and DHCP messages. The detail of the ULME usage sees TBD. |
| … | <Elements in Association frames> | When field Authentication algorithm is FAST_INITIAL_LINK_SETUP as defined in Table 8-29, multiple elements present in Association frames can be present in the third and fourth Authentication frames except the same elements present both Authentication and Association frames in order to implement function of Association frames during FILS authentication in concurrence. |
| Last-1 | Vendor Specific | One or more vendor-specific elements are optionally present. These elements follow all other elements. |
| Last | MIC | The MICE is present in the last two FILS Authentication frames as defined in Table 8-29. |

[Change Table 8-29 as:]

Table 8-29—Presence of fields and elements in Authentication frames

| Authentication algorithm | Authentication transaction sequence no. | Status code | Presence of fields 4- Last-1 |
| --- | --- | --- | --- |
| FILS | 1 | Reserved | One group of ULMEs are present and an EAPoL(EAP_Response/ID) is encapsulated in them. |
| FILS | 2 | Status | Two groups of ULMEs are present. An EAPoL(EAP_Request), the first EAP_Request of EAP method is encapsulated in first group of ULMs. The First EAPoL(EAPoL-Key) of 4-way handshake is encapsulated in second group of ULMs. |
| FILS | 2+x(x=1,3,5) | Status | One groups of ULMEs are present. An EAPoL(EAP_Response), one of the middle EAP_Response of EAP method is encapsulated in the ULMs. |
| FILS | 2+x(x=2,4,6) | Status | One groups of ULMEs are present. An EAPoL(EAP_Request), one of the middle EAP_Request of EAP method is encapsulated in the ULMs. |
| FILS | Last-1/3 | Status | Three groups of ULMEs are present. An EAPoL(EAP_Response), the last EAP_Response of EAP method is encapsulated in first group of ULMs. The second EAPoL(EAPoL-Key) of 4-way handshake is encapsulated in second group of ULMs. A DHCPDISCOVER with rapid commit option is encapsulated in third group of ULMs. |
| FILS | Last/4 | Status | Three groups of ULMEs are present. An EAPoL(EAP_Success or EAP_Failure), the result of EAP method is encapsulated in first group of ULMs. The third EAPoL(EAPoL-Key) of 4-way handshake is encapsulated in second group of ULMs. A DHCPACK with rapid commit option is encapsulated in third group of ULMs. |

[Change subclause 8.4.1.1 as:]

8.4.1.1 Authentication Algorithm Number field

The Authentication Algorithm Number field indicates a single authentication algorithm. The length of the Authentication Algorithm Number field is 2 octets. The Authentication Algorithm Number field is illustrated in Figure 8-35. The following values are defined for authentication algorithm number:

Authentication algorithm number = 0: Open System

Authentication algorithm number = 1: Shared Key

Authentication algorithm number = 2: Fast BSS Transition

Authentication algorithm number = 3: simultaneous authentication of equals (SAE)

Authentication algorithm number = 4: Fast Initial Link Setup (FILS)

Authentication algorithm number = 65 535: Vendor specific use

NOTE—The use of this value implies that a Vendor Specific element is included with more information.

All other values of authentication algorithm number are reserved.

8.4.2.27 RSN element

8.4.2.27.3 AKM suites

[Change Table 8-101 as:]

Table 8-101—AKM suite selectors

| OUI | Suite Type | Meaning |
| --- | --- | --- |
|  |  | Authentication type | Key management type | Key derivation type |
| 00-0F-AC | 10 | FILS over 802.1x | RSNA key management as defined in 11.6. | Defined in 11.6.1.2 |
| 00-0F-AC | 11 | FILS using PSK | RSNA key management as defined in 11.6, using PSK | Defined in 11.6.1.2 |
| 00-0F-AC | 12–255 | Reserved | Reserved | Reserved |

8.4.2.29 Extended Capabilities element

[Change Table 8-101 as:]

Table 8-103—Capabilities field

| Bit | Information | Notes |
| --- | --- | --- |
| 47 or any other? | Fast Initial Link Setup | The STA sets the Fast Initial Link Setup field to 1 when dot11MgmtOptionFILSActivated is true and sets it to 0 otherwise. See 10.25. |

[Change subclause 8.4.2.121 as:]

8.4.2.121 MIC element

The MIC element (MICE) provides message integrity to some management frames e.g. Mesh Peering Management frames and the last two FILS Authentication frames. The format of the MIC element is shown in Figure 8-401.

The Element ID is set to the value given in Table 8-54 for this element.

The Length field is set to 16.

Figure 8-401—MIC element format

The MIC field contains a message integrity code calculated over the management frame e.g. the Mesh Peering Management frame (as specified in 13.5) and the mesh group key handshake frame (as specified in 13.6) and the last two FILS Authentication frames (as specified in 10.25).

[Insert subclause 8.4.2.122 as:]

8.4.2.122 ULM element

The ULM element includes one or part of an upper layer message. Multiple ULM elements may be occurred in a management frame to carry a whole upper layer message. Multiple types of upper layer message may be included in ULM elements. This element is shown in Figure 8-11ai01.

Figure 8-11ai01 ULM element format

The Element ID is set to the value given in Table 8-54 (Element IDs) for this element.

The Length field is set to the value of bytes of the field Upper Layer Message.

The ULM Control field is shown in Figure 8-11ai02.

Figure 8-11ai02 ULM Control field format

The ULM Fragment Flag is set to 1 if another ULM element for the same upper layer message follows this element and is set to 0 if no more ULM element for the same upper layer message follows this element.

The ULM Tag is an identifier of upper layer message in order to matching the messages of same session on upper layer when the upper layer messages come into or go out from the IE layer.

ULM Body is a whole upper layer message or part of an upper layer message.

10.3.2 State transition diagram for non-mesh STAs

Figure 10-6 shows the state transition diagram for non-mesh STA states. Note that only events causing state changes are shown. The state of the sending STA given by Figure 10-6 is with respect to the intended receiving STA.

[Change Figure 10-6 as:]

Figure 10-6—Relationship between state and services

[Change subclause 10.3.4 as:]

10.3.4 Authentication and deauthentication

This subclause describes the procedures used for IEEE 802.11 authentication and deauthentication. The states used in this description are defined in 10.3.1.

Successful authentication sets the STA's state to State 2, if it was in State 1. Successful FILS authentication sets the STA’s state to State4 directly, if it was in State1. Unsuccessful authentication leaves the STA's state unchanged. The STA shall not transmit Class 2 frames unless in State 2 or State 3 or State 4. The STA shall not transmit Class 3 frames unless in State 3 or State 4.

Deauthentication notification sets the STA's state to State 1. The STA shall become authenticated again prior to sending Class 2 frames. Deauthentication notification when in State 3 or 4 implies disassociation as well. A STA may deauthenticate a peer STA at any time, for any reason.

If STA A in an infrastructure BSS receives a Class 2 or Class 3 frame from STA B that is not authenticated with STA A (i.e., the state for STA B is State 1), STA A shall discard the frame. If the frame has an individual address in the Address 1 field, the MLME of STA A shall send a Deauthentication frame to STA B.

Authentication is optional in an IBSS. In an infrastructure BSS, authentication is required. APs do not

initiate authentication.

10.3.4.2 Authentication—originating STA

Upon receipt of an MLME-AUTHENTICATE.request primitive, the originating STA shall authenticate with the indicated STA using the following procedure:

- If the STA is in an IBSS the SME shall delete any PTKSA and temporal keys held for communication with the indicated STA by using the MLME-DELETEKEYS.request primitive (see 11.5.15).

- The STA shall execute one of the following:

  - For the Open System or Shared Key authentication algorithm, the authentication mechanism described in 11.2.3.2 or 11.2.3.3, respectively.

  - For the FT authentication algorithm in an ESS, the authentication mechanism described in 12.5, or, if resource requests are included, 12.6.

  - For SAE authentication in an ESS, IBSS, or MBSS, the authentication mechanism described in 11.3.

  - For FILS authentication in an ESS, TBD.

- If the authentication was successful within the AuthenticateFailureTimeout, the state for the indicated STA shall be set to State 2 if it was State 1; the state shall remain unchanged if it was other than State 1.

- The MLME shall issue an MLME-AUTHENTICATE.confirm primitive to inform the SME of the result of the authentication.

10.3.4.3 Authentication—destination STA

Upon receipt of an Authentication frame with authentication transaction sequence number equal to 1, the destination STA shall authenticate with the originating STA using the following procedure:

- If Open System or Shared Key authentication algorithm is being used, the STA shall execute the procedure described in 11.2.3.2 or 11.2.3.3, respectively. These result in the generation of an MLME-AUTHENTICATE.indication primitive to inform the SME of the authentication request.

- If FT authentication is being used, the MLME shall issue an MLME-AUTHENTICATE.indication primitive to inform the SME of the authentication request, including the FT Authentication Elements, and the SME shall execute the procedure as described in 12.5 or 12.6.

- If SAE authentication is being used in an ESS, IBSS, or MBSS, the MLME shall issue an MLMEAUTHENTICATE. indication primitive to inform the SME of the authentication request, including the SAE Authentication Elements, and the SME shall execute the procedure as described in 11.3

- If FILS authentication is being used in an ESS TBD.

- If the STA is in an IBSS and management frame protection was not negotiated when the PTKSA(s) were created, the SME shall delete any PTKSA and temporal keys held for communication with the originating STA by using the MLME-DELETEKEYS.request primitive (see 11.5.15).

- Upon receipt of an MLME-AUTHENTICATE.response primitive, if the ResultCode is not SUCCESS, the MLME shall transmit an Authentication frame with the corresponding status code, as defined in 8.4.1.9, and the state for the originating STA shall be left unchanged. The Authentication frame is constructed using the appropriate procedure in 11.2.3.2, 11.2.3.3, 12.5 or 12.6.

- Upon receipt of an MLME-AUTHENTICATE.response primitive, if the ResultCode is SUCCESS, the MLME shall transmit an Authentication frame that is constructed using the appropriate procedure in 11.2.3.2, 11.2.3.3, 12.5 or 12.6, with a status code of Successful, and the state for the originating STA shall be set to State 2 if it was in State 1.

If the STA is in an IBSS, if the SME decides to initiate an RSNA, and if the SME does not know the security policy of the peer, it may issue an individually addressed Probe Request frame to the peer by invoking an MLME-SCAN.request primitive to discover the peer’s security policy.

[Insert subclause 10.25 as:]

10.25 Fast initial link setup

Describe what is FILS.

Describe how to FILS.

The main points are:

  - FILS Capability indication in Beacon and Probe Response

  - No Association for FILS

  - Changes to 4-Way handshake with concurrently running EAP

  - Changes to state machine for FILS authentication.

  - New information element for encapsulating upper layer message

  - IP address assigning in Authentication frames with DHCP rapid commit

# Text boxes

Notice: This document has been prepared to assist IEEE 802.11. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s).  The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.

Release: The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication.  The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.11.

Patent Policy and Procedures: The contributor is familiar with the IEEE 802 Patent Policy and Procedures <http:// ieee802.org/guides/bylaws/sb-bylaws.pdf>, including the statement "IEEE standards may include the known use of patent(s), including patent applications, provided the IEEE receives assurance from the patent holder or applicant with respect to patents essential for compliance with both mandatory and optional portions of the standard."  Early disclosure to the Working Group of patent information that might be relevant to the standard is essential to reduce the possibility for delays in the development process and increase the likelihood that the draft publication will be approved for publication.  Please notify the Chair <stuart@ok-brit.com> as early as possible, in written or electronic form, if patented technology (or technology under patent application) might be incorporated into a draft standard being developed within the IEEE 802.11 Working Group. If you have questions, contact the IEEE Patent Committee Administrator at <patcom@ieee.org>.