IEEE P802.11
Wireless LANs

| D1.0 Comment Resolutions on Link Adaptation CID 3730 |
| --- |
| Date: 2011-11-03 |
| Author(s): |
| Name | Affiliation | Address | Phone | Email |
| Hongyuan Zhang | Marvell | 5488 Marvell Ln, Santa Clara, CA 95054 | 408-222-1837 | hongyuan@marvell.com |

##### Abstract: Resolutions of D1.0 comments on Link Adaptations (9.27):  CIDs 3730

##### CIDs 3730

| 3730 | Wang, James | 9.27.3 | 88.43 | Note this statement is tru only for solicited feedback "Additionally, MFB estimate shall be based on the bandwidth indicated by the Channel Width subfield of the VHT MIMO Control field of the VHT Compressed Beamforming frame." | Please specify it is for solicited feedback only | Disagree |
| --- | --- | --- | --- | --- | --- | --- |

Discussions: This whole paragraph talks about the case in which the MFB is in the same PPDU as a VHT Compressed Beamforming frame. In this case, the quoted sentence is correct regardless solicited or unsolicited feedbacks.