IEEE P802.11
Wireless LANs

| CVS comments Resolution |
| --- |
| Date: 2011-11-04 |
| Author(s): |
| Name | Company | Address | Phone | Email |
| Eunsun Kim | LG Electronics | Mobile Comm. Lab, LG R&D Complex 533, Hogye1, Dongan, Anyang, Korea | +82-31-450-1860 | Esun.kim@lge.com |

Interpretation of a Motion to Adopt

A motion to approve this submission means that the editing instructions and any changed or added material are actioned in the TGaf Draft.  This introduction is not part of the adopted material.

Editing instructions formatted like this are intended to be copied into the TGaf Draft (i.e. they are instructions to the 802.11 editor on how to merge the text with the baseline documents).

TGaf Editor: Editing instructions preceded by “TGaf Editor” are instructions to the TGaf editor to modify existing material in the TGaf draft.  As a result of adopting the changes, the TGaf editor will execute the instructions rather than copy them to the TGaf Draft.

| CID | Page | Clause | Comment | Proposed Change |
| --- | --- | --- | --- | --- |
| 116 | 22.10 | 6.3.af6 | The figure illustrating basic protocol is presented as example which is informational and doesn’t add any additional content so it shouldn’t be in the normative section | Move the example to the appropriate explanatory section in Annex |

Discussion

(From 11-11/643r2 resolving CID 93) “Since the request/confirm/indication/response service primitives for layer management in MLME SAP interface follow standard structure of detailed text that has been already explained in 6.1 (Overview of management model) and 6.2 (Generic management primitives) of the baseline specification, it is not always required to include similar protocol exchange figures between two entities in the specification. While reviewing the recent baseline REVmb 11.0, only very few amendments (e.g. 802.11k) have provided such figures to some of the interfaces. However, none of the amendments have provided figures to all MLME request/response primitives.”

TGaf has approved resolutions for similar comments 91, 93 and 94 on other MLME clauses, disagreeing with the commenter and rejecting CIDs 91 and 94.

Propose Rejected for CID 116- the protocol exchange figures are not necessary for all SAP interfaces, as such figures may not provide any additional information than the text for implementation of the specification, per discussion in 11-11/1465r2. We propose to delete figure 6-29 and figure 6-30.

| 273 | 23.36 | 6.3.af6.1.4 | What happens if the request is received but there is no established RSNA? | Maybe add a .confirm that can report failure when RSNA is not established. |
| --- | --- | --- | --- | --- |
| 656 | 22.00 | 6.3.af6 | It seems from Figure 6-af2 that a STA sending out CVS doesn’t require acknowledgement from a STA that received it. How does the STA that sends out CVS make sure the CVS is correctly received and doesn’t need to retransmit the CVS? | Clarification |

Discussion

CID 273 asks if there is no RSNA established but the CVS.request is received but the CVS frame is always transmitted after RSNA establishment. CID 656 says that a CVS sending STA needs to know if the CVS receiving STA is correctly received the CVS or not. In order to the transmitter know that the CVS frame reached to the receiver and we propose to add a .confirm primitive for CVS frames.

Propose Revised for CID 273 per discussion and editing instruction in 11-11/1465r2. We propose to add a CVS.confirm primitive.

Propose Accepted for CID 656 per discussion and editing instruction in 11-11/1465r2. We propose to add a CVS.confirm primitive.

| 355 | 23.25 | 6.3.af6.1.2 | Contact Verification Signal element listed as "Valid range" | Specify values of valid range for Contact Verification Signal |
| --- | --- | --- | --- | --- |

Discussion

CID asks to specify values of valid range for Contact Verification Signal and it needs to be specified and it is already fixed in TGaf D1.04.

Propose Accepted for CID 355 per discussion in 11-11/1465r2 and it is already fixed in TGaf D1.04.

| 231 | 65.20 | 10.af.2.2 | The bahaviour if several WSMs with different version numbers are received is not explained / specified. | Insert new paragraph: "If a STA receives several WSMs with different Map versions, the STS shall realize that ist WSM in no longer valid and it should then transmit a Channel Availability Query Request frame, receiving a Channel Availability Query Respnse frame which contains an updated WSM." |
| --- | --- | --- | --- | --- |

Discussion

CID 231 says that text discussing a dependent STA getting more than one WSM with different version numbers is not explained / specified in P802.11af D1.0. Approved resolutions to other comments have changed the text to 10.38.4 White Space Map in P802.11af D1.04. “The value of the Map version bits shall be increased by 1 (modulo 128) whenever the GDC enabling STA transmits the updated WSM. The most recently received WSM shall be used by the WSM receiving STAs.”

Propose Revised for CID 231, per discussion in 11-11/1465r2. 10.38.4 White Space Map in P802.11af D1.04 says “The value of the Map version bits shall be increased by 1 (modulo 128) whenever the GDC enabling STA transmits the updated WSM. The most recently received WSM shall be used by the WSM receiving STAs.”

| 395 | 22.27 | 6.3.af6.1 | Hopefully the function is doing more than blindly sending a frame. | State what transmitting the frame is supposed to accomplish. |
| --- | --- | --- | --- | --- |

Discussion

CID 395 asks that the purpose of signalling be described and we agree.

Propose Accepted for CID 395 per discussion and editing instruction in 11-11/1465r2.

| 396 | 23.33 | 6.3.af6.1.3 | The SME's purpose must be more than just sending a frame. | State what the SME is trying to accomplish by transmitting the frame. |
| --- | --- | --- | --- | --- |
| 397 | 23.39 | 6.3.af6.1.4 | The usual 11mb statement for Effect of Receipt of request to transmits a frame is a bit more general, but also clearer. | Replace the sentence: "The STA then attempts…another STA." with: "This frame is then scheduled for transmission." |

Discussion

CID 396 proposes to state the purpose of SME of CVS and CID 397 asks to replace the sentence as proposed, “This frame is then scheduled for transmission.” We agree.

Propose Accepted for CID 396 and 397 per discussion and editing instructions in 11-11/1465r2.

| 398 | 24.29 | 6.3.af6.2.4 | This is a normative statement about the SME, which is out of scope. In addition, 10.af2.3 doesn't state anything that is clearly a function of the SME. | Replace the whole sentence "On receipt…in 10.af2.3." with "The SME is notified of the receipt of information about whether the regulatory database has been updated." |
| --- | --- | --- | --- | --- |

Discussion

CID 398 says that the specific sentence states normative behaviour of SME but not it is specified. It proposes to change the sentence and we agree. We propose the change the sentence as “the SME is notified of the receipt of Contact Verification Signal.”

Propose Revised for CID 398 per discussion and editing instruction in 11-11/1465r2.

| 657 | 23.33 | 6.3.af6.1.3 | Clarify "Protected", A CVS has to be protected, a NON protected CVS should not exist according to the rules. | Remove Protected, if CVS is always protected |
| --- | --- | --- | --- | --- |

Discussion

CID 657 asks to remove “Protected” because CVS frame needs to be always secure. We agree with the commenter and propose to remove “Protected”.

Propose Accepted for CID 657 per discussion and editing instructions in 11-11/1465r2. Delete “Protected”.

| 655 | 22.00 | 6.3.af6 | Contact verification signal is only transmitted by a mode II device or a fixed device to a mode I device. It cannot be transmitted by a mode I device, Figure 6-af2 doesn’t confine a mode I from sending CVS. | Modify the figure or add wording to confine the usage. |
| --- | --- | --- | --- | --- |

Discussion

CID 655 propose to confine that mode I device cannot transmit CVS and we agree. CVS frames are transmitted by GDC enabling STAs. Peer MAC entity just means a source / destination and specific rules are described in 10.38.5 (Contact Verification Signal). Therefore, no change is required in the figure but we propose to change the first sentence in 6.3.99.1 as “This primitive requests that a (Protected) Contact Verification Signal frame be sent to a peer entity by a STA to a specified peer MAC entity in order to validate a WSM.”

Propose Revised for CID 655 per discussion and editing instruction in 11-11/1465r2.

| 820 | 24.29 | 6.3.af6.2.4 | Remove wishy-washy requirement. | Change “should operate” to “operates”. |
| --- | --- | --- | --- | --- |

Discussion

CID 820 proposes to change “should operate” to “operates” and this is already reflected in TGaf D1.04.

Propose Accepted for CID 820. This is already changed in TGaf D1.04.

| 71 | 65.59 | 10.af.2.2 | "realizes that its WSM is not valid" are STAs self aware? | Change "realizes that its WSM is not valid" to "invalidates its WSM" |
| --- | --- | --- | --- | --- |

Discussion

CID 71 says that STAs does not “realize” but do validate WSM and we agree. In IEEE 802.11 TGaf D1.04, it has already changed to as, “If they are the same, then the GDC dependent STA assumes that its WSM is valid and it sets dot11GDCEnablementValidTimer equal to dot11ContactVerificationSignalInterval.”

Propose Revised CID 71 per discussion in 11-11/1465r2.

| 543/ 612/ 903/ | 64.00 | 10.af.2 | What is a difference between a dot11WhiteSpaceMapValidTime and Validity field in a White Space Map. Provide a clear behavior and interpretation of a validity times. | See forthcoming document 11-11/xxxxr0. |
| --- | --- | --- | --- | --- |

Discussion

CID 543, 612 and 903 ask for clarifying the behaviour of the case that STAs becomes unenabled. CVS signals determine the validity of a WSM and we propose to remove dot11WhiteSpaceMapValidTime and corresponding rules. As the approval of 11-11/1035r2 and 11-11/414r7 in July meeting, the method of maintaining “enabled” state and conditions that a GDC dependent STA becomes “unenabled” are now clear. Therefore, dot11WhiteSpaceMapValidTime is not necessary but the Validity field in a White Space Map indicates how long a specific channel is valid for operation of unlicensed device and the time would be different for each channels. See 11-11/1035r2 and 11-11/414r7 and we propose to remove dot11WhiteSpaceMapValidTime definition and corresponding operation from the draft.

Propose Revised for CID 543, 612 and 903 based on discussion and editing instructions in 11-11/1465r2. See 11-11/1035r2 and 11-11/414r7. We propose to remove dot11WhiteSpaceMapValidTime definition and corresponding operation from the draft.

Editing Instructions

TGaf editor: modify sub-clause 6.3.9.1.4 as follows:

6.3.93.1.4 Effect of Receipt

On receipt of this primitive, the MLME constructs a (Protected) GDC Enablement Request frame. The STA then attempts to transmit this to the peer entity. This frame is then scheduled for transmission.

TGaf editor: modify sub-clause 6.3.93.4.4 as follows:

6.3.93.4.4 Effect of Receipt

On receipt of this primitive, the MLME constructs a GDC Enablement Response frame. The STA then attempts to transmit this to the peer entity. This frame is then scheduled for transmission.

TGaf editor: modify sub-clause 6.3.94.3.4 as follows:

6.3.94.3.4 Effect of Receipt

On receipt of this primitive, the SME operates according to the procedure in 10.38.4 (White space map (WSM)). is notified of the receipt of White Space Map Announcement frame.

TGaf editor: modify sub-clause 6.3.99.1 and 6.3.99.2 as follows:

6.3.99.1 MLME-CVS.request

6.3.99.1.1 Function

This primitive requests that a (Protected) Contact Verification Signal frame be sent to a peer entity by a STA to a specified peer MAC entity in order to validate a WSM.

TGaf editor: Change the first sentence in sub-clause 6.3.99.1.3 as follows:

6.3.99.1.3 When Generated

This primitive is generated by the SME to request that a (Protected) Contact Verification Signal frame be sent to the peer entity by a STA to a specified peer MAC entity.

TGaf editor: Change the first sentence in sub-clause 6.3.99.1.4as follows:

6.3.99.1.4 Effect of Receipt

On receipt of this primitive, the MLME constructs a (Protected) Contact Verification Signal frame. The STA then attempts to transmit this to the peer entity. This frame is then scheduled for transmission.

TGaf editor: Change the sub-clause 6.3.99.2.1as follows:

6.3.99.2.1 Function

This primitive indicates that a (Protected) Contact Verification Signal frame was received from a specific peer MAC entity.

TGaf editor: Change the first sentence in sub-clause 6.3.99.1.4as follows:

6.3.99.2.3 When Generated

This primitive is generated by the MLME when a valid (Protected) Contact Verification Signal frame is received.

TGaf editor: Change the first sentence in sub-clause 6.3.99.1.4as follows:

6.3.99.2.4 Effect of Receipt

On receipt of this primitive, the SME operates according to the procedure in 10.38.5 (Contact verification signal (CVS)). is notified of the receipt of Contact Verification Signal.

TGaf editor: insert sub-clause 6.3.99.3 as follows:

6.3.99.3 MLME-CVS.confirm

6.3.99.3.1 Function

This primitive reports the result of an MLME-CVS.request primitive.

6.3.99.3.2 Semantics of the Service Primitive

The primitive parameters are as follows:

MLME-CVS.confirm (

ResultCode
)

| Name | Type | Valid Range | Description |
| --- | --- | --- | --- |
| ResultCode | Enumeration | SUCCESS, REFUSED, INVALID_PARAMETERS | Indicates the result response to the CVS process. |

6.3.99.3.3 When Generated

This primitive is generated by the MLME as a result of an MLME-CVS.request and indicates the results of the request.

6.3.99.3.4 Effect of Receipt

On receipt of this primitive, the SME evaluates the results of the MLME-CVS.request primitive and may use the reported data.

TGaf editor: insert sub-clause 6.3.99.4as follows:

6.3.99.4 MLME-CVS.response

6.3.99.4.1 Function

This primitive is used to send a response to a specified peer MAC entity that transmitted CVS frame with the STA that issued this primitive.

6.3.99.4.2 Semantics of the service primitive

The primitive parameters are as follows:

MLME-CVS.response (

PeerMACAddress,

ResultCode

)

| Name | Type | Valid range | Description |
| --- | --- | --- | --- |
| PeerMACAddress | MAC Address | Any valid individual MAC address | The address of the peer MAC entity to which the... |
| ResultCode | Enumeration | SUCCESS, | Indicates the result response of the channel availability query from the peer MAC entity. |

6.3.97.4.3 When generated

This primitive is generated by the SME of a STA as a response to an MLME-CVS.indication primitive.

6.3.97.4.4 Effect of receipt

This primitive initiates transmission of a response to the specific peer MAC entity that transmitted a CVS frame.

ASN.1 encoding of the MAC and PHY MIB

C.3 MIB Detail

TGaf editor: Remove the following entry, dot11WhiteSpaceMapValidTime from the dot11StationConfigEntry sequence list in TGaf D1.04:

Dot11StationConfigEntry::=

SEQUENCE {

.

.

.

dot11WhiteSpaceMapValidTime Unsigned32,

.

.

}

TGaf editor: Remove the following element from the dot11StationConfigTable element definitions in TGaf D1.04:

dot11WhiteSpaceMapValidTime OBJECT-TYPE

SYNTAX Unsigned32 (1..65535)

MAX-ACCESS read-write

STATUS current

DESCRIPTION

"This is a control variable.It is written by an external management entity.

Changes take effect for the next MLME-START.request primitive.

This attribute specifies the amount of time in units of seconds that a White Space Map element is valid for a dot11WhiteSpaceMapValidTime from the transmission of thebeacon frame containing WSM element.

”DEFVAL { 600 }

::= { dot11StationConfigEntry <ANA> }

# Text boxes

Abstract

Proposed resolutions to remaining comments in MAC CVS and some comments in MAC WSM:

116, 273, 355,231, 395, 396, 397, 398, 657, 655, 656, 820 543, 612 and 903

Editing instructions are based on P802.11af Draft 1.04.