## Slide 1: Green-Field 11ac Packet for TGah
Date: 2011-11-06
Authors:

## Slide 2: Abstract
In this submission, the 11ac greed field format for IEEE 802.11ah PHY is proposed with the similar approach in 802.11n.

## Slide 3: Backgound
The down-clocked version of 11ac is considered as the most possible candidate for 11ah.
11ah devices operate in sub 1GHz channels. There is no legacy devices like 11a/b/g/n.
Therefore, we do not need to consider the backward compatibility with legacy devices.
Unlike 11n, 11ac considers only mixed mode format with L-STF, L-LTF, L-SIG.
To improve the efficiency, the greed field format should be included for 11ah without considering backward compatibility.
Notes: 그냥 읽으면서 지나감.

## Slide 4: GF format in 11n
11n mixed mode format
11n greenfield format
  Reduced packet overhead
Legacy part

## Slide 5: Frame format in 11ac
The current 11ac packet
L-STF, L-LTF, L-SIG are not needed.
If MU-MIMO is not necessary in 11ah, VHT-SIG B is not needed.
Since the maximum Nsts is 4, we can save one bit in VHT-SIG A.
  With this saved bit and reserved bits, the additional transmission technique for range extension can be indicated.

## Slide 6: GF format for 11ah (1)
GF format
If MU-MIMO is not considered, it is not included.
The bit allocation can be modified.
Max Nsts = 4.
More MSC indication for adopting some range extension technique.

## Slide 7: GF format for 11ah (2)
In most use cases, the packet size may be small.
Therefore, the reduction of pakcet overhead is significant in terms of efficiency.

## Slide 8: Conclusions
In this submission, we consider the GF 11ac frame format for 11ah PHY.
11ah do not consider the backward compatibility.
With GF format, we can improve the system efficiency.

## Slide 9: Straw poll
Do you support that the TGah frame structure is in the form of green field format without consideration of backward compatibility?
Y/N/A : 16 / 0 /32