## Slide 1: Repetition Schemes for TGah
Date: 2011-11-06
Authors:

## Slide 2: Abstract
In this submission, TGah PAR requires 1km coverage. For TGah PHY, the 1/10 down clocked version of Tcac PHY can be considered. To meet the PAR, we may need an additiona feature improving the coverage. To this end, the repeated transmission can be adopted since it is the simplest way to improve the receiver sensivitiy.

## Slide 3: Backgound
The down-clocked version of 11ac is considered as the most possible cadicate for 11ah.
To meet the requirement of 1km coverage, a new feature will be needed.
The repetition is one of the simplest ways to extend the coverage.
We introduce serveral variations of repeated transmission for TGah PHY.
Notes: 그냥 읽으면서 지나감.

## Slide 4: Simple repetition in time domain (1)
Simple repetition of 2MHz Mode (20MHz 11ac + 1/10 down clock)
3dB Power gain

## Slide 5: Simple repetition in time domain (2)
Two repetited OFDM symbols are identical.
  3 different options of CP handling
    CP + OFDM repetition
      Symbol timing strucrue is maintained
    OFDM symbol repetition with sigle CP
      Throughput gain due to reduced CP ( ~11% throughput gain)
    OFDM symbol repeition with extended single CP
      can cover channels with longer delay spread

## Slide 6: Repetition in frequency domain
A QAM modulated symbol is transmitted in two subcarriers in the same OFDM symbol.
3dB Power gain +
freq. diversity gain
Phase rotation can be applied.
Freq. spreading
PAPR reduction [1]

## Slide 7: Permuted repetition in time domain (1)
Two OFDM symbols contain the same information [2].
  By permuting subcarriers, frequency diveristy gain can be obtained.
3dB Power gain +
freq. diversity gain
Phase rotation can be applied.

## Slide 8: Permuted repetition in time domain (2)
With only one OFDM symbol, the receiver can obtain all information in two repeated OFDM symbols.
The receivers, which do not support repetition, can also decode with the first OFDM SIG symbol.
  If repetition is optional, devices with this option can set NAV during the repeated packet by decoding single SIG symbol.

## Slide 9: Conclusions
For coverage extension, we introduce several repetition options.
Each option has its own merit.
This contribution can be background data to select the repetition method.

## Slide 10: References
[1] L. Gariou, “DFT-spread OFDM optimized for 802.11ah,” doc number: 11/0753r0, May 2011.
[2] H. Yu et al., “Coverage extension for IEEE 802.11ah,” doc number: 11/0035r1, Jan. 2011.

## Slide 11: Straw poll
Do you support that TGah includes the repeated transmission modes to support 1km coverage .
Y/N/A :