## Slide 1: GAS Version Control in 11ai
Name | Affiliations | Address | Phone | email
Phillip Barber | Huawei Technologies Co., Ltd. | 1700 Alma Rd, Ste 500 Plano, Texas 75075 USA | +1 972-509-5599 | pbarber@huawei.com
Zongming Yao | Huawei Technologies Co., Ltd. | Bldg C8, Software Park, Road Tianfu 801, Gaoxin District, Chengdu, Sichuan, China, 610041 | +86 28 65972966 | yaozongming@huawei.com
Xuehuan Wang | Huawei Technologies Co., Ltd. | Bldg C8, Software Park, Road Tianfu 801, Gaoxin District, Chengdu, Sichuan, China, 610041 | +86 28 65972965 | wangxuehuan@huawei.com
Date: 2011-10-24
Authors:

## Slide 2: Abstract
This document describes a technical proposal for TGai. In this proposal, some methods for GAS version control will be provided to reduce FILS processing time by potentially eliminating unproductive/redundant GAS/ANQP Request/Response events.

## Slide 3: Conformance w/ Tgai PAR & 5C
Conformance Question | Response
Does the proposal degrade the security offered by Robust Security Network Association (RSNA) already defined in 802.11? | No
Does the proposal change the MAC SAP interface? | No
Does the proposal require or introduce a change to the 802.1 architecture? | No
Does the proposal introduce a change in the channel access mechanism? | No
Does the proposal introduce a change in the PHY? | No
Which of the following link set-up phases is addressed by the proposal? (1) AP Discovery (2) Network Discovery (3) Link (re-)establishment / exchange of security related messages (4) Higher layer aspects, e.g. IP address assignment | 2

## Slide 4: GAS/ANQP
GAS/ANQP protocol introduced in 802.11u is designed for aiding network discovery and selection, enabling information transfer from external networks, enabling emergency services, and interfacing Subscription Service Provider Networks (SSPN) to 802.11 Networks that support Interworking with External Networks.
GAS/ANQP protocol may be used to retrieve locally stored or information remotely available from an AS (Advertisement Server); retrieved information could be Network Authentication Type information, Roaming Consortium list, IP Address Type Availability information, NAI Realm list, 3GPP Cellular Network information, AP Geospatial Location, Domain Name list, Emergency Call Number information, Vendor Specific Information .etc.
STA (especially when in public places like subway, airport, .etc) will use GAS/ANQP to retrieve information from AS for authentication/association, service discovery, .etc.
Notes: 虽然offload不需要做到无缝切换，但尽快地完成切换总是有好处的，因为大量用户同时连接WiFi又很快离开。

## Slide 5: Usual initial link setup example with GAS
When AP doesn’t provide enough
information in beacon or probe response
for STA to associate, STA shall perform
GAS Query to retrieve it from AS. After
that, STA could start association.
Normally, GAS Query will be performed
again even when later STA comes back to
associate with the same AP that it once had
successfully associated with.
No deterministic method for STA to identify that no GAS/ANQP relevant context is unchanged.
Repeat GAS Query with the same AP every
time is a waste of time, especially for those
STAs that want to benefit from FILS!

## Slide 6: Our considerations
The configurations on both AP and AS will rarely change. So when a STA comes back to the same AP later, it is likely that the AP will return exactly the same response to a GAS/ANQP Query as during a previous event. But currently not deterministic; the STA has no a priori method to know that the information is unchanged, so essentially redundant GAS/ANQP Query/Response made.
Based on the two realities above, we propose an optional version control method to eliminate unproductive and redundant GAS/ANQP Query/Response thus reducing processing time during recurring FILS event.
Notes: 虽然offload不需要做到无缝切换，但尽快地完成切换总是有好处的，因为大量用户同时连接WiFi又很快离开。

## Slide 7: Proposed IEs
Configuration change on AP side (e.g., 11u related information or vendor specific information, .etc) or on AS side are tracked as a whole within a single IE. A change in Configuration Change Counter/Version String would indicate a change in one or more values that may be returned in a GAS/ANQP Response:
  IE could be carried by beacon or probe response.
Or
Notes: 虽然offload不需要做到无缝切换，但尽快地完成切换总是有好处的，因为大量用户同时连接WiFi又很快离开。

## Slide 8: STA locally cached AP GAS/ANQP change table
Each record of locally cached AP table could possibly contain:
  AP Identifier (e.g., the AP’s MAC address);
  Configuration Change Counter or Configuration Version String;
  Configurations retrieved from AS by GAS Query procedure;
  Configurations on AP (e.g., 11u related configurations , Vendor Specific configurations, .etc)
  Others
In case of limiting the size of the locally cached AP table, an AP outage scheme could be provided, e.g., based on how often the AP is used or how many times the AP is used so far, .etc.
Number of records in table; size of table; retention period for records are implementation specific
The STA could use retained GAS/ANQP information and associated configuration change counter/string to make implementation specific decision to avoid redundant future GAS/ANQP Request/Response events
Notes: 虽然offload不需要做到无缝切换，但尽快地完成切换总是有好处的，因为大量用户同时连接WiFi又很快离开。

## Slide 9: Possible Protocol Detail

## Slide 10: Key changes to normative text
An information element for encapsulating configuration change counter (or configuration version string) will be defined. Beacon or probe response should carry this IE.

## Slide 11: Questions & Comments

## Slide 12: Remedy Variants
Slide 12
Huawei
Nov 2011

## Slide 13: Proposed IEs (cont.)
Remedy variant#2: Configuration change on AP side (e.g., 11u related information or vendor specific information, .etc) is tracked by one counter/string, while configuration change on AS side is tracked by another counter/string, but the two counters/strings are included by a single IE. This variant is a little bit different than first variant proposal since it could help to identify more details about whether changes happens only on AP side, or only on AS side, or on both AP side and AS side:
  IE could be carried by beacon or probe response.
Or
Notes: 虽然offload不需要做到无缝切换，但尽快地完成切换总是有好处的，因为大量用户同时连接WiFi又很快离开。

## Slide 14: Proposed IEs (cont.)
Configuration change on AP side (e.g., 11u related information or vendor specific information, .etc) is tracked by one counter/string, while configuration change on AS side is tracked by another counter/string, but the two counters/strings are included by separate IEs. This variant is a little bit different than first variant proposal since it could help to identify more details about whether changes happens only on AP side, or only on AS side, or on both AP side and AS side.
  IE could be carried by beacon or probe response.
Or
Notes: 虽然offload不需要做到无缝切换，但尽快地完成切换总是有好处的，因为大量用户同时连接WiFi又很快离开。

## Slide 15: Proposed IEs (cont.)
Remedy variant#3: Configuration change on AP side (e.g., 11u related information or vendor specific information, .etc) or on AS side are tracked separately within a single IE. A change in Configuration Change CounterN/Version StringN would indicate a change in one or more values that may be returned in a GAS/ANQP Response. Specific mapping of GAS/ANQP Info ID elements to CounterN/StringN elements required. This variant is a bit heavier than first variant proposal:
  IE could be carried by beacon or probe response.
Or
Notes: 虽然offload不需要做到无缝切换，但尽快地完成切换总是有好处的，因为大量用户同时连接WiFi又很快离开。

## Slide 16: Proposed IEs (cont.)
Configuration change on AP side (e.g., 11u related information or vendor specific information, .etc) or on AS side are tracked separately within separate IEs. A change in Configuration Change CounterN/Version StringN would indicate a change in one or more values that may be returned in a GAS/ANQP Response. Specific mapping of GAS/ANQP Info ID elements to CounterN/StringN elements required. This variant is a bit heavier than first variant proposal :
  IE could be carried by beacon or probe response.
Or
Notes: 虽然offload不需要做到无缝切换，但尽快地完成切换总是有好处的，因为大量用户同时连接WiFi又很快离开。