## Slide 1: MAC considerations for 802.11ah (Probe and Pull MAC)
Date: 2011-11-07
Authors:

## Slide 2: Abstract
DCF gives no guarantees for media access
  Not suitable for event-driven applications with real-time/deterministic requirements (Use Cases 1c: Environment monitoring., 1d: Industry process automation, 1f: Healthcare, 1g: Home/Building Automation) [1]
  Unfair [3,4] and inefficient [2, 3] in terms of throughput and energy when large numbers of STAs contend for media access at the same time
Contention-Free MAC should be considered for deterministic media access in 802.11ah
  As a reference, 802.15.4e offers three contention-free MACs
802.11 PCF/HCCA is contention free but not suitable for large networks (up to 6000 STAs in 802.11ah)
This presentation introduces the contention-free Probe and Pull MAC (PP-MAC), an alternative to PCF

## Slide 3: 802.11 Contention Free MAC: PCF/HCCA
Benefits of contention-free MAC such as PCF/HCCA
  Deterministic and fair
  Efficient for both low duty-cycle and heavy/bursty traffic
    Higher reliability and lower deployment cost
  No hidden terminal problem
  Energy efficient

## Slide 4: PCF/HCCA is not suitable for large networks
Example: 802.11ah with 2MHz bandwidth, 6000 STAs
  26 data bits/OFDM Symbol (BPSK 1/2), 40µs symbol duration
  SIFS=160µs, PIFS=208µs
  CF-Poll/-ACK message (28 bytes)  8.6 symbols (344 µs)
  Data (250 bytes)=3076µs + PLCP(400 µs) + MAC Header(344µs)
  If X% nodes have 1 uplink data packet, total time to collect all uplink data is approximately: 6000 * (1- X) * (CF-POLL + PIFS) + 6000 * X * (CF-POLL-ACK + SIFS + Data + SIFS)
Collect data from 6000 stations | X = 0% | X = 1% | X = 10% | X = 100%
Time (seconds) | 3.318 | 3.554 | 5.678 | 26.92
Overhead |  | 94.8% | 67.48% | 31.41%

## Slide 5: Probe and Pull MAC (PP-MAC)
Partition STAs into groups
Send Probe to a group of STAs
STAs with data to send will ACK (P-ACK) concurrently (in time-aligned manner)
AP resolves parallel ACKs with the use of Zadoff-Chu sequences [5]
AP initiates and schedules data transmissions with PULL
SIFS
Probe
AP
STA1
P-ACK
STA2
STA3
STA4
P-ACK
Pull
SIFS
have data to send
have data to send
Data
SIFS
SIFS
ACK
Data
SIFS
ACK
SIFS

## Slide 6: Overview of Parallel ACKs (P-ACKs) [5]
PART 1 | PART 2 | … | PART 8
ZC sequence for STA1
…
P-ACK
P-ACK
PART 1 | PART 2 | … | PART 8
STA1
STA2
ZC sequence for STA2
CP | part 1
CP | part 1
(a)
(b)
CP | part 8
CP | part 8
(a)
(b)
(a)
(b)
…
(a) Map a part of ZC sequence
to OFDM subcarriers
(b) IFFT and add cyclic prefix (CP)
P-ACK_STA1
P-ACK_STA2
Parallel ACKs to AP

## Slide 7: Parallel ACKs Detection Accuracy [5]

## Slide 8: PP-MAC Performance
PROBE: 28+2bytes (369µs), P-ACK: 8 symbols (352µs)
PULL:28+20bytes (590µs) to pull up to 32 STAs at the same time
  If group size is Y, and X% nodes have 1 uplink data (250bytes) packet, total time to collect all uplink data is approximately:
  6000/Y*
Collect Data from 6000 stations | X = 0% Y=32 | X = 1% Y=32 | X = 10% Y=32 | X = 100% Y=32
Time (seconds) | 0.108 | 0.509 | 2.756 | 25.22
Gain over PCF | 96.73% | 85.66% | 51.45% | 6.28%
Overhead |  | 63.76% | 33.01% | 26.81%
Gain Over PCF |  | 32.74% | 51.07% | 14.65%

## Slide 9: Throughput comparison (PER=1%)
The probability that a node
has data to transmit is 90%
The probability that a node
has data to transmit is 10%

## Slide 10: Conclusion
Based on the concept of parallel ACK, PP-MAC is a more efficient alternative to PCF for 802.11ah

## Slide 11: References
[1] 11-11-0457-00-00ah: potential-compromise-of-802-11ah-use-case-document
[2] 11-11-1248-00-00ah: Simulation Study of the Performance of DCF Under Heavy Traffics for 802.11ah
[3] 11-11-1019-01-00ah: simulation-large-number-of-stas-support
[4] 11-11-1511-00-00ah: Fairness of DCF
[5]

## Slide 12: Straw-poll 1
The specification framework should include a contention free MAC mechanism.
Y/N/A

## Slide 13: Straw-poll 2
The specification framework should include a mechanism to group STAs.
Y/N/A

## Slide 14: Straw-poll 3
The specification framework should include a mechanism to probe a group of STAs.
Y/N/A

## Slide 15: Straw-poll 4
The specification framework should include a mechanism to receive traffic indications from a group of STAs in parallel.
Y/N/A

## Slide 16: Motion 1
The specification framework should include a contention free MAC mechanism.
Y/N/A

## Slide 17: Motion 2
The specification framework should include a mechanism to group STAs.
Y/N/A

## Slide 18: Motion 3
The specification framework should include a mechanism to probe a group of STAs.
Y/N/A

## Slide 19: Motion 4
The specification framework should include a mechanism to receive traffic indications from a group of STAs in parallel.
Y/N/A