IEEE P802.11
Wireless LANs

| Resolutions for Highest Supported Data Rate CIDs |
| --- |
| Date: 2011-12-13 |
| Author(s): |
| Name | Affiliation | Address | Phone | email |
| Mark RISON | CSR | CB4 0WZ, U.K. | +44 1223 692000 | Mark.RISON@csr.com |

## Revision History

r0: Initial revision.

r1: Updated following presentation of r0 in Atlanta.

r2: Updated following presentation of r1 in Atlanta; split into three parts: just narrow focus on the letter of the comments, VHT changes, HT changes.

r3: Updated following presentation of r2 in Atlanta.

r4: Updated following presentation of r3 in Atlanta and post-Atlanta discussions.

r5: Updated following presentation of r4 in teleconference and discussion with Accord.

## Comments

| 3345 | Rosdahl, Jon | 54.33, 54.48 | Wording is inconsistent | Delete the "Set to the highest supported data rate" |
| --- | --- | --- | --- | --- |
| 2855 | Lindskog, Erik | As 3345 | As 3345 | As 3345 |
| 3253 | Reuss, Edward | 54.37 | For Rx Supported Data Rate, it says "If the maximum data rate expressed in Mb/s is not an integer, then the value is rounded up to the next integer." This could potentially lead to a STA advertising support for a data rate that is higher than it can actually support. I think this should read "rounded down to the next integer". (I believe that for the Tx Highest Supported Data Rate that it it is safe to leave it as "rounded up", as this won't cause any problems. | Change "rounded up" to "rounded down". |
| 3798 | Reuss, Edward | As 3253 | As 3253 | As 3253 |

## Discussion

Investigation of these comments has exposed spec holes.

The use to which the information passed in the Tx Highest Supported Data Rate and Rx Highest Supported Data Rate subfields of the VHT Supported MCS Set field of the VHT Capabilities element is put is not defined.  The only statement referring to this is in subclause 22.5 (my emphasis):

A VHT STA shall support single spatial stream MCSs within the range MCS 0 through MCS 7 for all channel widths for which it has indicated support regardless of the Tx or Rx Highest Supported Data Rate sub-field values in the VHT Supported MCS Set field. When more than one spatial stream is supported, the Tx or Rx Highest Supported Data Rate sub-field values in the VHT Supported MCS Set field may result in a reduced MCS range (cut-off) for greater than one spatial stream. Support for 20 MHz, 40 MHz and 80 MHz with NSS=1 is mandatory. Support for 20 MHz, 40 MHz and 80 MHz with NSS=2..8 is optional. Support for 160 MHz and 80+80 MHz with NSS=1..8 is optional.

The 802.11 specification has somewhat more information on the similar HT fields (my emphasis):

[Subclause 8.4.2.58.4 Supported MCS Set field:]

The Rx Highest Supported Data Rate subfield of the Supported MCS Set field defines the highest data rate that the STA is able to receive, in units of 1 Mb/s, where 1 represents 1 Mb/s, and incrementing by 1 Mb/s steps to the value 1023, which represents 1023 Mb/s. If the maximum data rate expressed in Mb/s is not an integer, then the value is rounded up to the next integer. The value 0 indicates that this subfield does not specify the highest data rate that the STA is able to receive; see 9.7.6.5.3.

[Subclause 8.4.2.58.6 Transmit Beamforming Capabilities:]

NOTE—The maximum number of space-time streams for which channel coefficients can be simultaneously estimated using the HT-LTFs corresponding to the data portion of the packet is limited by the Rx MCS Bitmask subfield of the Supported MCS Set field and by the Rx STBC subfield of the HT Capabilities Info field. Both fields are part of the HT Capabilities element.

[Subclause 9.7.6.5.3 Control response frame MCS computation:]

The Rx Supported MCS Set of the STA that transmitted the frame eliciting the response is determined from its Supported MCS Set field as follows:

— If a bit in the Rx MCS Bitmask subfield is equal to 0, the corresponding MCS is not supported.

— If a bit in the Rx MCS Bitmask subfield is equal to 1 and the integer part of the data rate (expressed in megabits per second) of the corresponding MCS is less than or equal to the rate represented by the Rx Highest Supported Data Rate subfield, then the MCS is supported by the STA on receive. If the Rx Highest Supported Data Rate subfield is equal to 0 and a bit in the Rx MCS Bitmask is equal to 1, then the corresponding MCS is supported by the STA on receive.

[Subclause 9.27 Sounding PPDUs:]

NOTE—The maximum number of space-time streams for which channel coefficients can be simultaneously estimated using the HT-LTFs corresponding to the data portion of the packet is limited by the Rx MCS Bitmask subfield of the Supported MCS Set field and by the Rx STBC subfield of the HT Capabilities Info field. Both fields are part of the HT Capabilities element.

[Subclause 9.28.2 Link adaptation using the HT Control field:]

NOTE—The MFB requester can advertise the maximum number of spatial streams that it can transmit in its HT Capabilities element. In order to do so, the MFB requester sets the Tx MCS Set Defined bit of the Supported MCS Set field to 1 and indicates the maximum number of streams in the Tx Maximum Number Spatial Streams Supported subfield of the Supported MCS Set field. If the Tx Rx MCS Set Not Equal bit is equal to 0, the Tx MCS set is equal to the Rx MCS set, and the maximum number of transmit spatial streams is derived from the value of this field.

When computing the MCS estimate for an MFB requester whose Tx MCS Set Defined field is equal to 1, the number of spatial streams corresponding to the recommended MCS shall not exceed the limit indicated by the Tx Maximum Number Spatial Streams Supported field. The MFB responder shall not recommend an MCS corresponding to UEQM unless the MFB requester supports such modulation, as indicated by the Tx Unequal Modulation Supported bit in the Supported MCS Set field.

[Subclause 9.29.2.4.3 Sounding exchange for calibration:]

If the sounding PPDU is not an NDP, the number of antennas used by the sender shall be less than or equal to the maximum number of space-time streams indicated by the Rx MCS Bitmask subfield of the Supported MCS Set field and the Rx STBC subfield of the HT Capabilities element transmitted by the intended receiver.

[Subclause 9.30.2 [Antenna selection] Procedure:]

If the sounding PPDU is not an NDP, the number of antennas used by the sender, as indicated by the ANTENNA_SET parameter in the TXVECTOR, shall be less than or equal to the maximum number of space-time streams indicated by the Rx MCS Bitmask subfield of the Supported MCS Set field and the Rx STBC subfield of the HT Capabilities element transmitted by the intended receiver.

Note HT does not have a Tx Highest Supported Data Rate subfield (it has Tx MCS Set Defined, Tx Rx MCS Set Not Equal, Tx Maximum Number Spatial Streams Supported and Tx Unequal Modulation Supported subfields).

The above analysis leads to the conclusion that:

- The Tx Highest Supported Data Rate subfield of the VHT Supported MCS Set field of the VHT Capabilities element is used for link adaptation but this needs specifying

- The Rx Highest Supported Data Rate subfield of the VHT Supported MCS Set field of the VHT Capabilities element is used for rate selection but this needs specifying

- We should support a special value 0 for Tx/Rx Highest Supported Data Rate

## Proposed changes w.r.t. D1.3

The changes are shown using Word change tracking. Select “Final Showing Markup” or “Final” as appropriate.  Editorial instructions are shown using bold italics.

The proposal is split into three change sets, which build upon each other.

### Change set #1 (narrow focus on the letter of the comments)

Modify existing text as follows:

8.4.2.58.4 Supported MCS Set field

The Rx Highest Supported Data Rate subfield of the Supported MCS Set field defines the highest data rate that the STA is able to receive, in units of 1 Mb/s, where 1 represents 1 Mb/s, and incrementing by 1 Mb/s steps to the value 1023, which represents 1023 Mb/s. If the maximum data rate expressed in Mb/s is not an integer, then the value is rounded down to the next integer. The value 0 indicates that this subfield does not specify the highest data rate that the STA is able to receive; see 9.7.6.5.3.

8.4.2.140.3 VHT Supported MCS Set field

| Rx Highest Supported Data Rate | Indicates the maximum data rate that the STA can receive. | In units of 1 Mb/s. If the maximum data rate expressed in Mb/s is not an integer, then the value is rounded down to the next integer. |
| --- | --- | --- |
| […] |  |  |
| Tx Highest Supported Data Rate | Indicates the maximum data rate that the STA will transmit. | In units of 1 Mb/s. If the maximum data rate expressed in Mb/s is not an integer, then the value is rounded down to the next integer. |

### Change set #2 (VHT changes)

Add a new subclause in 9.7:

9.7.x Rate selection constraints for VHT STAs

9.7.x.1 VHT Rx Supported MCS Set

The VHT Rx Supported MCS Set of a VHT STA is determined for each MCS, number of spatial streams n = 1, …, 8 and bandwidth (20 MHz, 40 MHz, 80 MHz and 160 or 80+80 MHz) from its VHT Supported MCS Set field as follows:

— If the Max MCS For n SS subfield in the Rx MCS Map subfield indicates support and the integer part of the data rate (expressed in megabits per second) for long GI of the MCS for n SS at that bandwidth is less than or equal to the rate represented by the Rx Highest Supported Long GI Data Rate subfield, then the MCS for n SS at that bandwidth is supported by the STA on receive.

— If the Max MCS For n SS subfield in the Rx MCS Map subfield indicates support and the Rx Highest Supported Long GI Data Rate subfield is equal to 0, then the MCS for n SS at that bandwidth is supported by the STA on receive.

— If support for the MCS for n SS at that bandwidth is mandatory (see 22.5), then the MCS for n SS at that bandwidth is supported by the STA on receive.

— Otherwise the MCS for n SS at that bandwidth is not supported by the STA on receive.

A VHT STA shall not, unless explicitly stated otherwise, transmit a VHT PPDU unless the MCS, number of spatial streams and bandwidth used are in the VHT Rx Supported MCS Set of the receiving STA(s).

NOTE—Support for a MCS for a given number of spatial streams at a given bandwidth implies support for both long GI and short GI on receive, if short GI is supported at that bandwidth.

9.7.x.2 VHT Tx Supported MCS Set

The VHT Tx Supported MCS Set of a VHT STA is determined for each MCS, number of spatial streams n = 1, …, 8 and bandwidth (20 MHz, 40 MHz, 80 MHz and 160 or 80+80 MHz) from its VHT Supported MCS Set field as follows:

— If the Max MCS For n SS subfield in the Tx MCS Map subfield indicates support and the integer part of the data rate (expressed in megabits per second) for long GI of the MCS for n SS at that bandwidth is less than or equal to the rate represented by the Tx Highest Supported Long GI Data Rate subfield, then the MCS for n SS at that bandwidth is supported by the STA on transmit.

— If the Max MCS For n SS subfield in the Tx MCS Map subfield indicates support and the Tx Highest Supported Long GI Data Rate subfield is equal to 0, then the MCS for n SS at that bandwidth is supported by the STA on transmit.

— If support for the MCS for n SS at that bandwidth is mandatory (see 22.5), then the MCS for n SS at that bandwidth is supported by the STA on transmit.

— Otherwise the MCS for n SS at that bandwidth is not supported by the STA on transmit.

NOTE—Support for short GI on transmit cannot be determined.

Modify existing text as follows:

8.4.2.58.4 Supported MCS Set field

The Rx Highest Supported Data Rate subfield of the Supported MCS Set field defines the highest HT PPDU data rate that the STA is able to receive, in units of 1 Mb/s, where 1 represents 1 Mb/s, and incrementing by 1 Mb/s steps to the value 1023, which represents 1023 Mb/s. If the maximum data rate expressed in Mb/s is not an integer, then the value is rounded down to the next integer. The value 0 indicates that this subfield does not specify the highest HT PPDU data rate that the STA is able to receive; see 9.7.6.5.3.

8.4.2.140.3 VHT Supported MCS Set field

Change Figure 8-401by as follows:

| Rx MCS Map | Rx Highest Supported Long GI Data Rate | Reserved | Tx MCS Map | Tx Highest Supported Long GI Data Rate | Reserved |
| --- | --- | --- | --- | --- | --- |

Change Table 8-183z as follows:

| Rx Highest Supported Long GI Data Rate | Indicates the highest long GI VHT PPDU data rate that the STA is able to receive. | In units of 1 Mb/s; see 9.7.x.1. The value 0 indicates that this subfield does not specify the highest long GI VHT PPDU data rate that the STA is able to receive. |
| --- | --- | --- |
| […] |  |  |
| Tx Highest Supported Long GI Data Rate | Indicates the highest long GI VHT PPDU data rate that the STA is able to transmit at. | In units of 1 Mb/s; see 9.7.x.2. The value 0 indicates that this subfield does not specify the highest long GI VHT PPDU data rate that the STA is able to transmit at. |

9.28.3 Link adaptation using the VHT variant HT Control field

[…]

The MFB requester may set the MRQ field to 1 in the VHT variant HT Control field of a frame to request a STA to provide MCS, N_STS and SNR feedback.

[…]

When computing the MFB estimate for an MFB requester, the MCS, N_STS and, for unsolicited MFB, BW field values in the MFB subfield from the MFB responder shall indicate a combination which is in the responder’s VHT Rx Supported MCS Set (see 9.7.x.1) and the requester’s VHT Tx Supported MCS Set (see 9.7.x.2), where the BW for solicited MFB is that defined in 9.28.3.

[…]

22.5 Parameters for VHT MCSs

A VHT STA shall support single spatial stream MCSs within the range MCS 0 through MCS 7 for all channel widths for which it has indicated support regardless of the Tx or Rx Highest Supported Long GI Data Rate sub-field values in the VHT Supported MCS Set field. When more than one spatial stream is supported, the Tx or Rx Highest Supported Long GI Data Rate sub-field values in the VHT Supported MCS Set field may result in a reduced MCS range (cut-off) for NSS=2..8. Support for 20 MHz, 40 MHz and 80 MHz with NSS=1 is mandatory. Support for 20 MHz, 40 MHz and 80 MHz with NSS=2..8 is optional. Support for 160 MHz and 80+80 MHz with NSS=1..8 is optional.

C.3 MIB Detail

dot11RMNeighborReportHTRxHighestSupportedDataRate OBJECT-TYPE

SYNTAX Unsigned32

MAX-ACCESS read-create

STATUS current

DESCRIPTION

"This is a status variable.

It is written by the SME when a measurement report is completed.

The HT Highest Supported Data Rate is a 10 bit subfield that

defines the highest HT PPDU data rate that the STA is able to

receive, in units of 1 Mb/s, where 1 represents 1 Mb/s, and

incrementing by 1 Mb/s steps to the value 1023, which represents

1023 Mb/s. See 8.4.2.58.4"

::= { dot11RMNeighborReportEntry 40 }

Other changes

“x through y” should be “x to y” throughout.

“Nss” should be “NSS” at 38.13, 54.58 (or maybe it should be “sending Rx Nss”?), 66.47, 123.55, 123.56, 279-280 (18 times).

“VHT Control” should be “VHT variant HT Control”.

### Change set #3 (HT changes)

Add a new subclause in 9.7.x:

9.7.x.1 HT Rx Supported MCS Set

The HT Rx Supported MCS Set of an HT STA is determined for each MCS and bandwidth (20 MHz and 40 MHz) from its HT Supported MCS Set field as follows:

— If the corresponding bit in the Rx MCS Bitmask subfield is equal to 1 and the integer part of the data rate (expressed in megabits per second) for long GI of the MCS at that bandwidth is less than or equal to the rate represented by the Rx Highest Supported Long GI Data Rate subfield, then the MCS at that bandwidth is supported by the STA on receive.

— If the corresponding bit in the Rx MCS Bitmask is equal to 1 and the Rx Highest Supported Long GI Data Rate subfield is equal to 0, then the MCS at that bandwidth is supported by the STA on receive.

— If support for the MCS at that bandwidth is mandatory (see 20.6), then the MCS at that bandwidth is supported by the STA on receive.

— Otherwise the MCS at that bandwidth is not supported by the STA on receive.

An HT STA shall not, unless explicitly stated otherwise, transmit an HT PPDU unless the MCS and bandwidth used are in the HT Rx Supported MCS Set of the receiving STA(s).

NOTE—Support for a MCS at a given bandwidth implies support for both long GI and short GI on receive, if short GI is supported at that bandwidth.

Modify existing text as follows:

Change references to the field name as follows throughout the baseline document (21 instances in mb/D12.0; some are included in the explicit changes shown here): HT Supported MCS Set

8.4.2.58.4 HT Supported MCS Set field

In Figure 8-251 change the third cell as follows: Rx Highest Supported Long GI Data Rate

[…]

The Rx Highest Supported Long GI Data Rate subfield of the HT Supported MCS Set field indicates the highest long GI HT PPDU data rate that the STA is able to receive, in units of 1 Mb/s. The value 0 indicates that this subfield does not specify the highest long GI HT PPDU data rate that the STA is able to receive; see 9.7.x.1.

8.4.2.140.3 VHT Supported MCS Set field

Change Table 8-183z as follows:

| Rx Highest Supported Long GI Data Rate | Indicates the highest long GI VHT PPDU data rate that the STA is able to receive. | In units of 1 Mb/s; see 9.7.x.2. The value 0 indicates that this subfield does not specify the highest long GI VHT PPDU data rate that the STA is able to receive. |
| --- | --- | --- |
| […] |  |  |
| Tx Highest Supported Long GI Data Rate | Indicates the highest long GI VHT PPDU data rate that the STA is able to transmit at. | In units of 1 Mb/s; see 9.7.x.3. The value 0 indicates that this subfield does not specify the highest long GI VHT PPDU data rate that the STA is able to transmit at. |

9.7.6.5.3 Control response frame MCS computation

[…]

<deletion>

[…]

— If the frame eliciting the response had an L-SIG duration value (see 9.23.5) and initiates a TXOP, the CandidateMCSSet is the MCS Set consisting of the intersection of the HT Rx Supported MCS Set (see 9.7.x.1) of the STA that sent the frame that is eliciting the response and the set of MCSs that the responding STA is capable of transmitting.

[…]

9.7.x Rate selection constraints for HT STAs

9.7.x.2 VHT Rx Supported MCS Set

9.7.x.3 VHT Tx Supported MCS Set

9.28.3 Link adaptation using the VHT variant HT Control field

When computing the MFB estimate for an MFB requester, the MCS, N_STS and, for unsolicited MFB, BW field values in the MFB subfield from the MFB responder shall not indicate a combination which is not in the responder’s VHT Rx Supported MCS Set (see 9.7.x.2) and the requester’s VHT Tx Supported MCS Set (see 9.7.x.3), where the BW for solicited MFB is that defined in 9.28.3.

C.3 MIB Detail

dot11RMNeighborReportHTRxHighestSupportedLongGIDataRate OBJECT-TYPE

SYNTAX Unsigned32

MAX-ACCESS read-create

STATUS current

DESCRIPTION

"This is a status variable.

It is written by the SME when a measurement report is completed.

The HT Rx Highest Supported Long GI Data Rate is a 10 bit subfield

that indicates the highest long GI HT PPDU data rate that the STA

is able to receive, in units of 1 Mb/s. See 8.4.2.58.4"

::= { dot11RMNeighborReportEntry 40 }

## Resolution

AGREE IN PRINCIPLE.  See Proposed changes in 1518r5.

# Comments

Note this was not in 11n-2009: it was recently added by TGmb to try to align 11mb with 11ac/D1.0

SGI or LGI? 20 MHz or 40 MHz?

Agreed to in Atlanta, i.e. passed motion in TG and incorporated in D1.4

e.g. 9.31.6 Transmission of a VHT NDP: “The NUM_STS parameter may be set to any value, subject to the constraint of the previous sentence, regardless of the value of the Supported MCS Set field of the VHT Capabilities field at either the transmitter or recipient of the NDP.”

The rounding behaviour is now specified there (“the integer part of the data rate […] is less than or equal to the rate represented by the Rx Highest Supported Data Rate subfield”)

Ditto

These are desirable for consistency

# Text boxes

Abstract

This document proposes a resolution for CIDs 2855, 3253, 3345 and 3798 on P802.11ac/D1.0, regarding Tx/Rx Highest Supported Data Rate.