## Slide 1: AP and Network Discovery Enhancements
Date: 2011-11-09
Authors:

## Slide 2: Abstract
The presentation summarizes feedback received during September and November 2011 TGai session wrt. improving passive and active scanning.
It identifies parts in the 802.11 standard that need to be changed in order to incorporate discussed solutions.
This presentation addresses schemes for
AP discovery / scanning

## Slide 3: Passive Scanning
Issue identified in SG Phase:
  Scan through all available channels
  STA “shall listen to each channel scanned for no longer than a maximum duration defined by the MaxChannelTime“
Technical approach discussed in Sept.
  Scanning procedure should be capable to report each found AP immediately
  Means to abort ongoing scanning procedure
Intended changes to 802.11:
  MLME-scan.request:
    Add parameter indicating that a mlme-scan.response shall be created every X ms, containing the results of the scanning process for the last reporting interval.
  MLME-scan.response:
    Add a new parameter indicating if the response is the final response of a scanning process or if it reports an “intermediate results” for the last reporting period
  MLME-scanAbort.request:
    New method aborting the ongoing scanning
No impact on frames exchanged between STA & AP

## Slide 4: Active Scanning
Issued identified during SG phase:
  Active scanning may immediately find an appropriate AP but does not immediately return
  “…. [scan until] ProbeTimer reaches MaxChannelTime, process all received probe responses“
Technical approach discussed in Sept.
  Scanning procedure should be capable to report each found AP immediately
  Means to abort ongoing scanning procedure
Intended changes to 802.11:
  MLME-scan.request:
    Add parameter indicating that a mlme-scan.response shall be created every X ms, containing the results of the scanning process for the last reporting interval.
  MLME-scan.response:
    Add a new parameter indicating if the response is the final response of a scanning process or if it reports an “intermediate results” for the last reporting period
  MLME-scanAbort.request:
    New method aborting the ongoing scanning
No impact on frames exchanged between STA & AP

## Slide 5: Straw Poll
Do you support changing the mlme-scan methods
  to allow for requesting “period reporting” on discoverd STAs (as opposed to a combined reporting we have today)
  Adding a mlme method resulting in aborting ongoing scanning
Result:
  Yes ;
  No ;
  Need more information: ;
  Abstain ;

## Slide 6: Active Scan for Multiband Operation
Issue identified in SG Phase:
  passive scanning in 5GHz takes too long
Technical approach discussed in Nov. (also along with REG SC)
  Enablement via an “out of band channel” not permitted per regulation
  Well within regulation to start scanning in 2.4 GHz channel and receive in 2.4GHz information on the “timing when the enabling signal will be transmitted in 5GHz”.
Intended changes to 802.11:
  Mlme-scan request: add parameter indicating that the information on multi-channel operation is requested
  Probe request: indicate that STA requests information from AP on multichannel operation
  Probe response:
    include list of channels the AP operates on
    Include information when the AP will send a Beacon (or similar frame) on the other channels its operates on
  Require the AP to send a beacon (or similar frame) within xx ms on all other channels it operates on.  One response on a different channel should be
  QUESTION: two modes of operation: send beacon on other channel within xx vs. just tell when the next regular beacon comes
Compliant to regulation as we do not emit energy on other channel before we receive an enabling signal (passive listening to beacon / other frame)
Backward compatibility: non-TGai-AP may just respond with existing probe response

## Slide 7: Straw Poll
Do you support adding a mechanisms expediting the process of detecting multi-band-operated APs?
Result:
  Yes:
  No:
  Abstain: