## Slide 1: Fast Authentication in TGai
Name | Affiliations | Address | Phone | email
George Cherian Santosh Abraham Hemanth Sampath | Qualcomm | 5775 Morehouse Dr, San Diego, CA, USA | +1 (858)-651-6645 +1 (858)-651-6107 +1(858)-658-1848 | gcherian@qualcomm.com sabraham@qualcomm.com hsampath@qualcomm.com
Jouni Malinen | Qualcomm | Hermiankatu 6-8 D Tampere, Finland |  | jouni@qca.qualcomm.com
Date: 2011-11-07
Authors:

## Slide 2: Abstract
This document proposes indications for IP address types and assignment methods

## Slide 3: Conformance w/ TGai PAR & 5C
Conformance Question | Response
Does the proposal degrade the security offered by Robust Security Network Association (RSNA) already defined in 802.11? | No
Does the proposal change the MAC SAP interface? | No
Does the proposal require or introduce a change to the 802.1 architecture? | No
Does the proposal introduce a change in the channel access mechanism? | No
Does the proposal introduce a change in the PHY? | No
Which of the following link set-up phases is addressed by the proposal? (1) AP Discovery (2) Network Discovery (3) Link (re-)establishment / exchange of security related messages (4) Higher layer aspects, e.g. IP address assignment | 3, 4

## Slide 4: Background
Previous contributions such as 11/1160r3 to 11ai for FILS feature proposed concurrent authentication and IP address assignment procedure:
  Single pair of messages of authentication
  Use of Beacon/ProbeResp to send Anonce
  Use of Association Req/Resp to send ULI
IP address assignment method chosen and IP address assignment type may vary based on different deployments
  STA may choose to encrypt IP address assignment request
  IP address assignment response is encrypted
We propose to indicate the IP address type and assignment methods supported by Access Point using Beacon/Probe Response
  Allows different IP address assignment methods for FILS
  See 1160r3 for call flow on how DHCP & RS/RA may be used for IP address assignment as an illustrative examples

## Slide 5: Proposal
Add two information elements to Beacon and Probe-Response frames
  IP address type Supported:
    IPv4, IPv6, IPv4v6
  IP address method supported:
    DHCP
    DHCPv6
    RS/RA for IPv6
    [more may be added]
An FILS AP will include the above information elements in Beacon/Probe Response