IEEE P802.11 								Wireless LANs

| D1.0 Comment Resolution – CID 2551 |
| --- |
| Date: 2011-11-7 |
| Author(s): |
| Name | Affiliation | Address | Phone | email |
| Reza Hedayat | Cisco Systems | 2200 E. G. Bush Turnpike, Richardson, TX 75082, USA |  | rehedaya at cisco dot com |

Baseline documents: 11ac D1.2

The document proposes resolutions for the following CIDs:

MAC: 	2551.

| CID 2551 Hunter, David 178 1 3.2 2 T Y 2.56 This definition just says the concept is not associated with the EDCAF. We need a bit more information on what it does, as opposed to what it does not do. Add information about what the secondary AC does, or is used for. MAC | Agree in Principle. See Doc 1534. |  |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

Proposed resolution: Agree in principle.

TGac Editor: Please apply the following changes:

3.2 Definitions specific to IEEE 802.11

secondary access category (secondary AC): an access category (AC) that is not associated with the enhanced

distributed channel access function (EDCAF) that gains channel access. Traffic associated with the secondary AC can be included in an MU PPDU that includes traffic associated with the primary AC. There could be multiple secondary ACs at a given time.