## Slide 1: Beam forming for 11ah
Date: 2011-12-12
Authors:

## Slide 2: Abstract
This submission proposes beamforming technique for coverage extension in TGah.

## Slide 3: Coverage extension in 802.11ah
Coverage extension is one of key requirements 802.11ah needs to achieve
  Coverage extension is highly needed in most of 802.11ah applications
    Smart Grid, Sensor networks which covers over 1km x 1km area
    Extended range Wi-Fi as well
  802.11ah FR-EM specifies the requirement up to 1km with a data rate over 100kbps at PHY SAP
But, coverage extension is not an easy one to achieve in 802.11ah
  Coverage is mainly limited by uplink range because many STAs are likely to be power saving single antenna devices
  Coverage is additionally limited by transmit power regulations across many countries
It is needed to exploit all the possible techniques to extend the coverage
  Repetition : already introduced for 802.11ah preamble design
  Beamforming, STBC et al.

## Slide 4: Beamforming
Beamforming technique enables
  Enhanced throughput for the same distance
    Specifically, quasi-ML detection performance can be achieved with quite reduced receiver complexity by introducing beamforming
  Coverage extension (it is more important feature in 802.11ah)
    By focusing transmitting energy on specific direction, signals can be transmitted much farther than not-beamformed transmission
Beamforming in 802.11
  In 802.11ac (or 11n)
    Main focus is on enhancing throughput at high SNRs rather than coverage extension
  In 802.11ad
    Due to 60GHz band characteristics, coverage extension is highly important in 802.11ad. Analog beamforming is used. But, 802.11ad puts up with CSMA/CA-based problems including hidden node things, because it may be in some sense beneficial in terms of spatial re-use (which could not be neglected in high resolution beam cases such 60GHz)
    802.11ad seems to prefer its another MAC architecture (TDMA MAC) when coverage extension is really important to take into consideration

## Slide 5: Beamforming in 11ac (or 11n)
Sounding protocol will be done before actual beamformed data transmission not only for channel sounding but for preventing hidden node problems
  Sounding protocol
    (RTS/CTS exchange),
    NDPA (NDP Announcement), NDP (Null Data Packet)
    VHT CB (Compressed Beamforming Report Feedback)

## Slide 6: Beamforming in 11ac (or 11n) (2)
If just try to apply 802.11ac-type beamforming to 802.11ah
  Control frames (including RTS/CTS exchange, NDPA, NDP et al.) are not beamformed (omni-directional). Even though beamformed actual data may be transmitted much farther, it may not meaningful because control frames cannot be heard at the extended distance.
  So, there is critical limitation on coverage extension due to range shortage of control frames.
transmitter
receiver
Range by omnidirectional transmission
Range by beamformed transmission

## Slide 7: Range extension of control frames
To extend range of control frames up to that of beamformed transmission
  Beamform control frames as well
    It is not possible to apply beamforming before any channel sounding
  Additional power boosting for control frames (when needed)
    It may put a hard burden on hardware implementation
  Additional coding option for control frames (when needed)
    e.g.) STBC may need to be considered firstly for control frames
  Additional repetition option for control frames (when needed)
    See next slide

## Slide 8: Additional repetition for ctrl frames
  In addition to already-introduced fixed repetition, it needs to have additional repetition option by which range of control frames can be matched to (or larger) that of beamformed data transmission
    Additional repetition may be chosen for control frames among multiple options (e.g. 2/4 or 2/4/8 et al.) if it is determined to be really critical for coverage extension
Range by omnidirectional control frames (with add. repetition)
Range by omnidirectional control frames (without add. repetition)
Range by beamformed
data frames
transmitter
receiver

## Slide 9: Additional repetition for ctrl frames (2)
If introducing additional repetition for control frames
  This repetition option needs to be selected considering the number of (max.) antennas which may be involved in beamformed transmission (mainly in AP’s side), because range extension by beamformed transmission is apparently depending on it
  In this case, length of STF and LTF in the control frames also needs to be adjusted accordingly to enhance other subsequent performances such as channel estimation, synchronization, packet detection and so on.
  Indication of which repetition option is used can be indicated in the SIG field

## Slide 10: Additional repetition for ctrl frames (3)
For preamble and data in that control frame
Data length extension
according to additional repetition
SIG length extension according to additional repetition
Repetition option can be indicated in SIG
STF length extension
(not necessarily according to additional repetition)
LTF length extension
(not necessarily according to additional repetition)