IEEE P802.11
Wireless LANs

| Some Corrections on Extended Power Constraint element |
| --- |
| Date: 2011-11-08 |
| Author(s): |
| Name | Affiliation | Address | Phone | Email |
| Illsoo Sohn | LG Electronics | LG R&D Complex 533, Hogye-1dong, Dongan-Gu, Anyang-Shi, Kyungki-Do, 431-749, Korea | +82-31-450-1882 | Illsoo.sohn@lge.com |
| Yongho Seok | LG Electronics | LG R&D Complex 533, Hogye-1dong, Dongan-Gu, Anyang-Shi, Kyungki-Do, 431-749, Korea | +82-31-450-1947 | yongho.seok@lge.com |

Abstract

This document includes some corrections on 8.4.2.172 Extended Power Constraint element in11ac draft.

Text changes for the baseline spec are proposed based on REVmb_D10.0.

Text changes for the TGac spec are proposed based on 11ac_D1.3.

##### Situation:

With the support of very wide bandwidths in VHT, the transmission signal may be subject to various transmit power constraint given by the regulatory body. Thus, in IEEE meeting #126, TGac accepted to introduce a new Extended Power Constraint element to enable efficient power control for very widebands. Please see 11/306r2 for detailed proposal with text changes and 11/290r4 for TGac March 2011 Agenda with motions.

However, while 11ac_draft 0.3 is being created after IEEE meeting #126, some texts included in 11/306r2 are missing or changed by mistake. Unfortunately, those seem to be essential parts to understand the new element.

- Missing texts: mb

| Document | Texts |
| --- | --- |
| 11/306r2 | 7.3.2.15 Power Constraint element The Power Constraint element contains the information necessary to allow a STA to determine the local maximum transmit power in the current primary 20MHz and primary 40MHz channel. The format of the Power Constraint element is shown in Figure 7-52 (Power Constraint element format). |
| 11ac_draft0.3 (also draft1.3) | Nothing (text changes are missing) |

- Mis-conveyed texts: definition

| Document | Texts |
| --- | --- |
| 11/306r2 | 7.3.2.15a Extended Power Constraint element The Extended Power Constraint element contains the information necessary to allow a STA to determine the local maximum transmit power in each of the operating channel bandwidths. |
| 11ac_draft0.3 (also draft1.3) | 8.4.2.99 Extended Power Constraint element(#559) The Extended Power Constraint element determines the local maximum transmit power in each of the operating frequency segment(Ed). |

##### Discussion:

The issues shown above seem like simple editing mistakes. However, those are quite misleading to people who try to understand the Extended Power Constraint element. Thus, it is strongly recommended to correct them as soon as possible before the next LB.

## Editing instructions:

8. Frame formats

8.4 Management and Extension frames(11ad) body components

8.4.2 Information elements

TGac editor: Change the following section 8.4.2.16 Power Constraint element as follows:

8.4.2.16 Power Constraint element

The Power Constraint element contains the information necessary to allow a STA to determine the local maximum transmit power in the current primary 20MHz and primary 40MHz channel. The format of the Power Constraint element is shown in Figure 8-97 (Power Constraint element format).

…

TGac editor: Change the following section 8.4.2.172 Power Constraint element as follows:

8.4.2.172 Extended Power Constraint element

The Extended Power Constraint element determines the local maximum transmit power in each of the operating frequency segment channel width. The format of the Power Constraint element is shown in Figure 8-ac23.

…

##### Pre-Motion:

Move to accept text changes with Editing Instruction as in 11/1543r0.

Y / N / A