## Slide 1: Scanning Considerations
Date: 2011-11-09
Authors:

## Slide 2: Abstract
The presentation introduces passive and active scanning operations. The passive scanning is considered to be implementation specific and the main focus is set to active scanning.
The challenges, active scanning operation and goals of scanning are questioned and explained.

## Slide 3: Background, how the FILS delay is measured?
How is the setup delay of the Fast Initial Link Setup (FILS) measured: (Assuming that time is measured to WLAN Link establishment)
  Is it the duration from the time when WLAN network is available (Time A)
  Or is it the measured from the time when the STA starts to scan the channels? (Time B)
  Or is it measured from the time when STA has discovered available network? (Time C)
WLAN Link is established
WLAN network is available
STA has discovered WLAN network
Time A
STA scans the channels
Time B
Time C

## Slide 4: Target outcome of the scanning
A STA may scan to:
  Discover all available BSSs
    The end user selects the network from the list of available networks
  Discover a BSS that the scanning device may use
    When a network from predefined list is found, the use of the network is automatic
  Discover is a new or more optimal BSS
    Background operation to maintain available networks and prepare for ”FILS”
What is the target outcome of the scanning in FILS?

## Slide 5: Scanning mechanisms
The scanning should find appropriate network fast and precisely, and avoid creating overhead
The 802.11 defines two scanning mechanisms:
  Passive scanning
  Active scanning
The scanning mechanisms are described in more details in the following slides

## Slide 6: Recap, passive scanning
The device selects a channel and tries to receive a frame
  Other than beacon, probe response and GAS response frames may reveal the network topology and MAC address of an AP
  The operating parameters of AP are present in beacon, probe responses and GAS responses
The passive scanning may be always ongoing when a STA is Awake
  The device may receive traffic and collect information of available networks and APs

## Slide 7: Recap, passive scanning
Passive scanning does not create overhead to scanned channel, but the scanning may take long time
  Short passive scanning may not discover all networks and BSSs
Passive scanning is implementation specific
  No signaling or knowledge of the operation is needed for other STAs
  Scanning STA may select the duration for scanning
  Logic for passive scanning needs not to be specified in 802.11 standards
For these reasons the passive scanning is not discussed further in the presentation

## Slide 8: Recap, active scanning
The active scanning consists of requests and responses
  Two protocols are defined:
    Probe, defined in 802.11 and mainly used for AP discovery
    GAS, defined originally in 802.11u and mainly used for network discovery
A request may be addressed to an individual or a broadcast address
  Individually addressed request is responded by the addressed STA, i.e. at maximum one STA responds
  The broadcast addressed request is responded by all STAs that receive the request and match with the response conditions, i.e. multiple STAs may respond

## Slide 9: Challenge related to requests
  Currently each STA has right to transmit a probe request at any time. The amount of requests is hard to limit
  Even, if the very same request is transmitted by two STAs, the coverage areas of the requesting STAs are different
  The scanning delays get easily longer, if the STA waits and tries to obtain request from other STA to avoid duplicate requests
    If all STAs wait to receive request from other STA, the scanning duration is increased
    It is not easy to test or specify the logic how STAs limit the amount or requests
  The requests are becoming more unique, the responses to other requests may not be applicable

## Slide 10: Short response to unique request
One target of the active scanning is to transmit very precise and specific requests
If the response conditions are specific, is the response information really needed?
  The requesting STA may already know what the response information will include
  The requesting STA may only be interested to measure the link to the responding STA
How much the response may be shortened?
  The Null Data Packet (NDP) includes PLCP headers needed to estimate the link to responding STA
  The requesting STA may use NDP responses for continous background scanning

## Slide 11: Recap, response addressing
The responses are addressed to individual address of the requesting STA
  The response is acknowledged by the requesting STA. If no acknowledgment is received the response is retransmitted
  Lack of retransmissions easily results to larger amount of requests and responses, because requesting STAs do not rely that they have received all responses
It is assumed that the STAs receive also the responses that are addressed to other devices
  Multiple addressing schemes of response frames complicates the implementation

## Slide 12: Recap, response to request to broadcast address
Probe request transmitted to broadcast address may result to many responses
  All responses are set to transmission at the same time
    This easily causes congestion and transmission collisions
  802.11ae is solving the collisions by using AC_BE (AC1) to
    Probe requests transmitted to broadcast address
    Probe responses transmitted as response to broadcast addressed probe request
  AC_BE (AC1) causes longer delays to delivery of the probe request and responses, especially when traffic from higher ACs is transmitted

## Slide 13: Request to broadcast address
The probe request transmitted to broadcast address is extensively used by legacy STAs
  The legacy STAs will continue to transmit probe requests to broadcast address in future
The discovery of the limiting parameters (SSID, etc) of the broadcast addressed requests may consume time
    The probe request transmitted to broadcast address is good mechanism on idle channels to avoid delays of passive scanning
Mechanisms to coordinate and control the responses to request transmitted to broadcast address should be studied and developed
  For instance, mechanisms to eliminate responses from already known or unnecessary SSIDs or BSSIDs are needed

## Slide 14: Response to request to individual address
Requests addressed to individual address and responses to these requests are transmitted with the highest AC_VO
  Individually addressed request and response are faster to transmit
  The individually addressed request needs to be addresssed to a specific MAC address
    Discovery of the MAC address may consume time
  Multiple individually addressed requests may:
    Consume more bandwidth than one broadcast addressed request and multiple responses
    Increase scanning delays, due transmission of multiple requests

## Slide 15: Content of the response
The response contains information of the responding AP, information of other BSSs is not present
  Lack of other BSS information may result to transmission of unnecessary requests and responses
Many presentations propose to add information of other BSSs to responses
  The same information could be aggregated to less response frames
    Own response to broadcast addressed request should be cancelled, if the requesting STA has already received the information
Benefits of reducing the amount of responses:
  The contention is reduced
  The transmission delay of responses is shorter
  The system capacity is increased

## Slide 16: Ending the reception at a channel
The requesting STA may stop receiving probe responses after Max_Probe_Response_time
  No indication is transmitted when the requesting STA stops receiving at the channel
  The responses cannot be acknowledged without the acknowledging (requesting) STA
  The retransmission of the response is complicated. Why is the acknowledgment not received?
    Due to collision or failed transmission?
    Or due to lack of acknowledging STA?

## Slide 17: Succesful scanning
The scanning STA has discovered the suitable SSID
      May the scanning request be more specific, i.e. Limit the responses to suitable SSID to discover the candidate AP?
The scanning STA has discovered the candidate AP and started the FILS, or that scanning STA has ended the reception at the channel
  How the scanning STA may indicate that it is no longer interested to receive more probe responses?
The time consumption of scanning may vary a lot
  The duration that the scanning STA is in Awake State mechanism should be minimized
  The mechanism should allow the responding APs to continue the responses transmission to enable passive scanning of other STAs

## Slide 18: Summary
The presentation explained the current operation of hte active scanning
  The goals and challenges of the active scanning were described
The presentation provided means to transmit more specific requests and enable more control and coordination to requesting STA
The presentation provided means to include more information to responses and to reduce overhead in active scanning
These remedies make scanning faster and more reliable