IEEE P802.11 Wireless LANs

| Antenna Indication in VHT Capabilities Info |
| --- |
| Date: 2011-11-09 |
| Author(s): |
| Name | Affiliation | Address | Phone | email |
| Reza Hedayat | Cisco Systems |  |  | rehedaya at cisco dot com |
| Brian Hart | Cisco Systems |  |  | brianh at cisco dot com |

Baseline specification: 802.11ac D1.3

| 3398 |  | 8.4.2.100.2 | 86.40 | The number of antennas is not necessarily the same with the number of space-time streams depending on the implementation. Focusing the number of space-time streams seems more reasonable. | Use the number of space-time streams instead of the number of antennas. | Agree in principle. See Doc 11/1566, 11/1568. |
| --- | --- | --- | --- | --- | --- | --- |

Proposed resolution: Agree in principle. Motivation and details are in 11/1558.

TGac Editor: Please apply the following changes:

8.4.2.167.2 VHT Capabilities Info field

The structure of the VHT Capabilities Info field(#2129) is defined in Figure 8-ac15.

| B13 B15 | B16 B18 | B19 | B20 | B21 | B22 | B23 B25 | B26 B27 | B28 | B29 | B30B31 |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Compressed Steering Number of BF Antennas Supported | Number of Sounding Dimensions | MU Beamformer Capable | MU Beamformee Capable | VHT TXOP PS | +HTC-VHT Capable | Max A-MPDU Length Exponent | VHT Link Adaptation Capable | RX Antenna Pattern Consistency | TX Antenna Pattern Consistency | Reserved |
| Bits: 3 | 3 | 1 | 1 | 1 | 1 | 3 | 2 | 1 | 1 | 2 |  |

Figure 8-ac15—VHT Capabilities Info field

The subfields of the VHT Capabilities Info field are defined in Table 8-ac14 (Subfields of the VHT Capabilities Info field).

TGac Editor: Add the following rows to the end of Table 8-ac14

Table 8-ac14—Subfields of the VHT Capabilities Info field

| Subfield | Definition | Encoding |
| --- | --- | --- |
| RX Antenna Pattern Consistency | Indicates the possibility of RX antenna pattern change | Set to 0 if RX antenna pattern might change during association. Set to 1 if RX antenna pattern does not change during association. |
| TX Antenna Pattern Consistency | Indicates the possibility of TX antenna pattern change | Set to 0 if TX antenna pattern might change during association. Set to 1 if TX antenna pattern does not change during association. |

TGac Editor: Please add the following sub-clause:

10.39.4 VHT STA antenna indication

A VHT STA that does not change its RX antenna pattern after association shall set RX Antenna Pattern Consistency subfield in VHT Capabilities Info field to 1; otherwise the STA shall set RX Antenna Pattern Consistency subfield in VHT Capabilities Info field to 0.

A VHT STA that does not change its TX antenna pattern after association shall set TX Antenna Pattern Consistency subfield in VHT Capabilities Info field to 1; otherwise the STA shall set TX Antenna Pattern Consistency in VHT Capabilities Info field to 0.