## Slide 1: Proposal for an Accelerated Link Setup Procedure
Date: 2012-01-12
Authors:

## Slide 2: Abstract
This document proposes a baseline procedure for Fast Initial Link Setup by using pre-acquired knowledge at AP and/or STA.

## Slide 3
Conformance w/ TGai PAR & 5C
Conformance Question | Response
Does the proposal degrade the security offered by Robust Security Network Association (RSNA) already defined in 802.11? | No
Does the proposal change the MAC SAP interface? | No
Does the proposal require or introduce a change to the 802.1 architecture? | No
Does the proposal introduce a change in the channel access mechanism? | No
Does the proposal introduce a change in the PHY? | No
Which of the following link set-up phases is addressed by the proposal? (1) AP Discovery (2) Network Discovery (3) Link (re-)establishment / exchange of security related messages (4) Higher layer aspects, e.g. IP address assignment | 1,2,3, 4

## Slide 4
Proposal Summary
Use pre-acquired knowledge to accelerate initial link setup
Enable both AP and STA to initiate optimizations for initial link setup
Introduce a baseline procedure to accommodate various possible optimizations for initial link setup in a flexible and interoperable way
Provide link setup optimization examples
  FILS using AP’s knowledge of the upcoming STA’s identity
  FILS using STA pre-established security association with the network
Meet the RSNA security requirement

## Slide 5: Initial Link Setup with Pre-Acquired Knowledge
There are 802.11ai use cases where the AP and the STA could pre-acquire knowledge of the link to be setup, e.g.,
  The STA has been previously connected to another network, e.g., 3G to WLAN Handover, and Hot-Spot Pass-Through Internet Access to offload traffic from other network;
  An AP at a transit station can access the information such as the train arrival schedule, and active internet users that are arriving in the train;
The pre-acquired knowledge can be used to accelerate the link setup, a useful mechanism in other technologies;
It is feasible, and practical, to use pre-acquired knowledge in initial link setup in the 802.11 context, with proper procedural and signaling supports.

## Slide 6: AP-Initiated vs. STA-Initiated Link Setup Optimizations
In the current link setup process, all the function phases, e.g., Network Discovery, TSF, 802.11 Authentication, Association, etc., are initiated by the STA, which means:
  STA can choose and pick, not AP;
  AP only passively responds.
There are cases where the AP has the proper or even better knowledge to initiate link setup optimizations, e.g.,
  AP knows the services that can be provided by the network behind it;
  AP knows the required air link transmission adjustment of the STA based on the reception of the frames from the STA.

## Slide 7: Supporting Multiple Link Setup Optimization Variants
TGai has received a good set of proposals to accelerated the link setup process from different angles, e.g.,
  AP Discovery, Network Discovery, security setup, encapsulation of upper layer message in Layer-2 message, etc.
Many TGai proposals are valid for only a selected set of use cases and scenarios;
A TGai solution should be able to accommodate multiple link setup optimization variants in a flexible, and interoperable way.

## Slide 8: Baseline FILS Procedure
We propose a baseline FILS procedure for link setup between two FILS-capable stations, which enables:
  Pre-acquired knowledge to be used to accelerate the link setup;
  AP to initiate link setup optimizations;
  A TGai solution which accommodates multiple link setup optimizations in a flexible and interoperable way.
The proposed baseline FILS procedure consists of the following logic functions:
  Pre-acquire knowledge; (does not count as part of the link setup time based on tgai-evaluation-methodology 11/0811r7)
  Optimized AP discovery
    Multiple optimization variants to find a right AP in the range, with / without pre-acquired knowledge
    Negotiation of customized post-AP-Discovery link setup procedure
  Customized Post-AP-Discovery link setup procedure.

## Slide 9: Baseline FILS Procedure – Con’t

## Slide 10: Baseline FILS Procedure – Con’t
Proposed procedural actions and Signaling support considerations:
  FILS capability indication:
    Essentially an one-bit flag, should be provided in the earlier messages of the link to be setup.
  Pre-acquired knowledge indication/provision, and confirmation:
    Should be provided in the first round of unicast messages between the two ends;
    Information IEs should be carried by the existing management frames, e.g., Probe Request / Response.
  Negotiation of a customized post-AP-discovery link setup procedure:
    Should be conducted at the AP-discovery phase, piggybacking the existing management message rounds, i.e., no additional message rounds are required;
    Pre-assign a unique identifier (e.g., a 16-bit code) to each TGai-supported post-AP-discovery link setup procedures.

## Slide 11: Example 1: AP knows STA’s Identity and Service needs

## Slide 12: Example 2: STA has pre-established Security Association

## Slide 13: Conclusion
A preliminary baseline FILS procedure is recommended for the link setup between two FILS-capable stations, which enables:
  Pre-acquired knowledge to be used to accelerate the link setup process;
  AP to initiate link setup optimizations;
  A TGai solution to accommodate multiple link setup optimizations in a flexible and interoperable way.
Further details are still in development.

## Slide 14: Questions / Comments ?
Thank You!

## Slide 15: References
802.11-2007
802.11u-2011
11-11-0238-19-00ai-use-case-reference-list-for-tgai
11-11-0745-05-00ai-tgai-functional-requirements
11-11-0811-07-00ai-tgai-evaluation-methodology
11-09-1000-06-0wng-ieee802-11-for-high-speed-mobility
11-10-0988-02-0fia-protocol-comparison
11-10-0922-02-0fia-achievable-gains-in-ap-discovery
11-11-1237-01-00ai-tgai-key-technical-ideas

## Slide 16: Strawpolls
  Do you agree TGai solution should accommodate multiple link setup optimizations in a flexible and interoperable way?
  Yes: No: Don’t know:
  Do you think there are TGai use cases where pre-acquired knowledge can be used to accelerate link setup?
  Yes: No: Don’t know:
  Do you think a baseline procedure is needed in a TGai solution?
  Yes: No: Don’t know: