## Slide 1: Coarse BSS Metric IE
Date: 2011-12-11
Authors:

## Slide 2: Abstract
This document proposes an advertisement scheme of AP operational status for STAs.

## Slide 3: Conformance w/ TGai PAR & 5C
Conformance Question | Response
Does the proposal degrade the security offered by Robust Security Network Association (RSNA) already defined in 802.11? | No
Does the proposal change the MAC SAP interface? | No
Does the proposal require or introduce a change to the 802.1 architecture? | No
Does the proposal introduce a change in the channel access mechanism? | No
Does the proposal introduce a change in the PHY? | No
Which of the following link set-up phases is addressed by the proposal? (1) AP Discovery (2) Network Discovery (3) Link (re-)establishment / exchange of security related messages (4) Higher layer aspects, e.g. IP address assignment | 1 & 2

## Slide 4: Motivation
TGai compliant STA will connect with TGai compliant AP very fast.
But it may be meaningless for the STA to associate with APs which are in bad situation even if the link setup is very fast.
AP status consultations by GAS query/response will cause packet congestions especially in use case of Tokyo central station. In that case, many STAs send GAS query packets when they go through near AP.

## Slide 5: Proposal
This document proposes Coarse BSS Metric IE for Beacon and Probe Response including the following information:
  Number of associating STAs and air-time occupation
  Backhaul link speed (including in/out of service)
A STA determines to associate with the AP or not after receiving Coarse BSS Metric IE.
Content size of Coarse BSS Metric IE should be small in order to minimize air-time occupancy increment.

## Slide 6: IE details (Coarse BSS Metric IE)
Element ID
Length
Coarse BSS metric
Octets:
1
1
1
Coarse Station Capacity
WAN Link Speed
Coarse Channel Utilization
Reserved
Bits:
2
2
2
2

## Slide 7: Proposed values
Name | Explanation | Values (temporary)
Coarse Station Capacity | The remaining amount of STAs connected available | 0: 0 to 10 1: 11 to 50 2: 51 to 100 3: over 100
WAN Link Speed | WAN connection speed to the internet | 0: Link down 1: up to 10 Mbps 2: up to 100Mbps 3: over 100Mbps
Coarse Channel Utilization | The percentage of time occupancy by carrier sense mechanism | 0: Not shown 1: 0 to 50% 2: 50 to 75% 3: over 75%
Reserved |  | 0
It may be sufficient to update these metrics in every 5 or 10 minutes.
Frequent update in every second requires difficult implementation.

## Slide 8: Air-time occupancy
The size of Coarse BSS metric IE is only 3 octets.
The increment of time occupancy of Beacon with BSS metric IE is 24 usec. (8*3 / 1Mbps)
When the AP transmits Beacons every 100 msec, the time occupancy increment by Coarse BSS metric IE is 240 usec in a second. (0.024%)

## Slide 9: GAS protocol in FILS
FILS protocol shall be achieved even without using GAS protocol.
In FILS use cases, STAs normally knows the target SSIDs which STAs want to associate with. It isn’t Interworking use case with external network. So, what is the information to be obtained by GAS protocol in addition?
This document proposes Coarse BSS metric advertisement by Beacon. The air-time occupation increment is very small.
Just one GAS query packet occupies over 360usec (just DIFS+CW duration) at least. It is much larger than the air-time occupation increment by Coarse BSS metric IE.
I don’t think of any necessities to discuss GAS protocol in TGai. (Any objections?)

## Slide 10: GAS protocol in FILS (cont.)
STA
AP
Beacon
GAS request
GAS response
Association request (FILS)
This part should be discussed separately from TGai.

## Slide 11: Questions and Comments

## Slide 12: References
Doc.: IEEE 11-11/1565r0
IEEE802.11-2007