## Slide 1: Higher Layer Setup Proposal Presentation
Name | Affiliations | Address | Phone | email
Hitoshi MORIOKA | Allied Telesis R&D Center | 2-14-38 Tenjin, Chuo-ku, Fukuoka 810-0001 JAPAN | +81-92-771-7630 | hmorioka@root-hq.com
Gabor Bajko | Nokia | 200 S Mathilda Ave, Sunnyvale | 8585253693 | gabor.bajko@nokia.com
Hiroshi Mano | Allied Telesis R&D Center | 7-21-11 Nishi-Gotanda, Shinagawa-ku, Tokyo 141-0031 JAPAN | +81-3-5719-7630 | hmano@root-hq.com
Mark RISON | CSR | Cambridge Business Park, Cowley Road, Cambridge CB4 0WZ UK | +44-1223-692000 | Mark.Rison@csr.com
Marc Emmelmann | Fraunhofer FOKUS | Kaiserin-Augusta-Alle 31 10589 Berlin Germany | +49-30-3463-7268 | emmelmann@ieee.org
Date: 2012-01-10
Authors:

## Slide 2: Abstract
This document describes a technical proposal for TGai which addresses upper layer setup phase.
This proposal is assumed to combine with EAP-RP (11/1160r4).

## Slide 3: Conformance w/ Tgai PAR & 5C
Conformance Question | Response
Does the proposal degrade the security offered by Robust Security Network Association (RSNA) already defined in 802.11? | No
Does the proposal change the MAC SAP interface? | No
Does the proposal require or introduce a change to the 802.1 architecture? | No
Does the proposal introduce a change in the channel access mechanism? | No
Does the proposal introduce a change in the PHY? | No
Which of the following link set-up phases is addressed by the proposal? (1) AP Discovery (2) Network Discovery (3) Link (re-)establishment / exchange of security related messages (4) Higher layer aspects, e.g. IP address assignment | 4

## Slide 4: Typical Sequence for Internet Access by IPv4
STA
AP
DHCP
DHCP Server
Authentication, Association, Key negotiation
Gateway
Correspondent Node
Communication
ARP
3 round-trips of frame exchanges between AP and STA before communication in addition to authentication, association and key negotiation

## Slide 5: Reduce Frame Exchanges
One of the target of TGai is to accommodate a lot of STAs simultaneously.
Each frame consumes air-time for IFSs regardless of the frame length.
So reducing the number of frame exchanges is effective for this target.

## Slide 6: Optimized Sequence for Internet Access with 1 Round-trip Association (11/1160r3)
STA
AP
DHCP Server
Gateway
Correspondent Node
Communication
AS
Virtually Simultaneous
(RADIUS for AAA)
Assoc. Req.
w/HLS Request
Element
(could be
encrypted)
Assoc. Resp.
w/HLS Response
Element
(could be
encrypted)
e.g. DHCP w/Rapid Commit Option
ARP/ND

## Slide 7: Concept
The proposed protocol is terminated at the AP.
This protocol is NOT DHCP/RA. Just uses the message format for future flexibility.
AP
STA
.11ai HLS
DHCP
RA
Static
Out of Scope

## Slide 8: Modified Existing Element
Extended Capabilities element
  Add the following fields.
    IPv4ConfigDuringAssoc (1bit)
      Indicates that the AP supports Higher Layer Setup for IPv4.
    IPv6ConfigDuringAssoc (1bit)
      Indicates that the AP supports Higher Layer Setup for IPv6.
    OnlyOneIPConfigDuringAssoc (1bit)
      If 1, the AP provides either IPv4 or IPv6 Higher Layer Setup.

## Slide 9: New Elements
HLS Request Element
HLS Response Element

## Slide 10: HLS Request Element
Element Format
HLS Request Flags
  Encrypted: Optional subelements are encrypted or not.
  IPv4: The STA requests IPv4 HLS or not.
  IPv6: The STA requests IPv6 HLS or not.

## Slide 11: HLS Response Element
Element Format
HLS Response Flags
  Encrypted: Optional Subelements are encrypted or not.

## Slide 12: Optional Subelements
Subelement ID | Name | Length | HLS Request | HLS Rsponse
0 | Reserved |  |  | 
1 | IPv4 Configuration | 1-250 | 1 | 1
2 | IPv4-MAC address | 1-250 |  | Multiple
3 | IPv6 Configuration | 1-250 | 1 | 1
4 | IPv6-MAC address | 1-242 |  | Multiple
5 | IPv6 RA | 1-250 |  | Multiple
6-220 | Reserved |  |  | 
221 | Vendor Specific | 1-250 | Multiple | Multiple
222-255 | Reserved |  |  | 

## Slide 13: IPv4 Configuration Subelement
Subelement Format
  IPv4 Configuration Message field contains a DHCPDISCOVER (HLS Request) or a DHCPACK (HLS Response) message defined in RFC2131 without MAC header, IP header, UDP header.

## Slide 14: IPv4-MAC Address Subelement
Subelement Format
  IPv4-MAC Address Combination
  This subelement is used for reducing ARP packet exchanges.

## Slide 15: IPv6 Configuration Subelement
Subelement Format
  IPv6 Configuration Message field contains a DHCP SOLICIT (HLS Request) or a DHCP REPLY (HLS Response) message defined in RFC3315 without MAC header, IP header, UDP header.

## Slide 16: IPv6-MAC Address Subelement
Subelement Format
  IPv6-MAC Address Combination
  This subelement is used for reducing NDP packet exchanges.

## Slide 17: IPv6 RA Subelement
Subelement Format
  MAC Address field contains the MAC address of the router that transmits the Router Advertisement.
  Router Advertisement field contains a Route Advertisement message defined in RFC4861 including IP header but without MAC header.

## Slide 18: Fragmentation
HLS Request/Response and all subelements can be fragmented.
  Example (400octest of IPv4 Configuration and 1 combination of IPv4-MAC address in HLS Responses)
IPv4 Config. subelement
IPv4-MAC Addr. subelement
402
12
HLS Resp. Header
3
IPv4 Config. subelement
IPv4-MAC Addr. subelement
12
HLS Resp. Header
3
IPv4 Config. subelement
254
150
HLS Resp. Header
3
IPv4 Config. subelement
IPv4-MAC Addr. subelement
12
HLS Resp. Header
3
IPv4 Config. subelement
254
150
IPv4 Config. subelement
IPv4-MAC Addr. subelement
402
12
AP
STA

## Slide 19: IPv4 Behavior
AP transmits IPv4ConfigDuringAssoc flag in Beacon/Probe Response.
STA transmits Assoc. Req. to AP with IPv4 flag in HLS Request element.
  This is NOT DHCP message. Just indicate to request IPv4 configuration.
  Optionally the STA can include IPv4 Configuration subelement to specify which parameters are required.
The AP authenticate the STA.
After successful authentication, the AP assigns an IPv4 address of the STA and other parameters. Then the AP transmits Assoc. Resp. with HLS Response element with IPv4 Configuration subelement and IPv4-MAC Address subelement to the STA.
  The IPv4 Configuration subelement may include the IPv4 address of the STA, the netmask, the IPv4 address of the default router, the IPv4 addresses of the DNS servers.
  The IPv4-MAC Address subelement may include the IPv4 address-MAC address pair of the default router.
The STA setup its IPv4 layer.

## Slide 20: IPv6 Behavior
AP caches the latest RA.
  AP can know DHCPv6 is required or not by receiving RA.
AP transmits IPv6ConfigDuringAssoc flag in Beacon/Probe Response.
STA transmits Assoc. Req. to AP with IPv6 flag in HLS Request element.
  This is NOT DHCP/RS message. Just indicate to request IPv6 configuration.
  Optionally the STA can include IPv6 Configuration subelement to specify which parameters are required.
The AP authenticate the STA.
After successful authentication, the AP assigns an IPv6 address of the STA and other parameters. Then the AP transmits Assoc. Resp. with HLS Response element with IPv6 Configuration subelement and IPv6 RA subelement to the STA.
  The IPv6 Configuration subelement may include the IPv6 addresses of the STA, the prefix length, the IPv6 addresses of the DNS servers.
  The IPv6 RA subelement may include the IPv6 address and MAC address of the router.
The STA setup its IPv6 layer.

## Slide 21: Configuration Refresh
The higher layer configurations that is assigned by HLS service must be maintained by HLS refresh procedure.
STA
AP
Association w/HLS
Refresh by
HLS Action frames

## Slide 22: HLS Action Frame
HLS Request
HLS Response

## Slide 23: IPv6 Address Assignment
Stateless Autoconfiguration (RFC4862)
Stateful Autoconfiguration (DHCPv6, RFC3315)

## Slide 24: Stateless Autoconfiguration Sequence
Host
Router
1. Generate tentative address
2. NS for duplication check
3. Assign link-local address to I/F
4. NA
5. RS
6. RA
7. NS for DAD
8. Assign global address to I/F
9. NA

## Slide 25: Stateful Autoconfiguration Sequence
Host
Router
1. Generate tentative address
2. NS for duplication check
3. Assign link-local address to I/F
4. NA
5. RS
6. RA
8. NS for DAD
9. Assign global address to I/F
10. NA
DHCP Server
7. DHCP

## Slide 26: IPv4 Only Network
If STA can know that the network does not support IPv6, it should stop transmitting IPv6/ICMPv6 packets.
When IPv6ConfigDuringAssoc in Extended Capabilities is false, STA MUST NOT transmit any IPv6/ICMPv6 packets
Host
1. Generate tentative address
2. NS for duplication check
3. Assign link-local address to I/F
4. NA
5. RS (& retry)
Waste of airtime
mDNS query

## Slide 27: Implementation Example for IPv4
WLAN driver
IP stack
Userland
WLAN driver
DHCP client
DHCP server
Configure to use IPv4 FILS
Setup
STA
AP
DHCP Server
IEs
Trigger
DHCP
Message
DHCP
synchronous/asynchronous

## Slide 28: Questions & Comments