## Slide 1: Performance Eveluation
Name | Affiliations | Address | Phone | email
Hitoshi MORIOKA | Allied Telesis R&D Center | 2-14-38 Tenjin, Chuo-ku, Fukuoka 810-0001 JAPAN | +81-92-771-7630 | hmorioka@root-hq.com
Date: 2012-01-12
Authors:

## Slide 2: Abstract
This document describes an example of measurement and performance evaluation of existing protocol.

## Slide 3: Example of Existing Protocols
Authentication: EAP-TTLS/MS-CHAPv2
Key Exchange: EAPOL Key
IP address assignment: DHCPv4
Address Resolution: ARP

## Slide 4: Sequence of Existing Protocols
STA
AP
Auth
DHCP Server
Gateway
ARP
AS
Assoc
EAP-TTLS
/MS-CHAPv2
EAPOL
Key
DHCP

## Slide 5: Performance Definition
Link Setup Latency
  from non-AP STA transmits Authentication
  to complete resolution of the default gateway MAC address
  This shows how fast a non-AP STA to setup the link.
Occupied Airtime
  Total airtime occupied by each frame for one non-AP STA to complete link setup.
  This includes transmission time, IFSs, CW and ACK transmission time (unicast).
  This shows how many non-AP STAs can be accomodated.
Auth
ARP Reply
ACK
SIFS
DIFS
CW
Occupied Airtime (Auth)
Link Setup Latency
Occupied Airtime
(ARP Reply)

## Slide 6: Link Setup Latency Measurement
Most of Link Setup Latency is caused by the latency of processing on STA, AP and servers.
So I measured the latency of existing protocols.
Latency is strongly depends on the environment.
It’s just an example.
STA
AP
AS
DHCP Server
Gateway
Internet
WLAN I/F
(to capture WLAN frames)
Capture both WLAN frames
and Ethernet frames.
(for timestamp syncronization)
iPhone4
PentiumM 1.7GHz, FreeBSD

## Slide 7: Measured Latency
Frame | STA |  | AP |  | Server | Subtotal
Auth Req |  | > |  |  |  | 
Auth Rep |  | < | 2 |  |  | 
Assoc Req | 1 | > |  |  |  | 
Assoc Resp |  | < | 2 |  |  | 5
EAP Req Id |  | < | 90 |  |  | 
EAP Resp Id | 20 | > | 2 | > |  | 
EAP Req TTLS |  | < | 32 | < | 1 | 
EAP Resp Cl Hello | 150 | > | 2 | > |  | 
EAP Req Sv Hello, Cert |  | < | 11 | < | 0 | 
EAP Resp | 33 | > | 1 | > |  | 
EAP Req Sv Hello, Cert |  | < | 16 | < | 0 | 
EAP Resp | 29 | > | 1 | > |  | 
EAP Req Sv Hello, Cert |  | < | 15 | < | 0 | 
TLS Cl key exch. | 26 | > | 1 | > |  | 
TLS Cipher Spec… |  | < | 8 | < | 25 | 
MSCHAP ID | 19 | > | 1 | > |  | 
MSCHAP Challenge |  | < | 3 | < | 0 | 
MSCHAP Challenge | 20 | > | 1 | > |  | 
EAP Success |  | < | 83 | < | 0 | 590
EAPOL Key 1 |  | < | 2 |  |  | 
EAPOL Key 2 | 3 | > |  |  |  | 
EAPOL Key 3 |  | < | 5 |  |  | 
EAPOL Key 4 | 4 | > |  |  |  | 14
[ms]
Fragmented

## Slide 8: Measured Latency (Cont’d)
Frame | STA |  | AP |  | Server | Subtotal
DHCPDISCOVER | 34 | > | 1 | > |  | 
DHCPOFFER |  | < | 62 | < | 193 | 
DHCPREQUEST | 1035 | > | 1 | > |  | 
DHCPACK |  | < | 3 | < | 1 | 1330
ARP Req. | 1629 | > | 1 | > |  | 
ARP Rep. |  | < | 1 | < | 0 | 1631
Total | 3003 |  | 347 |  | 220 | 3570
Duplicate Address
Check
Wait for other offer
Duplicate Address
Check & Gratuitous
ARP
[ms]
Frame | STA |  | AP |  | Server | Subtotal
DHCPDISCOVER | 34 | > | 1 | > |  | 
DHCPOFFER |  | < | 3 | < | 0 | 
DHCPREQUEST | 5 | > | 1 | > |  | 
DHCPACK |  | < | 3 | < | 1 | 48
ARP Req. | 5 | > | 1 | > |  | 
ARP Rep. |  | < | 1 | < | 0 | 7
Total | 349 |  | 288 |  | 27 | 664
Optimized (Optimistic & Aggressive) DHCP Implementation
[ms]
From receipt of
DHCPDISCOVER to
transmission of ARP
From receipt of
DHCPACK to
transmission of ARP
for duplication check
Assuming same
as below
Maybe environmental issue (congestion)
more than 80% reduced

## Slide 9: Occupied Airtime Calculation (DS1)
Parameters
  TXRate: 1Mbps (DS1)
  aSlotTime: 20us
  aSIFSTime: 10us
  aPreambleLength: 144us
  aPLCPHeaderLength: 48us
  aCWmin: 31
  aCWmax: 1023
  DIFS = aSIFSTime+2*aSlotTime = 50us
  CWave = aCWmin*aSlotTime/2 = 310us (No contention assumed)
  ACKLength: 18octets
  FrameLength (inluding MAC Header): n octets
Rough Occupied Airtime by n octets frame (including MAC header and FCS)
  Broadcast from AP (no ACK) Tbroadcast(n) = aPreambleLength+aPLCPHeaderLength+n*8/TXRate+DIFS+CWave = 144+48+n*8/1+50+310 [us] = n*8+552 [us]
  Other
  Tunicast(n) = Tbroadcast(n)+aPreambleLength+aPLCPHeaderLength+ACKLength/TXRate+aSIFSTime = n+552+144+48+18/1+10 [us] = n+772 [us]

## Slide 10: Occupied Airtime Calculation (OFDM6)
Parameters
  TXRate: 6Mbps (OFDM6)
  aSlotTime: 9us
  aSIFSTime: 16us
  aPreambleLength: 16us
  aPLCPHeaderLength: 4us
  aCWmin: 15
  aCWmax: 1023
  DIFS = aSIFSTime+2*aSlotTime = 34us
  CWave = aCWmin*aSlotTime/2 = 67.5us (No contention assumed)
  ACKLength: 18octets
  FrameLength (inluding MAC Header): n octets
Rough Occupied Airtime by n octets frame (including MAC header and FCS)
  Broadcast from AP (no ACK) Tbroadcast(n) = aPreambleLength+aPLCPHeaderLength+n*8/TXRate+DIFS+CWave = 16+4+n*8/6+34+67.5 [us] = n*4/3+121.5 [us]
  Other
  Tunicast(n) = Tbroadcast(n)+aPreambleLength+aPLCPHeaderLength+ACKLength/TXRate+aSIFSTime = n*4/3+121.5+16+4+18/6+16 [us] = n*4/3+160.5 [us]

## Slide 11: Occupied Airtime
Frame | Size | Airtime (DS1) | Subtotal (payload) |  | Airtime (OFDM6) | Subtotal (payload | 
Auth Req | 45 | 1132 |  |  | 221 |  | 
Auth Rep | 34 | 1044 |  |  | 206 |  | 
Assoc Req | 90 | 1492 |  |  | 281 |  | 
Assoc Resp | 50 | 1172 | 4840 | (1752) | 227 | 934 | (292)
EAP Req Id | 50 | 1172 |  |  | 227 |  | 
EAP Resp Id | 49 | 1164 |  |  | 226 |  | 
EAP Req TTLS | 46 | 1140 |  |  | 222 |  | 
EAP Resp Cl Hello | 192 | 2308 |  |  | 417 |  | 
EAP Req Sv Hello, Cert | 1064 | 9284 |  |  | 1579 |  | 
EAP Resp | 46 | 1140 |  |  | 222 |  | 
EAP Req Sv Hello, Cert | 1064 | 9284 |  |  | 1579 |  | 
EAP Resp | 46 | 1140 |  |  | 222 |  | 
EAP Req Sv Hello, Cert | 232 | 2628 |  |  | 470 |  | 
TLS Cl key exch. | 376 | 3780 |  |  | 662 |  | 
TLS Cipher Spec… | 109 | 1644 |  |  | 306 |  | 
MSCHAP ID | 183 | 2236 |  |  | 405 |  | 
MSCHAP Challenge | 135 | 1852 |  |  | 341 |  | 
MSCHAP Challenge | 46 | 1140 |  |  | 222 |  | 
EAP Success | 44 | 1124 | 41036 | (29456) | 219 | 7317 | (4909)
EAPOL Key 1 | 135 | 1852 |  |  | 341 |  | 
EAPOL Key 2 | 157 | 2028 |  |  | 370 |  | 
EAPOL Key 3 | 191 | 2300 |  |  | 415 |  | 
EAPOL Key 4 | 135 | 1852 | 8032 | (4944) | 341 | 1466 | (824)

## Slide 12: Occupied Airtime (Cont’d)
Frame | Size | Airtime (DS1) | Subtotal (payload) |  | Airtime (OFDM6) | Subtotal (payload | 
DHCPDISCOVER | 380 | 3812 |  |  | 667 |  | 
DHCPOFFER | 380 | 3812 |  |  | 667 |  | 
DHCPREQUEST | 380 | 3812 |  |  | 667 |  | 
DHCPACK | 380 | 3812 | 15248 | (12160) | 667 | 2669 | (2027)
ARP Req | 80 | 1412 |  |  | 267 |  | 
ARP Rep | 98 | 1556 | 2968 | (1424) | 291 | 558 | (237)
Total |  | 72124 |  | (49736) | 12944 |  | (8289)

## Slide 13: Conclusion
In practical environment, major link setup latency is brought by DHCP.
Optimistic and Aggressive DHCP implementation may reduce most of DHCP latency. But it’s unrecommended procedure according to the protocol specification.
Another configuration procedure which is optimized for wireless network should be considered.
Major airtime occupancy is brought by authentication phase.
30-35% of airtime is consumed by overheads (IFSs, CW, preamble…).
Reducing number of frames is effective.
DS consumes much more airtime than OFDM. Especially this is caused by long overhead.
To quit using DS is effective.

## Slide 14: Future Work
Evaluate the performance of the proposed protocols to help the TG decision.
Airtime
Latency
proposal A
proposal B
proposal C

## Slide 15: Questions & Comments