## Slide 1: TGai FILS Authentication Protocol
Name | Affiliations | Address | Phone | email
Robert Sun; Yunbo Li Edward Au; Phil Barber Junghoon Suh; Osama Aboul-Magd | Huawei Technologies Co., Ltd. | Suite 400, 303 Terry Fox Drive, Kanata, Ontario K2K 3J1 | +1-613-2871948 | Rob.sun@huawei.com
Paul Lambert Yong Liu | Marvell Semiconductor | 5488 Marvell Lane Santa Clara, CA 95054 | + 1-650-787-9141 | paul@marvel.com
Date: 2011-11-15
Authors:

## Slide 2: Abstract

## Slide 3: Conformance w/ TGai PAR & 5C
Conformance Question | Response
Does the proposal degrade the security offered by Robust Security Network Association (RSNA) already defined in 802.11? | No
Does the proposal change the MAC SAP interface? | No
Does the proposal require or introduce a change to the 802.1 architecture? | No
Does the proposal introduce a change in the channel access mechanism? | No
Does the proposal introduce a change in the PHY? | No
Which of the following link set-up phases is addressed by the proposal? (1) AP Discovery (2) Network Discovery (3) Link (re-)establishment / exchange of security related messages (4) Higher layer aspects, e.g. IP address assignment | 3

## Slide 4: RSNA Security Analysis
Stage 1:Network and Security Capability Discovery
Stage 2: 802.11 Authentication and Association
    802.11 Open System Authentication is included only for backward compatibility
Stage 3: EAP/802.1X/RADIUS Authentication
    This stage execute the mutual authentication protocol based on EAP (i.e EAP-TLS, EAP-SIM/AKA/TTLS) authentication
    AP is functioning as authenticator to relay EAP messages
    This stage COULD be skipped in the scenarios of :
      1) PMK cached for re-authentication
      2) PSK is shared between STA and AP
Stage 4: 4-way handshake:
    Both STA and the AP can trust each other with the authorized token (PMK) to derive the PTK and GTK

## Slide 5: RSNA Security Analysis
Stage 5 (Optional): Group Key Handshake
    The AP will generate the fresh GTK and distributed this GTK to the STA
    GTK may be distributed during the Stage 4
Stage 6: Secure Data Communication
    DHCP request/response
    …

## Slide 6: The Security Model of RSNA
Policy
Decision
Point
Policy
Decision
Point
Policy
Enforcement
Point
Policy
Enforcement
Point
STA
AS
AP
Authenticate to derive
MSK
2: Derive PMK from MSK
3: Use PMK to enforce
802.11 channel access
Derive and use PTK
Reference: “IEEE 802.11i Overview”, 2002, Nancy Cam-Winget, et al

## Slide 7: RSNA Components
IEEE 802.1X for Access Control
EAP (RFC 4017) for authentication and cipher suite negotiation
4-Way Handshake for establishing security association between STA and AP
Pre-Shared Key (PSK) mode between AP and STA

## Slide 8: RSNA Establishment Procedures (I)
Supplicant
Unauthenticated
Unassociated
802.1x Blocked
Authenticator
Unauthenticated
Unassociated
802.1x Blocked
Authentication
Server
(Radius)
(1) Beacon +AA RSN-IE
(2) Probe Request
(3) Probe Response + AA RSN-IE
(4) 802.11 Authentication Request
(5) 802.11 Authentication Response
(6) Association Request +SPA RSN IE
(7) 802.11 Association Response
Authenticated
Associated
802.1x Blocked
Security Params
Authenticated
Associated
802.1x Blocked
Security Params
(8) EAPOL-Start
(9) EAPOL-Request Identity
(10) EAPOL-Response Identity
Stage 1:
Network and Security
Capability
Discovery
Stage 2:
802.11
Authentication
And Association
Stage 3:
EAP/802.1X/
Radius
Authentication
This Open authentication and association is nothing but an RSN negotiation between STA and AP, Could FILS authentication be in parallel here?
At this stage, no MPDUs are allowed due to the 802.1X state machine blocking , Can we allow traffic to go through at this stage?
Observation and
potential Improvement Areas for FILS
Area 1:

## Slide 9: RSNA Establishment Procedures (II)
Supplicant
Unauthenticated
Unassociated
802.1x Blocked
Authenticator
Unauthenticated
Unassociated
802.1x Blocked
Authentication
Server
(Radius)
(12) Mutual Authentication
(14) EAPOL Success
(16) {AA, Anounce, sn, msg1}
Master Session
Key (MSK)
(17) {SPA, Snounce, SPA, sn, msg2, MIC}
(18) {AA, Anounce, AA ,GTK, sn+1, msg3, MIC}
(19) {SPA, sn+1, msg4, MIC}
(11) Radius Request
(13) Radius Accept
Master Session
Key (MSK)
Pairwise Master
Key (PMK)
Pairwise Master
Key (PMK)
Pairwise Transient
Key (PTK)
PTK, GTK
Stage 3:
EAP/802.1X/
Radius
Authentication
Stage 4
4-Way
Handshake
3) This EAP/802.1X/Radius is supplementing the Open system authentication with mutual authentication between STA and Radius, Can this authentication be skipped if FILS authentication CAN take place at stage 2.
4) Can this FILS authentication be faster in generating the PMK?
Area 2:
5) 4-way handshake guarantees the STA can mutually trust the AP and share their keys with the indication of the PMK, Can this
process be skipped or optimized to satisfy the FILS performance requirements?
Area 3:
Pairwise Master
Key (PMK)

## Slide 10: RSNA Establishment Procedures (III)
Supplicant
Unauthenticated
Unassociated
802.1x Blocked
Authenticator
Unauthenticated
Unassociated
802.1x Blocked
Authentication
Server
(Radius)
GTK, 802.1X
Unblocked
802.1X unblocked
Generate
Rand GTK
(20) EAPOL-Key {Group, sn+2,GTK, Key ID, MIC}
(21) EAPOL-Key {Group, Key ID, MIC}
New GTK Obtained
(22 ) Protected Data Packets
Stage 5
Group Key
Handshake
(Optional)
Stage 6
Secure
Data
Communication
(23) DHCP Req/Res
DHCP
Server

## Slide 11: Modified 802.11 Authentication and Association State Machine
State 1
Unauthenticated,
Unassociated
Class 1 Frames
State 2
Authenticated,
Unassociated
Class 1 & 2 Frames
State 3
Authenticated,
Associated
(Pending RSN Authentication)
Class 1 ,2 & 3 Frames
IEEE 802.1X Controlled Port Blocked
State 4
Authenticated,
Associated
Class 1 ,2 & 3 Frames
IEEE 802.1X Controlled Port
UnBlocked
Successful
802.11 Authentication
Successful
(Re)Association –RSNA Required
4- way Handshake Successful
Deauthentication
Deauthentication
Deassociation
Deauthentication
Unsuccessful
(Re)Association
(Non-AP STA)
Successful
802.11
Authentication
Unsuccessful
(Re)Association
(Non-AP STA)
Disassociation
Successful
802.11 Authentication
Successful
(Re) Association
No RSNA required or
Fast BSS Transitions
State 5
FILS Authenticated
Class 1 & 2 Frames
With Selected Management &
Data Frames
IEEE 802.1x controlled Port blocked
Successful
FILS Authentication
FILS
Deauthentication
FILS Key Handshake
Slide 11

## Slide 12: FILS Authenticated State
Upon receipt of a Beacon message from a AP STA or Probe Request from non-AP STA with FILS authentication number, both the STA and AP’s shall transition to FILS Authenticated state
STA at FILS Authenticated State , it allows Class 1,2 and selected Data frames piggybacked over Class 1 &2 frames to be transmitted
Upon receipt of a De-association frame from either STA or AP STA with reasons, the STA at the FILS authenticated state will be transitioned to State 1. STA transitioned back to State 1 may retry with FILS authentication or use the RSNA authentication
Upon receipt of a FILS key exchange success, the STA shall transition to state 3 which is allows full class 1, 2 and 3 frames to pass through.
Selected Management Frames and Data Frames | Reasons
EAPOL | To carry out the EAPOL authentication at FILS Authenticated State
DHCP | To enable the parallel DHCP processing

## Slide 13: Appropriate FILS Authentication Properties
Mandatory Properties | 802.11i | FILS Security
Mutual Authentication with key agreement | Yes | Yes
Strong Confidentiality | Yes | Yes
RSNA Security Model | Yes | Yes
Key Confirmation | Yes | Yes
Key Derivation | Yes | Yes
Fast Re-authentication | Yes | Yes
Strong Session Key | Yes | Yes
Replay Attack Protection/MTIM protection/Dictionary Attack /Impersonation Attack Protection | Yes | Yes
Recommended Properties | 802.11i | FILS Security
Fast and Efficient | No | Yes
Forward Secrecy | Implementation Related | Implementation Related
Denial of Service Resistance | Implementation Related | Implementation Related

## Slide 14: Authentication Algorithm Number Field
Insert the following FILS Authentication Algorithm Number
  Authentication algorithm number = 0: Open System
  Authentication algorithm number = 1: Shared Key
  Authentication algorithm number = 2: Fast BSS Transition
  Authentication algorithm number = 3: simultaneous authentication of equals (SAE)
  Authentication algorithm number = 4: FILS Authentication
  Authentication algorithm number = 65 535: Vendor specific use

## Slide 15: IEEE 802.11 TGai FILS Authentication (Revising 802.11Revmb Section 4.10.3.2)
Supplicant
AP /
Authenticator
AS
1) 802.11 Beacon
2) 802.11 Probe Request
3) 802.11 Probe Response
4) |802.1x EAP OL-Start with Security Parameters for FILS handshake)
5) Access Request (EAP Request)
6) EAP Authentication Protocol Exchange
AS Generates
PMK
7) Accept/ EAP Success/ PMK
8) 802.1x EAPOL success || msg 1: EAPOL-KEY (Anounce, Unicast))
Supplicant
Generates PMK
Removing
EAP-Identity Request / Response Message
Authenticator
Stores PMK
And Generate
Anounce
Supplicant
Derives PTK
4 Way Handshake
Message is overhauled in 802.11 Auth Resp
State 1
State 5
State 1
State 5

## Slide 16: IEEE 802.11 TGai FILS Handshake (Revising 802.11Revmb Section 4.10.3.2)
Supplicant
AP /
Authenticator
9) 802.11 Association Request ( Msg 2: EAPOL-Key (Snounce, Unicastm MIC)
10) 802.11 Association Response ( Msg 3: EAPOL-Key (Install PTK, unicast, MIC, Encrypt (GTK, IGTK) ))
Msg 4: EAPOL-Key (Unicast, MIC)
Secure Data Communication
Supplicant with
PTK
Authenticator with
PTK |GTK|IGTK
Optional Msg 4 for key confirmation
Install PTK, GTK
IGTK
Install PTK, GTK
IGTK
State 5
State 4
State 5
State 4

## Slide 17: Protocol Analysis
Parallelize the Open Authentication Request/Response with EAPOL Authentication for STA and AS to execute the mutual authentication with EAP method neutral and generate PMK
Remove the EAP Identity Request and Response messages whose functions will be carried out in EAPOL start message
Parallelize the message 1 of 4-way handshake (now 3 way handshake) on 802.11 association response for STA to simultaneously generate the PMK and PTK
Parallelize the 3 way handshake with 802.11 association request/response message handshakes
Original 4 way handshake is reduced to 3 way handshake to satisfy the performance requirements (changing from Bilateral Key confirmation to Unilateral key confirmation).
No violating RSNA security protocol and security models
Total of 10 message handshakes vs 21 message handshakes
Dec 2011

## Slide 18: Further Development for FILS authentication
Problem observed: The EAP authentication between STA and AP usually takes longer processing time given some specific EAP methods being deployed (i.e EAP-TLS with RSA and DH cipher suites)
Suggested working area:

## Slide 19: Questions & Comments