## Slide 1: Scanning with FILS
Date: 2012-01-15
Authors:

## Slide 2: Abstract
The presentation is related to 11-1619 active scanning normative text. This presentation describes:
Recap of general description of the passive and active scanning
  Recap of available enhancements for passive scanning
Improvements for active scanning mechanisms:
  Fast transmission of precise availability information with low overhead

## Slide 3: Recap, Scanning mechanisms as seen by the scanning STA
Passive scanning: The STA listens at a channel and detects the availability of the APs from the received frames
  Especially Beacons, Measurement Pilots and Probe Responses have good set of information for the scanning STA
Active scanning: The STA requests of responses and the STA receives all frames, and detects from the received frames the availability of the AP
  A response to request indicates that the response is received
  The same frames as in passive scanning are received during the scanning operation
  The reception time for probe responses is shorter than in passive scanning

## Slide 4: Recap, Scanning mechanism as seen by AP
The passive scanning STA is invisible for AP
  No signal from scanning devices
  The AP periodically transmits Beacon and Measurement Pilots
The active scanning requests are visible to AP
  The requests indicate presence of the scanning STAs
  The AP responses the requests:
    Currently each request is responded by a single response
    Currently there is no means to combine responses and coordinate to deliver the parameters:
      To deliver the parameters of the most relevant BSS
      To reduce the overhed

## Slide 5: Recap, Measurement Pilot frame
The APs may periodically transmit Beacons and Measurement Pilots to provide their availability information for passive scanning devices
  Measurement Pilot is defined in 802.11 standard
  Measurement Pilots are transmitted periodically, the AP may select the length of period (for instance AP may transmit a Measurement every 10ms)
  Measurement Pilot may include any information elements, so APs may construct a light weight beacon with information AP considers relevant for the scanning devices

## Slide 6: Active Scanning Enhancements

## Slide 7: More precise Probe Request
The probe request should indicate the devices to respond and not to respond
  Filterlist indicates the APs or SSIDs that are not requested to answer
  The repetition of already received information is eliminated
    This speeds up the responses delivery, coungestion is reduced
  The unknown APs have better opportunity to transmit probe responses
AP1
AP2
AP3
STA 1
1st Probe Request
STA 1
Probe Response
AP1
AP2
AP3
STA 1
2nd Probe Request + Filtering List
Indicate probe response from AP 2 is not desired
AP1
AP2
AP3
STA 1
Probe Responses
AP1
AP2
AP3

## Slide 8: Challenge, knowledge of the availability of scanning STA
The STA that transmitted Probe Request does not have means to indicate when it will no longer be available to receive Probe Responses
  The individually addressed Probe Responses will not be acknowledged and they will be retransmitted
  The responses may be transmitted unnecessarily if the requesting STA is not present to receive the responses

## Slide 9: Stopping reception at a channel
The scanning device should be able to indicate that it no longer scans the channel
  The Max Channel Time parameter is added to Probe Request frame, after Max Channel Time, the scanning STA
  Probe End frame to indicate that scanning STA is no longer available to receive
  The Probe Responses shall not be retransmitted after Max Channel Time or after Probe End is transmitted

## Slide 10: Probe Response collision avoidance: Comprehensive probe response
One probe response may contain information of multiple APs at the same band
  The total amount of responses is reduced
    The sample of the radio performance may be obtained through any frame
STA 1
Probe Request
Chn 1
Chn 6
Request for information of other BSSs
AP1
AP2
AP3
STA 1
Probe Response + Neighbor List
Contains information of itself (AP 2), as well as AP 1 and AP 3
Chn 1
Chn 6
AP1
AP2
AP3

## Slide 11: Probe Response collision avoidance: Elimination of unnecessary Probe Responses
When many probe requests are being transmitted, the amount of probe responses may become high
The APs should avoid sending unnecessary copies of probe responses
  Single copy of probe response or beacon frame is enough
  Probe Response transmitted to Broadcast address avoids retransmissions in congested situations
STA 1
Probe Request
STA 2
STA2 misses the probe request transmission
AP1
AP2
AP3
STA 1
Probe Response
STA 2
Receive probe responses
AP1
AP2
AP3
STA 1
Probe Request
STA 2
AP1
AP2
AP3

## Slide 12: Summary
The filter list more precise Probe Request reduces unnecessary Probe Response
The knowledge of the time that the scanning device is available avoids unncessary (re)transmissions
The collision avoidance mechanisms to probe response:
  Eliminates unnecessary copies of the Probe Responses
  Comprehensive Probe Responses combines information of multiple APs to single Response and provides guidance to select the next channel for scanning

## Slide 13: References
11-11-1619r1, Active Scanning