## Slide 1: Selection of the AP for Scanning
Date: 2011-01-12

## Slide 2: Abstract
Scanning time is one of the major cause of the delay in initial Link Setup
In active scanning, a STA transmits Probe Request frame in Broadcast, usually using wildcard SSID to find APs.
It can cause unnecessary packet exchange which increases the network traffic and causes link setup delay
This proposal reduces the overhead of active scanning by providing precise selection mechanism of the AP s to respond with Probe Response
Approach:
  Add Exclusion List to the Probe Request frames to precisely limit the scope of APs or STAs that should transmit probe response
  Make the substring of the BSSIDs or Mesh IDs can be used to indicate the APs or STAs to be excluded

## Slide 3: Conformance w/ Tgai PAR & 5C
Conformance Question | Response
Does the proposal degrade the security offered by Robust Security Network Association (RSNA) already defined in 802.11? | No
Does the proposal change the MAC SAP interface? | No
Does the proposal require or introduce a change to the 802.1 architecture? | No
Does the proposal introduce a change in the channel access mechanism? | No
Does the proposal introduce a change in the PHY? | No
Which of the following link set-up phases is addressed by the proposal? (1) AP Discovery (2) Network Discovery (3) Link (re-)establishment / exchange of security related messages (4) Higher layer aspects, e.g. IP address assignment | 1

## Slide 4: Selection of the AP to Scan - Background
To discover the AP to associate, a STA transmits Probe Request in Broadcast with wildcard SSID
APs transmit Probe Response  too many probe responses
AP 1
AP 2
AP 3
AP 4..
AP n
STA
Probe Request on channel x (broadcast)
Probe Response
flooding
Probe Response
Probe Response
Probe Response
Probe Response
Probe Response
Probe Response
Probe Response (Retransmission)
Probe Response (Retransmission)
Probe Response (Retransmission)

## Slide 5: Selection of the AP to Scan - Approach
Exclusion List is added to the Probe Request frames to precisely limit the scope of APs or STAs that should transmit probe response frame
Substring can be used in the Exclusion List to indicate SSID or Mesh ID
  helps to reduce the size of the Exclusion List
  Not necessary to include individual IDs in the Exclusion List
Exclusion List with substring capability can provide precise
selection of the AP to transmit Probe Response frame

## Slide 6: Selection of the AP to Scan – Example (1/5)
AP1
AP 2
AP 3
AP 4..
AP n
STA
Probe Request(broadcast,
with Exclusion List)
Probe Response
Probe Response
.
.
.
Only AP that is not included in the Exclusion
List reponds
SSID = NETGEAR
SSID = ETRI#1
SSID = ETRI#2
SSID = ETRI#3
…..
SSID = Company A
SSID = SKT
Exclusion List: contains “ETRI”
and indicated as a substring
Example: filter SSID that contains “ETRI” as a substring

## Slide 7: Selection of the AP to Scan – Example (2/5)
Example: Existing active scanning method
. The user does not know the exact SSID of the AP to connect
ETRI0002
ETRI0003
ETRI0004
ETRI0005
ETRI0006
ETRI0001
KT0002
KT0003
KT0004
KT0005
WVPN-7-33
KT0003
KT0004
KT0005
WVPN-7-32
WVPN-6-1
Hyatt_1
VeriLAN
Hyatt_2
Hyatt_2
STA
Probe Request
(wildcard SSID)
Too many Probe Response frames !!
.
.
.

## Slide 8: Selection of the AP to Scan – Example (3/5)
Example: Selection of the AP using Exclusion List
The user does not know the exact SSID. He does not subscribe to KT.
The user does not want to access the corporate VPN services or company APs (ETRI)
 Exclude them in the scanning
- Add substring KT, ETRI, VPN into the Exclusion List !
KT0002
KT0003
KT0004
KT0005
WVPN-7-33
KT0003
KT0004
KT0005
WVPN-7-32
WVPN-6-1
Hyatt_1
VeriLAN
Hyatt_2
Hyatt_2
STA
Probe Request
(Exclusion List with SSID substring)
Reduced Probe Responses
x
x
x
x
x
x
x
x
x
x
ETRI0002
ETRI0003
ETRI0004
ETRI0005
ETRI0006
ETRI0001
x
x
x
x
x
x

## Slide 9: Selection of the AP to Scan – Example (4/5)
Example: Existing active scanning method
The user does not subscribe to KT but SKT
SKT0002
SKT0003
SKT0004
SKT0005
SKT0006
SKT0001
KT0002
KT0003
KT0004
KT0005
KT0003
KT0004
KT0005
SKT000x
SKT000z
SKT000y
VeriLAN
Hyatt_2
Hyatt_2
STA
Probe Request
(wildcard SSID)
Too many Probe Response frames !!
.
.
.

## Slide 10: Selection of the AP to Scan – Example (5/5)
Example: Exclusion List with substring – using substringInfo field
The user does not subscribe to KT but SKT
SKT0002
SKT0003
SKT0004
SKT0005
SKT0006
SKT0001
KT0002
KT0003
KT0004
KT0005
KT0003
KT0004
KT0005
VeriLAN
Hyatt_2
Hyatt_2
STA
SKT000x
SKT000z
SKT000y
Probe Request
(ExclusionList with substring)
Add substring KT and indicate
“starts with” in the substringInfo field
(SKT is not filtered !)
 Do not need to list all the SSIDs to filter
x
x
x
x
x
x
x

## Slide 11: Exclusion List
Added to the Probe Request frames to precisely limit the scope of STAs to respond
Specifies the set of STAs that should not transmit a response to a Probe Request frame
If STAs are selected by BSSID, SSID, SSID List, HESSID, or Mesh ID and if some of the selected STAs are indicated by the lists in the Exclusion List, then they should not transmit a response to the Probe Request frame
Substring can be included in the Exclusion List

## Slide 12: Exclusion List: MLME-SCAN.request (1/2)
MLME-SCAN.request( )
MLME-SCAN.request(
BSSType,
BSSID,
SSID,
ScanType,
ProbeDelay,
ChannelList,
MinChannelTime,
MaxChannelTime,
RequestInformation,
SSID List,
ChannelUsage,
AccessNetworkType,
HESSID,
MeshID,
Exclusion List,
VendorSpecificInfo
)

## Slide 13: Exclusion List: MLME-SCAN.request (2/2)
Name | Type | Valid range | Description
Exclusion List | As defined in 8.4.x.x | As defined in 8.4.x. | Specifies the set of STAs that should not transmit a response to a Probe Request frame. If STAs are selected by BSSID, SSID, SSID List, HESSID, or Mesh ID and if some of the selected STAs are indicated by the lists in the Exclusion List, then they should not transmit a response to the Probe Request frame. This element is optionally present only if dot11FILSActivated is true and any of the fields in this element are nonzero

## Slide 14: Exclusion List format (1/4)
1. BSSID element
The BSSID field contains a BSSID or a MAC address of a STA. A BSSID field of all 1s is used to indicate the wildcard BSSID
2. HESSID element
The HESSID field contains a HESSID. A HESSID field of all 1s is used to indicate the wildcard HESSID
Element ID | Length | BSSID
Octets: 1 1 6
Element ID | Length | HESSID
Octets: 1 1 6

## Slide 15: Exclusion List format (2/4)
3. BSSID List element
The BSSID List field is a list of BSSID elements, each including the element ID, length field and BSSID information field for which the STA is requesting information
4. HESSID List element
The HESSID List field is a list of HESSID elements, each including the element ID, length field and HESSID information field for which the STA is requesting information
Element ID | Length | BSSID List
Octets: 1 1 variable
Element ID | Length | HESSID List
Octets: 1 1 variable

## Slide 16: Exclusion List format (3/4)
5. MESHID List element
The MESHID List field is a list of MSEHID elements, each including the element ID, length field and MESHID information field for which the STA is requesting information
Element ID | Length | MESHID List
Octets: 1 1 variable

## Slide 17: Exclusion List format (4/4)
6.Exclusion List element
Includes SubstringInfo, SSID List element, BSSID List element, MESHID List element, and HESSID List element
Included in the Probe Request frame
Substrings can be used in SSID elements or MESHID elements
  - Interpretation of the strings are indicated in the SubstringInfo field
Octets: 1 1 1 variable
Element ID | Length | SubstringInfo | SSID List | BSSID List | MESHID List | HESSID List

## Slide 18: SubstringInfo field format
Included in Exclusion List
Make it possible to indicate SSID or Mesh ID by their substrings
Several substring type can be indicated (starts with, ends with,…)
SubstringInfo field indicates whether the the strings contained in the SSID or Mesh ID elements included in the Exclusion List are substrings of the actual SSID or Mesh ID that indicates the STAs that should respond with the Probe Request frame.
The Substring Supported subfield:
  Set to 1 if the STA supports the indication of substring of SSID or Mesh ID
  Set to 0 if the STA does not support the indication of substring and if it is set to 0, the value of Substring Type is reserved.
Substring Supported | Substring Type | Reserved
bits: 1 3 4

## Slide 19: Substring Type subfield
The Substring Type field indicates the type of substring used in the BSSID or Mesh ID elements.
Value | Meaning
0 | Strings used in the SSID or Mesh ID elements in the Exclusion List are the actual SSIDs or Mesh IDs (not substring)
1 | The actual SSIDs or Mesh IDs of the intended STAs are the SSIDs or Mesh IDs that start with, or end with, or contain the substrings specified in the SSID or Mesh ID elements in the Exclusion List.
2 | The actual SSIDs or Mesh IDs of the intended STAs are the SSIDs or Mesh IDs that start with the substrings specified in the SSID or Mesh ID elements in the Exclusion List.
3 | The actual SSIDs or Mesh IDs of the intended STAs are the SSIDs or Mesh IDs that end with the substrings specified in the SSID or Mesh ID elements in the Exclusion List.
4-7 | Reserved

## Slide 20: Probe Request Frame
Order | Information | Notes
xx | Exclusion List | The Exclusion List element is optionally present only if dot11FILSActivated is true and any of the fields in this element are nonzero.
Exclusion List is includes in the Probe Request frame
Legacy STA that does not recognize the Exclusion List element
just ignores the element
Exclusion List provides additional refinement of the selected STA, chosen by BSSID, SSID, MeshID, and HESSID in legacy standard
If the STA does not support TGai capability or Exclusion List feature,
Exclusion List is not used by the STA and the selected STA is a superset of
the STAs that can be additionally limited by TGai STAs
Substrings in the Exclusion List is not used by legacy STA and causes no problem (legacy SSID, SSID List, Mesh ID outside the Exclusion List do not use the substring)

## Slide 21: Sending a Probe Response (1/3)
STAs receiving Probe Request frames shall respond with a probe response only if:
The Address 1 field in the probe request is the broadcast address or the specific MAC address of the STA, and either item b) or item c) below
b) The STA is a mesh STA and
1) The Exclusion List does not include the Mesh ID or substrings of the Mesh ID of the STA in the MESHID List element, or the specific MAC address of the STA in the BSSID List element, if the Exclusion List is present in the Probe Request and the dot11FILSActivated is true, and
2) The Mesh ID in the probe request is the wildcard Mesh ID, or the specific Mesh ID, of the STA

## Slide 22: Sending a Probe Response (2/3)
c) The STA is not a mesh STA and
1) The Exclusion List does not include the SSID or the substrings of the SSID of the STA in the SSID List element, or the specific BSSID of the STA in the BSSID List element, if the Exclusion List is present in the Probe Request and the dot11FILSActivated is true, and
2) The SSID in the probe request is the wildcard SSID, the SSID in the probe request is the specific SSID of the STA, , or the specific SSID of the STA is included in the SSID List element, and
3) The Address 3 field in the probe request is the wildcard BSSID or the BSSID of the STA

## Slide 23: Sending a Probe Response (3/3)
Additionally, STAs with dot11InterworkingServiceActivated equal to true, receiving Probe Request frames containing an Interworking field in the Extended Capabilities element set to 1 shall examine the Interworking element in the received Probe Request frame and respond with a probe response only if
d) The Exclusion List does not include the HESSID of the STA in the HESSID List element if the Exclusion List is present in the Probe Request and the dot11FILSActivated is true, and the HESSID field, if present in the Interworking element, is the wildcard HESSID or the HESSID of the STA, and
e) The Access Network Type field in the Interworking element is the wildcard Access Network Type or the Access Network Type of the STA.

## Slide 24: Conclusion
Scanning time is one of the major cause of the delay in initial Link Setup
Legacy active scanning can cause unnecessary packet exchange which increases the network traffic and causes link setup delay
In this proposal:
  Exclusion List is added to the Probe Request frames to precisely limit the scope of APs or STAs that should transmit probe response frame
  Use of substring in the Exclusion List to indicate SSIDs or Mesh IDs
    helps to reduce the size of the Exclusion List
    Not necessary to include individual IDs in the Exclusion List
    Provides flexible substring matching
   helps to reduce the unnecessary exchange of Probe Request frame thus increasing the efficiency of the active scanning