## Slide 1: Selective transmission of the Probe Response
Date: 2011-01-12

## Slide 2: Abstract
In active scanning, Probe Response can cause unnecessary packet exchange which increases the network traffic and causes link setup delay
We propose the selective transmission of the Probe Response frame to reduce the unnecessary Probe Response frame
Approach:
  Filter the Probe Response frame by the responding AP based on Capabilities and Preferences of the STA that has sent the Probe Request frame
    can reduce the traffic caused by Probe Response frames
    helps the selection of appropriate STAs to be associated
Jae Seung Lee, ETRI

## Slide 3: Conformance w/ Tgai PAR & 5C
Conformance Question | Response
Does the proposal degrade the security offered by Robust Security Network Association (RSNA) already defined in 802.11? | No
Does the proposal change the MAC SAP interface? | No
Does the proposal require or introduce a change to the 802.1 architecture? | No
Does the proposal introduce a change in the channel access mechanism? | No
Does the proposal introduce a change in the PHY? | No
Which of the following link set-up phases is addressed by the proposal? (1) AP Discovery (2) Network Discovery (3) Link (re-)establishment / exchange of security related messages (4) Higher layer aspects, e.g. IP address assignment | 1
Jae Seung Lee, ETRI

## Slide 4: Selective Probe Response - Background
To discover the AP to associate, a STA transmits Probe Request in Broadcast with wildcard SSID
APs transmit Probe Response
Too many probe responses: Need to reduce the unnecessary Probe response
APs respond to the Probe Response even if the requesting STA cannot or will not associate with the AP
  Due to the lack of the capability of the STA, or
  The STA does not want to use certain capability
   Sending Probe Response to such STAs is not necessary
Jae Seung Lee, ETRI

## Slide 5: Active Scanning - Problem
AP 1-1
AP 1-2
AP 1-3
AP 1-…
AP 1-n
STA
AP 3-1
AP 3-2
AP 3-3
AP 3-…
AP 3-n
AP 5-1
AP 5-2
AP 5-3
AP 5-…
AP 5-n
Probe Request on channel 1 (broadcast, wildcard SSID)
Channel 1
Channel 2
(idle)
Probe Request on channel 3 (broadcast, wildcard SSID)
Probe Request on channel 5 (broadcast, wildcard SSID)
Probe Request on channel 2 (broadcast, wildcard SSID)
Probe Request on channel 4 (broadcast, wildcard SSID)
Probe Request on channel n (broadcast, wildcard SSID)
Channel 3
Channel 5
Channel 4
(idle)
Channel n
Probe Response
.
.
.
Probe Response
.
.
.
Probe Response
.
.
.
Sequential
Scanning
Of all
Channels
Jae Seung Lee, ETRI
APs respond to the Probe Request
although the STA cannot associate with
some of the APs

## Slide 6: Selective Transmission – Approach (1/2)
Filtering Information including Capabilities and Preferences of the STA is included in the Probe Request frame
The Responding APs or STAs can check the capabilities and preferences of the STA that transmitted the Probe Request
  Capability information such as security capability including RSN capability is included in the Probe Request frame
  Preference information such as request for security processing, or request for no security processing or request for associate with HT, VHT, or non-HT STA is included in the Probe Request frame
Jae Seung Lee, ETRI

## Slide 7: Selective Transmission – Approach (2/2)
  If the preferences of the STA cannot be satisfied by the
  responding APs, or
  (2) If the capabilities of the STAs that transmit Probe Request
  frame cannot fulfill the security policy of the APs that
  receive the Probe Request frame, or
  (3) The responding AP cannot accept the STA because of the AP’s current condition (e.g., high Load)
  The responding APs do not transmit Probe Response frame
  reduces unnecessary Probe Response
  helps selection of AP to associate
AP Channel Report element received in the probe responses during the active scanning can be used to help the selection of the next channel to be scanned
Jae Seung Lee, ETRI

## Slide 8: Capability and Preference based Filtering
No Response to the STAs that cannot fulfill the responding AP’s capability requirement or if the responding AP cannot satisfy the preference of the STAs
If the responding AP cannot accept the new STA because of its own reasons, such as high load, it can disallow the association by not responding the Probe Request
Solution: Add CapabilityFilterInfo to Probe Request
CapabilityFilterInfo IE contains Security capability element including security capabilities of the Requesting STA
  AP can check the security capabilities of the Requesting STAs
CapabilityFilterInfo IE contains Filtering Preference element including preferences of the STA to the responding AP
  Includes request of Security processing or request to associate HT, VHT, or non-HT STA, etc
Jae Seung Lee, ETRI
Slide 8

## Slide 9: Benefits of the Filtering
Reduces the Probe Response traffic
  filter the Probe Response because the STA cannot be associated with the responding AP
    No reason to transmit Probe Response frame
Prevent the association of the STAs that cannot be accepted by the responding AP
Helps the association process by enabling the STA to choose the appropriate APs that can be associated with the STA
  If the STA cannot be associated with the responding AP, Probe Response is not received  association with the AP is prohibited
Jae Seung Lee, ETRI

## Slide 10: Selective Probe Response – Example (1/2)
Jae Seung Lee, ETRI
Example: Using existing active scanning method
The requesting STA is a VHT STA and only wants to associate with a VHT AP
The STA requires management frame protection
STA
Probe Request
(Broadcast)
Receives Probe Responses
although the STA cannot,
or will not associate with the APs
.
.
.
STA41
(non-HT, no security)
STA11
(HT, No Security)
STA 28
(non-HT,
no security)
STA05
(VHT, Security,
MFPC=1,MFPR=1)
STA09
(VHT, No Security)
STA07
(HT, Security,
MFPC=1,MFPR=1)
STA40
(VHT, Security,
MFPC=0, MFPR=0)
STA29
(VHT, Security,
MFPC=1,MFPR=1)
STA03
(VHT, no security)
High Load!
STA39
(VHT, Security,
MFPC=1,MFPR=1)

## Slide 11: Selective Probe Response – Example (2/2)
Jae Seung Lee, ETRI
Example: Using CapabilityFilterInfo in Probe Request
The requesting STA is a VHT STA and only wants to associate with a VHT AP
The STA requires management frame protection
STA41
(non-HT, no security)
STA
Probe Request (Broadcast)
Reduced Probe Responses!
STA11
(HT, No Security)
STA 28
(non-HT,
no security)
STA05
(VHT, Security,
MFPC=1,MFPR=1)
STA09
(VHT, No Security)
STA07
(HT, Security,
MFPC=1,MFPR=1)
STA40
(VHT, Security,
MFPC=0, MFPR=0)
STA29
(VHT, Security,
MFPC=1,MFPR=1)
STA03
(VHT, no security)
High Load!
x
x
x
x
x
x
x
x
O
O
Require VHT, Require Security,
MFPC=1, MFPR=1
(CapabilityFilterInfo)
STA39
(VHT, Security,
MFPC=1,MFPR=1)

## Slide 12: MLME-SCAN.request()
MLME-SCAN.request( )
MLME-SCAN.request(
BSSType,
BSSID,
SSID,
ScanType,
ProbeDelay,
ChannelList,
MinChannelTime,
MaxChannelTime,
RequestInformation,
SSID List,
ChannelUsage,
AccessNetworkType,
HESSID,
MeshID,
CapabilityFilterInfo
VendorSpecificInfo
)
Jae Seung Lee, ETRI

## Slide 13: MLME-SCAN.request()
Name | Type | Valid range | Description
CapabilityFilterInfo | CapabilityFilterInfo element | As defined in 8.4.x. | Specifies options required for Probe Response frame filtering by the responder of the Probe Request based on the capabilities or preferences of the requesting STAs. This element is present only if dot11FILSActivated is true.
Jae Seung Lee, ETRI

## Slide 14: CapabilityFilterInfo element
Element ID | Length | Filtering Preference | Security capability element
Octets: 1 1 2 variable
Jae Seung Lee, ETRI
Slide 14
Specifies options required for Probe Response frame filtering by the responder of the probe request based on the capabilities or preferences of the requesting STAs

## Slide 15: Filtering Preference Field
bits: 1 1 1 1 1 1 10
Filter Request | Require Security | Require No Security | Require HT | Require VHT | Require non-HT | Reserved
Specifies the filtering preferences of the STAs that transmit Probe Request frame
Jae Seung Lee, ETRI

## Slide 16: Filtering Preference Field – Subfields (1/3)
Filter Request subfield
  indicates whether the STA prefers the filtering of the Probe Response frame by the responder of the Probe Request frame based on the CapabilityFilterInfo element
If set to 1, the responder of the probe request shall send the Probe Response frame
  If the responding STA can satisfy all the preferences of the requesting STA specified in the Filtering Preference field, and
  If the Security capabilities included in the Security capability element sent by the requesting STA meets all the security policy of the responding STA, and
  If the supported rates of the requesting STA indicated in the Supported rates element in the Probe Request frame supports all the rates in the BSSBasicRateSet parameter of the responding STA
Jae Seung Lee, ETRI

## Slide 17: Filtering Preference Field – Subfields (2/3)
Meaning of the Require Security and Require No Security subfield
Require Security | Require No Security | Meaning
1 | 1 | . No Security Preference by the requesting STA. . Security capability element shall be included in the CapabilityFilterInfo element.
1 | 0 | . The requesting STA requires the use of the security options. . Security capability element shall be included in the CapabilityFilterInfo element.
0 | 1 | . The requesting STA requires no security options to be used. . Security capability element may not be included in the CapabilityFilterInfo element.
0 | 0 | . Reserved.
Jae Seung Lee, ETRI

## Slide 18: Filtering Preference Field – Subfields (3/3)
Meaning of the the Require HT subfield, require VHT subfield, and Require non-HT
Require HT | Require VHT | Require non-HT | Meaning
1 | 1 | 1 | No preference
1 | 0 | 0 | The requesting STA requires to associate with only HT STAs
0 | 1 | 0 | The requesting STA requires to associate with only VHT STAs
0 | 0 | 1 | The requesting STA requires to associate with only non-HT STAs
1 | 1 | 0 | The requesting STA requires to associate with HT STAs or VHT STAs
1 | 0 | 1 | The requesting STA requires to associate with HT STAs or non-HT STAs
0 | 1 | 1 | The requesting STA requires to associate with VHT STAs or non-HT STAs
0 | 0 | 0 | Reserved
Jae Seung Lee, ETRI

## Slide 19: Security capability element (1/2)
Security capability element specifies the security capability of the STAs that transmit Probe Request frame
Present if Require Security bit is set
Element ID | Length | Version | Group Data Cipher Suite Count | Group Data Cipher Suite List | Pairwise Cipher Suite Count | Pairwise Cipher Suite List | AKM Suite Count | AKM Suite List
RSN Capabilities | Group Management Cipher Suite Count | Group Management Cipher Suite List
Octets: 1 1 2 2 4 x m 2 4 x n 2 4 x o
Octets: 2 2 4 x p
m: group data cipher suite count, n: pairwise cipher suite count, o: AKM suite count, p: group management cipher suite count
Jae Seung Lee, ETRI

## Slide 20: Security capability element (2/2)
Almost identical to RSN IE, but multiple Group Data Cipher Suite and Group Management Cipher Suite can be indicated
  Version, Pairwise Cipher Suite Count, Pairwise Cipher Suit List, AKM Suite Count, AKM Suite List, RSN Capabilities fields are the same fields used in the RSN element
  The Group Data Cipher Suite Count field: the number of Group data cipher suite selectors that are contained in the Group Data Cipher Suite List field
  The Group Management Cipher Suite Count: the number of Group management cipher suite selectors that are contained in the Group Management Cipher Suite List field
If the requesting STA supports a Cipher Suite but if it does not want to use it with the STAs that it wants to transmit Probe Request frame, then it may not include it in the Security capability element
Jae Seung Lee, ETRI

## Slide 21: Probe Request Frame
Order | Information | Notes
Xx | CapabilityFilterInfo | The CapabilityFilterInfo element is present only if dot11FILSActivated is true .
Jae Seung Lee, ETRI
Simple extension to existing Probe Request frame
Probe Response frame is not modified

## Slide 22: Sending a Probe Response (1/4)
The STA responds with a Probe Response only if:
Filter Request subfield in the CapabilityFilterInfo element is set to 0 or if b) and c) are satisfied
b) Filter Request subfield is set to 1 and
The responding STA satisfies the security processing preferences specified in Require Security subfield and Require No security subfield in CapabilityFilterInfo element, and
The responding STA satisfies the preferences specified in Require HT, Require VHT, and Require non-HT subfield in the CapabilityFilterInfo element, and
The security capabilities of the requesting STA satisfies the security policy of the responding STA when the Require Security subfield is set to 1 and Require No Security subfield is set to 0
  If both the Require Security subfield/Require No Security subfield are set to 1, and if the responding STA chooses to use security processing with the requesting STA, then the responding STA responds with Probe Response frame only if the security capabilities of the requesting STA satisfies the security policy of the responding STA, and the condition 1 and 2 are met
  If both the Require Security subfield/Require No Security subfield are both set to 1, and if the responding STA does not choose to use security processing with the requesting STA, then the responding STA responds with Probe Response frame if the condition 1 and 2 are met
Jae Seung Lee, ETRI

## Slide 23: Sending a Probe Response (2/4)
c) Filter Request subfield in the CapabilityFilterInfo element is set to 1 and the supported rates of the requesting STA indicated in the Supported rates element in the Probe Request frame supports all the rates in the BSSBasicRateSet parameter of the responding STA
(Note: c) is based on 10.3.5.3 AP association receipt procedures:
“The SME shall refuse an association request from a STA that does not support all the rates in the BSSBasicRateSet parameter”)
If the responding STA decide that it cannot accept the requesting STAs because of some reasons, such as high load of the responding STA, then it does not respond with Probe Response frame to prevent the association of the requesting STAs
  How to decide whether the STA can accept the association request or not is out of scope of this standard
Jae Seung Lee, ETRI

## Slide 24: Sending a Probe Response (3/4)
The security capabilities of the requesting STA does not satisfy the security policy of the responding STA if
  The responding STA is an AP and Group Data Cipher Suite or Pairwise Cipher Suite or AKM Suite or Group Management Cipher Suite that are required by the AP is not included in the Security capability element, or
  The responding STA is an AP, and the AP supports CCMP or the AP is an HT STA, and the requesting STA is an HT STA but it supports only old cipher suite such as TKIP or WEP-40 or WEP-104, or
  The responding STA is an AP and the AP is RSNA-enabled and wants to use RSNA with the requesting STA, but the values of MFPC and MFPR in the RSN capabilities included in the Security capability element sent by the requesting STA are not suitable for the AP to associate with the requesting STA, or
  The responding STA is an IBSS STA and the requesting STA and the responding STA do not support a common subset of pairwise cipher suites or a common single group cipher suite or common AKM Suite, or
Jae Seung Lee, ETRI

## Slide 25: Sending a Probe Response (4/4)
The responding STA is an IBSS STA, and the responding IBSS STA supports CCMP or the responding IBSS STA is an HT STA, and the requesting STA is an HT STA but it supports only old cipher suite such as TKIP or WEP-40 or WEP-104, or
The responding STA is an IBSS STA and the STA is RSNA-enabled and wants to use RSNA with the requesting STA, but the values of MFPC and MFPR in the RSN capabilities included in the Security capability element sent by the requesting STA are not suitable for the responding IBSS STA to associate with the requesting STA, or
The responding STA is a Mesh STA and the requesting STA and the responding Mesh STA do not support a common subset of pairwise cipher suites or a common single group cipher suite, or
The responding STA is a Mesh STA and the requesting STA supports only old cipher suite such as TKIP or WEP-40 or WEP-104 as a pairwise cipher suite or a group cipher suite.
(Note: slide 24~25 are based on 11.5.3 RSNA policy selection in an ESS, 11.5.5 RSNA policy selection in an IBSS, and 11.5.7 RSNA policy selection in an MBSS)
Jae Seung Lee, ETRI

## Slide 26: Selective Scanning
AP Channel Report element is included in Probe Response Frame
  AP Channel Report element contains a list of channels in an operating class where a STA is likely to find an AP, excluding the AP transmitting the AP Channel Report (From 802.11 Revmb)
: It can help to perform selective channel scanning
If AP Channel Report element is included in the received probe responses, then a channel in the ChannelList that is also included in the AP Channel Report element that is not scanned yet may be selected as the next channel to be scanned
  The AP Channel Report element included in the most recently received probe response is used.
Jae Seung Lee, ETRI

## Slide 27: Selective Probe Response & Selective Scan
AP 1-1
AP 1-2
AP 1-3
AP 1-…
AP 1-n
STA
AP 3-1
AP 3-2
AP 3-3
AP 3-…
AP 3-n
AP 5-1
AP 5-2
AP 5-3
AP 5-…
AP 5-n
Probe Request on channel 1
Channel 1
Probe Request on channel 3
Probe Request on channel
Channel 6
Channel 11
Probe Response
Probe Response
Probe Response
Probe Response
No response
Check the Preference and Capability of The
Requesting STA in the Probe Response
Selective Scanning
Of the Channel
Jae Seung Lee, ETRI

## Slide 28: Conclusion
In active scanning, Probe Response can cause unnecessary packet exchange
We proposed the selective transmission of the Probe Response frame to reduce the unnecessary Probe Response frame
In this proposal:
  Filter the Probe Response frame send by the AP using Capability and Preferences of the STA that has sent the Probe Request frame
  Selective transmission of the probe response helps to reduce the traffic caused by Probe Response frames, and also helps to select appropriate STAs to be associated with
  Selective Scanning of the channels based on the channel information can reduce the scanning time
Jae Seung Lee, ETRI