## Slide 1: Link adaptation in active scanning
Author:
Date: January 13, 2011
Name | Company | Address | Phone | email
Jae-Hyung Song | LG Electronics | LG R&D Complex 533, Hogye-1dong, Dongan-gu, Anyang-shi, Kyungki-do, Korea | +82-10-5778-0915 | jaehyung.song@lge.com
Yongho Seok | LG Electronics | LG R&D Complex 533, Hogye-1dong, Dongan-gu, Anyang-shi, Kyungki-do, Korea | +82-31-450-1947 | yongho.seok@lge.com
Hyangsun You | LG Electronics | LG R&D Complex 533, Hogye-1dong, Dongan-gu, Anyang-shi, Kyungki-do, Korea | +82-31-450-7897 | sssun.you@lge.com
Jihyun Lee | LG Electronics | LG R&D Complex 533, Hogye-1dong, Dongan-gu, Anyang-shi, Kyungki-do, Korea | +82-31-450-1860 | Jihyun1220.lee@lge.com
Jonghyun Park | LG Electronics | LG R&D Complex 533, Hogye-1dong, Dongan-gu, Anyang-shi, Kyungki-do, Korea | +82-31-450-7117 | Jonghyun10.park@lge.com

## Slide 2: Abstract
This presentation provides
  A method for fast association by using adaptive MCS in active scanning procedure

## Slide 3: Open-loop rate adaptation in WLAN
Open-loop rate adaptation
  MCS is adaptable to a variety of wireless channel environments
  It requires no channel state information feedback
General concept of open-loop rate adaptation in WLAN
  In initial stage, the lowest code rate is applied to transmit frame
  If previous transmission is successful, the code rate for the next transmission is increased
  If previous transmission is failed, the code rate for the next transmission is reduced
  Successful transmission can be reported by ACK frame or related response

## Slide 4: Association protocol in WLAN
Active Scanning / Authentication / Association Protocol
  It requires many management frames such as
    Probe Request/Response
    Authentication Request/Response
    Association Request/Response
Inefficiency of association protocol
  In the association stage, the lowest code rate is applied to frame transmission at first
  The code rate is adjusted gradually according to the open-loop rate adaptation scheme
  It makes the association procedure to be performed in low rate level, and it can give negative effect to the throughput in the association stage

## Slide 5: Proposed link adaptation scheme
Concept of the proposed idea
  Link adaptation in scanning procedure
    Obtain channel information in scanning procedure
    Use appropriate MCS for frame transmission in association stage
  Effect of the proposed link adaptation
    If appropriate MCS can be used from the association stage, faster association can be accomplished

## Slide 6: Proposed link adaptation scheme
Proposed link adaptation in active scanning
  STA transmits Probe Request frame and this frame acts as NDPA
  NDP is transmitted after Probe Request frame
  AP estimates the channel quality using NDP and decides the MCS index of the STA
  The decided MCS index in transmitted by Probe Response frame as a feedback of NDPA
  Apply the obtained MCS index for the next frame transmission

## Slide 7: Proposed link adaptation scheme
Frame format for the proposed link adaptation
  Probe Request frame
Order | Element
1 | SSID
2 | Supported rates
3 | Request Information
4 | Extended Supported Rates
5 | DS Parameter Set
6 | Supported Operating Classes
7 | HT Capabilities
8 | 20/40 BSS Coexistence
9 | Extended Capability
10 | NDPA
Last | Vender Specific
 | Element ID | Length | NDP Information
Octets: | 1 | 1 | 1
 | Reserved | NDPA Indication | Sequence Number
Bits: | 1 | 1 | 6
  NDPA element format
  NDP Information field
  Probe Request frame body format

## Slide 8: Proposed link adaptation scheme
Frame format for the proposed link adaptation
  Probe Response frame
 | Element ID | Length | Number of Spatial Streams | MCS Index
Octets: | 1 | 1 | 1 | 1
  MCS Feedback element format
Order | Element
1 | Timestamp
2 | Beacon interval
3 | Capability
4 | SSID
. . . | . . .
38 | Overlapping BSS Scan Parameters
39 | Extended Capabilities
40 | MCS Feedback
Last–1 | Vendor Specific
Last–n | Requested elements
  Probe Response frame body format