## Slide 1: On Traffic Stream Setup for Audio/Visual Bridging
Date: 2012-01-14
Authors:

## Slide 2: Abstract
This submission addresses issues related to traffic stream (TS) Setup when it is initiated by the AP

## Slide 3: Problem Statement
In interworking with “higher“ layers, the AP adds interworking to its functionality.
  In SRP language [1], the AP is the Designated MSRP Node (DMN) in the above scenario
situations may arise when TS setup process is required to be indicated by the MDN (AP in this case)
Talker
WLAN Access Point
Listener
WLAN
Segment
Ethernet
Switch
Talker-Listener Path
Request
Request
Response
Response
TS Setup

## Slide 4: TS Setup in IEEE 802.11
TS setup is always initiated by non-AP STA.
  “It is always the responsibility of the non-AP STA to initiate the creation of a TS regardless of its direction” Revmb 12.0, pp 1083.
  Recognition of the AP role in an infrastructure BSS, with view on available resources and ability to allocate these resources.
TS Setup is initiated by sending an ADDTS Request frame from the STA to the AP.
  ADDTS Request frame includes a TSPEC IE describing the TS and related traffic. Relevant here are the TSID, Directionality, and traffic parameters.
The AP responds by sending an ADDTS Response frame that includes the result of the setup.
  SCHEDULE IE is present if the TS setup is successful.

## Slide 5: TS Setup Procedure
Non-AP STA
AP
ADDTS Request
ADDTS Response
TSPEC Information Element
Schedule Information Element

## Slide 6: IEEE 802.11aa Proposed Solutions [2]
Problems with the current proposal include:
  It changes how TS set up is done in IEEE 802.11 by introducing a new procedure for an already well-defined and existing procedure.
  Assumes Non-AP STA has the capability to reject AP resource allocation.
  It may be difficult for the AP to assign a TSID for the STA.
    When the TS direction is UL or bi-directional.
Talker
Ethernet
Switch
WLAN Access Point
Listener
Setup
Setup
ADDTS Reserve
Request
ADDTS Reserve
Response
ADDTS
Request
ADDTS Response
optional

## Slide 7: Alternate Proposal
Introduce a new action frame, “ADDTS Start” to instruct the non-AP STA to start the TS setup procedure as usual.
Preserve the current IEEE 802.11 TS Setup procedure.
  Doesn’t add a new procedure for performing a function that already exists.
Talker
Ethernet
Switch
WLAN Access Point
Listener
Setup
Setup
ADDTS START
ADDTS
Request
ADDTS Response
Response
Response

## Slide 8: ADDTS START Frame Format
TSPEC IE includes:
  Directionality: uplink/downlink/bi-directional
  TSID: The Non-AP STA shall reset the TSID field to a value that is consistent with its current reserved TS.
    A non-AP STA can support up to 8 TS streams from HC to itself, and up to 8 TS streams to other STA, including the HC.
  TSEPC Traffic parameters are set according to the rules specified in [1].
Order | Information
1 | Category
2 | QoS Action
3 | TSPEC
4 | Higher Layer Stream ID

## Slide 9: References
[1] Virtual Bridged Local Area Networks -Amendment XX:Stream Reservation Protocol (SRP): IEEE P802.1Qat/D6.1, June 4, 2010.
[2] Part 11: Wireless LAN Medium Access Control 9 (MAC) and Physical Layer (PHY) specifications, Amendment 2: MAC Enhancements for Robust 12 Audio Video Streaming, IEEE P802.11aa/D6.0, July 2011