IEEE P802.11
Wireless LANs

| Additional Changes between D8.0 and D9.0 (changes not in the Resolution Spreadsheet) |
| --- |
| Date: 2012-01-17 |
| Author(s): |
| Name | Affiliation | Address | Phone | email |
| Graham Smith | DSP Group | 2941 Sunrise Blvd, Ste 100 Rancho Cordova, CA 95762 | 916 379 8709 | Graham.smith@dspg.com |

Change #1:

"Remove second sentence on page 101 clause 10.27.2.3, namely "the operating class field shall be set to the operating class that is currently being used by the AP."

Reason: To cater for conditions where the AP is using a different operating class than the STAs.  Proposed by Peter Ecclesine.

Change #2:

Replace

"52" with "89" on line 43 page 118,

"53" with "90" line 64 page 118,

"54" with "91" line 20 page 119, and

"55" with "92" line 40 page 119.

Also on page 118 line 19 change "dot11STAStatisticsReportingReasonRsnaCounters OCTET STRING" with "dot11STAStatisticsnonSTBCCTSFailureCount Counter32".

Reason: To comply with 11mb numbering.  Proposed by Alex Ashley.

Change #3:

On page 84 line 20, change “Send an ADDTS Request action frame to the AP to negotiate the TSPEC parameters. This negotiation may involve multiple ADDTS Request/ADDTS Response exchanges between the non-AP STA and the AP. ”

to

“Send an ADDTS Request action frame to the AP. There might be multiple ADDTS Request/ADDTS Response exchanges between the non-AP STA and the AP, as described in 10.4.4, to negotiate the TSPEC parameters.”

Reason:  To clarify that the standard ADDTS request response exchange may be used.  Proposed by Osama Aboul-Mahd.

Change #4:

Insert on Page 117 before line 12,
“DEFVAL {‘<Publication Editor to insert the RAC allocated GCR Concealment address here>’H}”

Reason:  To provide the location for inserting the GCR Concealment MAC address when it is allocated by RAC.  Proposed by Alex Ashley.

# Text boxes

Abstract

During the second re-circulation Sponsor Ballot, 6 comments were received. The comment resolution committee has made 4 minor changes as well as preparing resolutions to all of the comments.  The comments and their resolutions are available here

https://mentor.ieee.org/802.11/dcn/11/11-12-0002-02-00aa-second-sb-comments.xls

For convenience, a list of the four changes that were not comment resolutions, are contained in this document.