## Slide 1: Proposed Additions to SFD
Date: 2012-01-19
Authors:
Name | Affiliations | Address | Phone | email
Phillip Barber | Huawei Technologies Co., Ltd. | 5360 Legacy Rd, Ste 175 Plano, Texas 750724 USA |  | pbarber@huawei.com

## Slide 2: Abstract
This document describes a technical proposal for TGai. In this proposal technical point items are provided for inclusion in the Framework Document.

## Slide 3: Conformance w/ TGai PAR & 5C
Conformance Question | Response
Does the proposal degrade the security offered by Robust Security Network Association (RSNA) already defined in 802.11? | No
Does the proposal change the MAC SAP interface? | No
Does the proposal require or introduce a change to the 802.1 architecture? | No
Does the proposal introduce a change in the channel access mechanism? | No
Does the proposal introduce a change in the PHY? | No
Which of the following link set-up phases is addressed by the proposal? (1) AP Discovery (2) Network Discovery (3) Link (re-)establishment / exchange of security related messages (4) Higher layer aspects, e.g. IP address assignment | 1

## Slide 4
From 11-12-0050r1; harmonized into 1619; add to SFD section for AP Discovery, Scanning
AP may send Probe Response to the broadcast address
From 11-12-0053r0; add to SFD section for Network Discovery
AP may include a GAS configuration-change element in the Beacon and Probe Response to indicate changes in a set of static GAS parameters
From 11-12-0067r0; harmonized into 1619; add to SFD section for AP Discovery, Scanning
STA may include a wait-time-for-Probe-Response element to Probe Request to provide a max listening duration for which the STA indicates it will wait for Probe Response transmission
SFD points

## Slide 5
From 11-12-0079r0; add to SFD section for Network Discovery
STA may include an inclusion selection filter or ‘white’ list element to GAS Request to indicate selection for a set of APs to be included as part of Neighbor Report ANQP element in GAS Response
From 11-12-0080r0; add to SFD section for AP Discovery
AP may include an indicator for AP availability to attachment to the Beacon and Probe Response
SFD points (continued)