## Slide 1: Proposed SFD Text for 802.11ai Link Setup Procedure
Date: 2012-03-02
Authors:

## Slide 2: Abstract
This document proposes text to be inserted in TGai Specification Framework Document (SFD) regarding 802.11ai link setup procedures based on the proposal given in the contribution 12/0010r1.

## Slide 3
Conformance w/ TGai PAR & 5C
Conformance Question | Response
Does the proposal degrade the security offered by Robust Security Network Association (RSNA) already defined in 802.11? | No
Does the proposal change the MAC SAP interface? | No
Does the proposal require or introduce a change to the 802.1 architecture? | No
Does the proposal introduce a change in the channel access mechanism? | No
Does the proposal introduce a change in the PHY? | No
Which of the following link set-up phases is addressed by the proposal? (1) AP Discovery (2) Network Discovery (3) Link (re-)establishment / exchange of security related messages (4) Higher layer aspects, e.g. IP address assignment | 1,2,3, 4

## Slide 4
Background
12/0191r0: Call for Contributions to the TGai Specification Framework Document (SFD);
12/0151r2: Approved TGai SFD initial document; (12/0151r3 with page numbers)
12/0010r1: the contribution presented in January Jacksonville regarding 11ai link setup procedures, and Received Positive feedback on the straw polls.

## Slide 5: Key Points Re-cap of Contribution 12/0010r1
Key points presented in contribution 12/0010r1:
  Use Pre-acquired knowledge to accelerate the link setup process;
  Enable AP and STA to initiate link setup optimizations;
  Allow a TGai solution to accommodate assorted link setup optimizations in a flexible and interoperable way.

## Slide 6: Initial Link Setup with Pre-Acquired Knowledge
There are 802.11ai use cases where the AP and the STA could pre-acquire knowledge of the link to be setup, e.g.,
  The STA has been previously connected to another network, e.g., 3G to WLAN Handover, and Hot-Spot Pass-Through Internet Access to offload traffic from other network;
  An AP at a transit station can access the information such as the train arrival schedule, and active internet users that are arriving in the train;
The pre-acquired knowledge can be used to accelerate the link setup, a useful mechanism used in other technologies;
It is feasible, and practical, to use pre-acquired knowledge in initial link setup in the 802.11 context, with proper procedural and signaling supports.

## Slide 7: AP-Initiated vs. STA-Initiated Link Setup Optimizations
In the current link setup process, all the function phases, e.g., Network Discovery, TSF, 802.11 Authentication, Association, etc., are initiated by the STA, which means:
  STA can choose and pick, not AP;
  AP only passively responds.
There are cases where the AP has the proper or even better knowledge to initiate link setup optimizations, e.g.,
  AP knows the services that can be provided by the network behind it;
  AP knows the required air link transmission adjustment of the STA based on the reception of the frames from the STA;
  AP knows its own capacity and loading, so AP can proactively decline a FILS link setup request because of its capacity limitation.

## Slide 8: Supporting Assorted Link Setup Optimization Variants
TGai has received a good set of proposals to accelerate the link setup process from different angles, e.g.,
  AP Discovery, Network Discovery, security setup, encapsulation of upper layer message in Layer-2 message, etc.
Many TGai proposals are valid for only a selected set of use cases and scenarios;
A TGai solution should be able to accommodate assorted link setup optimization variants in a flexible, and interoperable way.

## Slide 9: Straw Polls for Proposed Text for SFD
Straw Poll-1: add the follow sentence to TGai SFD, 12/0151r3
  AP and STA may use pre-acquired knowledge to accelerate the link setup.
Result Yes NO Need more info

## Slide 10: Straw Polls for Proposed Text for SFD – con’t
Straw Poll-2: add the follow sentence to TGai SFD, 12/0151r3
  A TGai solution may allow AP and STA to initiate link setup optimizations.
  Result Yes NO Need more info

## Slide 11: Straw Polls for Proposed Text for SFD – con’t
Straw Poll-3: add the follow sentence to TGai SFD, 12/0151r3
  A TGai solution may accommodate assorted link setup optimizations in flexible and interoperable ways.
  Result Yes NO Need more info

## Slide 12: Motions for Proposed Text for SFD
Motion-1: add a new section, called “Link Setup General Framework” to line 24, page 3, in the TGai SFD, 12/0151r3; and also change the section numbers accordingly for the sections after this newly proposed section, i.e.,
3. Link Setup General Framework
3 4. Security Framework
4 5. IP Address Assignment
5 6. Fast Network Discovery
Result Yes NO Abstain

## Slide 13: Motions for Proposed Text for SFD
Motion-2: add the follow text to the TGai SFD, 12/0151r3.
AP and STA may use pre-acquired knowledge to accelerate the link setup.
Result Yes NO Abstain

## Slide 14: Motions for Proposed Text for SFD – con’t
Motion-3: add the follow sentence to TGai SFD, 12/0151r3
A TGai solution may allow AP and STA to initiate link setup optimizations.
  Result Yes NO Abstain

## Slide 15: Motions for Proposed Text for SFD – con’t
Motion-4: add the follow sentence to TGai SFD, 12/0151r3
  A TGai solution may accommodate assorted link setup optimizations in flexible and interoperable ways.
  Result Yes NO Abstain