## Slide 1: Necessity of Probe Reduction
Date: 2012-03-08
Authors:

## Slide 2: Abstract
This document raises warning alarm against heavy usage of probes for fast AP discovery.
TGai should consider methods for reducing probes in FILS use cases.

## Slide 3: Review of doc. 11/1413r3 Occupied Time Calculation Result
Packet type | Occupancy rate (%) | Occupied time (sec)
Beacon | 7.06 | 21.17
Probe Req. | 3.58 | 10.75
Probe Res. | 14.74 | 44.22
Others | 74.62 | 223.86
Total | 100.00 | 300.00
Observed duration = 300 sec
Observation was executed at a train station in Tokyo on Ch6 (single channel).

## Slide 4: From captured log data….
Beacons : 14275 frames/300sec (=47.0 frames/sec)
Probe Requests : 7139 frames/300sec (=23.5 frames/sec)
Probe Response : 24687 frames/300sec (=81.3 frames/sec)
These mean:
4~5 APs existing and
23.5 STAs searching AP by active scanning in a second
around observed location.

## Slide 5: Imagining FILS use case,
100 STAs associate with AP in a second.
If 100 STAs execute active scanning in a second for fast AP discovery, about 4 times more probes will be exchanged.
 | Observed occupancy rate (23.5 STA ) | Assumed occupancy rate (100 STA)
Beacon | 7.06% | 7.06%
Probe Request | 3.58% | 15.23%
Probe Response | 14.74% | 62.72%
Total | 25.38% | 85.01%
* 4~5 APs are responding.

## Slide 6: Considerations
This high occupancy rate (85%) breaks FILS requirement just by probe exchanges.

## Slide 7: Conclusion
Persistently explaining,
Probe request with wildcard SSID will bring severe packet flooding.
Reduction of Probe requests should be considered too.
I’m thinking that:
Air-time occupancy rate should be demonstrated in coming contributions especially about fast AP discovery in order to achieve FILS requirement.

## Slide 8: Questions & Comments

## Slide 9: Supplementary Consideration

## Slide 10: Mathematical consideration (1) Assumptions
 | Assumed frame length (octets) | Air-time occupancy (usec)
Beacon | 122 | 1528
Probe Request | 143 | 1696
Probe Response | 116 | 1794
* Method for air-time occupancy calculation is described in doc. 11/1031r0.
Frame lengths are from field experimentation in Tokyo.

## Slide 11: Mathematical consideration (2) Air-time occupancy by Probes
(Responding APs)
No. of probe request / sec
* Frame conflicts aren’t considered.