## Slide 1: Comment Resolution Receiver Parameters
Date: 2012-2-15
Authors:

## Slide 2: Comment 6144 – Receiver Sensitivity for MCS2
21.3.3.9 | 488 | 39 | T | Receiver sensitivity of MCS 1 at -68 dBm is only 1 dB lower than MCS2. This does not make sense for repetition coding. Based on simulation results in P42 of IEEE 802.11-10/0432r0, the MCS1 should be 2 dB lower tha MCS2. | Change MCS1 sensitivity to -69 dBm
MCS1 employs repetition coding and the performance should be approximately 3 dB better than MCS2.
The difference between ½ code and 5/8 code should be approximately 1 dB

## Slide 3: SCM Performance-AWGN
Simulation Conditions:
Packet Length-8192 Bytes
AWGN
Red line-With impairments (PN, PA)
Blue line-no impairments
BPSK MCSs
QPSK MCSs
16QAM MCSs
2 dB
1 dB

## Slide 4: Proposed Receiver Sensitivity
 | Current Sensitivity | Proposed Value
MCS1 | -68 | -68
MCS2 | -67 | -66
MCS3 | -65 | -65
Motion: Instruct the editor to change the sensitivity of MCS2 in Table 21-3 Page 489 to -66 dBm

## Slide 5: 6145 Receiver Maximum Input Level
21.3.3.8 | 488 | 23 | T | It is not clear about the definition of the receiver maximum input level "the maximum power level at the receive antenna(s) of the incoming signal, in dBm, present at the input of the receiver for which the error rate criterion (defined at the RX Sensitivity subclause) is met." It is not clear whether it is defined at antenna port (same as receiver sensitivity) or at the air to antenna interface. It makes more sense to be at air to antenna plane. For some docking applications in close proximity, the defined level seems too low. | Please clarify it and revises the value if necessary.

## Slide 6: Proposed Maximum Receiver Input
Typical phased-array device transmit EIRP ~ 25 dBm
For some applications, the distance can be as short as .5 meter
Maximum input level should be defined at air-to-antenna plane
Field strength
  10 microwatt/cm^2 = 25 dBm/Area = 25 dBm/(4*π* 50^2)

## Slide 7: Proposed Text for .5 Meter or Higher
Maximum Input Requirement
The receiver maximum input level is the maximum power level at the receive antenna(s) of the incoming signal, in dBm, present at the input of the receiver antenna for which the error rate criterion (defined 21 at the RX Sensitivity subclause) is met. A compliant receiver shall have a receiver maximum input level at the receive antenna(s) of at least -33 dBm 10 microwatts/cm^2 for each of the modulation formats that the receiver supports.

## Slide 8
Thank You!