IEEE P802.11
Wireless LANs

| 802.11 TGac WG Letter Ballot LB187 Proposed resolutions to comments on Clause 6 |
| --- |
| Date: 2012-03-08 |
| Author(s): |
| Name | Company | Address | Phone | email |
| Adrian STEPHENS | Intel Corporation | 64, CB24 8TA, U.K. |  | Adrian.p.stephens@intel.com |

| 5402 | Yusuke Asai | 10.12 | 6.3.3.3.2 | Four primitive parameters are newly added to MLME-SCAN.request; however, there is no change in semantics of it. | Add the following four primitive parameters to the primitive parameters for MLME-SCAN.request; VHT Capabilities, VHT Operation, VHTBSSBasicMCSSet and VHTOperationalMCSSet. |
| --- | --- | --- | --- | --- | --- |

Proposed Resolution:

Rejected.  No new parameters are added to the MLME-SCAN.request.   The cited location contains additions to the BSSDescription table, which is associated with the MLME-SCAN.confirm.

| 5335 | Yasuhiko Inoue | 10.12 | 6.3.3.3.2 | The primitive parameter for MLME-SCAN.confirm is not written here. | Add the primitive parameters with underlined new items specifying the order of the parameters. For example,"The primitive parameters are as follows:MLME-SCAN.confirm ( BSSDescriptionSet, BSSDescriptionFromMeasurementPilotSet, VHT Capabiliti |
| --- | --- | --- | --- | --- | --- |

Proposed resolution:

Rejected.  The table being amended is the BSSDescription table.   It is cited as a single parameter in the MLME-SCAN.confirm semanatics, so the semantics don’t need to be changed.

| 5404 | Yusuke Asai | 10.33 | 6.3.3.3.2 | "VHTBasicMCSSet" should be revised as "VHTBSSBasicMCSSet." Ditto P20/L36. | As in comment. |
| --- | --- | --- | --- | --- | --- |

Discussion:

The commenter is correct.   The term used elsewhere is “VHTBSSBasicMCSSet” (22 instances).

Proposed resolution:

Accept.

| 4547 | Dorothy Stanley | 12 | 6.3.7.3.2 | Entry "QMFPolicy" from 11ae D8.0 Page 4 is missing | Insert "QMFPolicy" on P12L45, after "QosMapSet" |
| --- | --- | --- | --- | --- | --- |

Proposed resolution:

Accept.

| 5337 | Yasuhiko Inoue | 12.05 | 6.3.7.2.2 | It is not clear whether the VHT Capabilities parameter of the MLME-ASSOCIATE.request includes only contents of the VHT Capabilities Info field or the contents of VHT Capabilities Info field and VHT Supported MCS Set field. | Clarify, please. |
| --- | --- | --- | --- | --- | --- |
| 5338 | Yasuhiko Inoue | 13.01 | 6.3.7.3.2 | It is not clear whether the VHT Capabilities parameter of the MLME-ASSOCIATE.confirm includes only contents of the VHT Capabilities Info field or the contents of VHT Capabilities Info field and VHT Supported MCS Set field. | Clarify, please. |

| 5339 | Yasuhiko Inoue | 14.01 | 6.3.7.4.2 | It is not clear whether the VHT Capabilities parameter of the MLME-ASSOCIATE.indication includes only contents of the VHT Capabilities Info field or the contents of VHT Capabilities Info field and VHT Supported MCS Set field. | Clarify, please. |
| --- | --- | --- | --- | --- | --- |
| 5341 | Yasuhiko Inoue | 15.06 | 6.3.7.5.2 | It is not clear whether the VHT Capabilities parameter of the MLME-ASSOCIATE.response includes only contents of the VHT Capabilities Info field or the contents of VHT Capabilities Info field and VHT Supported MCS Set field. | Clarify, please. |
| 5343 | Yasuhiko Inoue | 15.61 | 6.3.8.2.2 | It is not clear whether the VHT Capabilities parameter of the MLME-REASSOCIATE.request includes only contents of the VHT Capabilities Info field or the contents of VHT Capabilities Info field and VHT Supported MCS Set field. | Clarify, please. |
| 5344 | Yasuhiko Inoue | 16.47 | 6.3.8.3.2 | It is not clear whether the VHT Capabilities parameter of the MLME-REASSOCIATE.confirm includes only contents of the VHT Capabilities Info field or the contents of VHT Capabilities Info field and VHT Supported MCS Set field. | Clarify, please. |
| 5345 | Yasuhiko Inoue | 17.34 | 6.3.8.4.2 | It is not clear whether the VHT Capabilities parameter of the MLME-REASSOCIATE.indication includes only contents of the VHT Capabilities Info field or the contents of VHT Capabilities Info field and VHT Supported MCS Set field. | Clarify, please. |
| 5346 | Yasuhiko Inoue | 18.22 | 6.3.8.5.2 | It is not clear whether the VHT Capabilities parameter of the MLME-REASSOCIATE.response includes only contents of the VHT Capabilities Info field or the contents of VHT Capabilities Info field and VHT Supported MCS Set field. | Clarify, please. |

| 5347 | Yasuhiko Inoue | 20.07 | 6.3.11.2.2 | It is not clear whether the VHT Capabilities parameter of the MLME-START.request includes only contents of the VHT Capabilities Info field or the contents of VHT Capabilities Info field and VHT Supported MCS Set field. | Clarify, please. |
| --- | --- | --- | --- | --- | --- |
| 5348 | Yasuhiko Inoue | 20.11 | 6.3.11.2.2 | It is not clear whether the VHT Operation parameter of the MLME-START.request includes only contents of the VHT Operation Info field or the contents of VHT Operation Info field and VHT Basic MCS Set field. | Clarify, please. |

Discussion:

I believe it is intended to be the entire element, like every other parameter that cites an element.

The question is whether we need to make this more obvious.   If we decide so, we are potentially saying that every other parameter that cites an element without calling out the entire element in some way is open to mis-interpretation. The wording in HT Capabilities is almost identical.

Proposed resolution (to all):

Rejected.  The wording used here parallels that of REVmb D12 for the HT Capabilities element (see 131.48).   The VHT Capabilities parameter is intended to specify the entire contents of the VHT Capabilities element, not some subset of it.

| 4017 | Adrian Stephens | 12.06 | 6.3.7.2.2 | "that are supported by the MAC entity"The capabilities are not solely the properties the MAC. Things like which MCSs are supported are clearly a PHY function. | Replace "MAC entity" by "STA"; or remove "by the MAC entity".Make change globally in this context in Clause 6. |
| --- | --- | --- | --- | --- | --- |

Context: 12.06:

Proposed change: (to Description)

Specifies the parameters in the VHT

Capabilities element that are supported by

the STA. The parameter is present if

dot11VHTOptionImplemented is true and is

absent otherwise.

Proposed Resolution:

Revised.   Change “MAC entity” to STA at: 12.06,  13.09,  14.08, 15.08, 15.64, 16.49, 17.36, 18.24, 20.18, 20.27, 38.21, 40.38

| 5483 | Zhendong Luo | 12.33 | 6.3.7.3.2 | The term "RMEnabledCapabilities" is not clearly defined. Refer to the standards of IEEE802.11-2007,IEEE802.11k-2008 and 802.11n-2009, which the "RRM" means "Radio Resource Measurement".We propose here should either give the definition of "RM" or change th | "RMEnabledCapabilities" here should be changed into "RRMEnabledCapabilities" in subclause "6.3.7.3.2", and the same for "6.3.7.4.2", "6.3.7.5.2","6.3.8.3.2","6.3.8.4.2","6.3.8.5.2" |
| --- | --- | --- | --- | --- | --- |

Propose Resolution:

Rejected.

As identified at 1.47, this amendment is based on P802.11REVmb D12.  During its life-time REVmb modified the “RRM” terminology, which was used inconsistently in 802.11k, to “RM”.   802.11ac D2 correctly quotes its baseline at the cited location.

| 4548 | Dorothy Stanley | 14 | 6.3.7.5.2 | Entry "QMFPolicy" from 11ae is missing in the list of entries in the base text | Insert "QMFPolicy" after "QoSMapSet," P14L45.Similarly in 6.3.8.3.2 and 6.3.8.5.2, also entry missing in 6.3.11.2.2 |
| --- | --- | --- | --- | --- | --- |

Proposed Resolution:

Accepted.

| 4273 | Brian Hart | 19.62 | 6.3.11.2.2 | Extended BSS Load and Extended Power Constraint change during BSS lifetime, so need to passed via more than just the start request. | Find a better interface - e.g. a) generated entirely inside MLME, b) sent via MIB variable, c) some other SME-driven config operation. Check what happened for Legacy Power constraint and BSS Load elements |
| --- | --- | --- | --- | --- | --- |

Status:

It is known that these elements are dynamic,  so a change to the START.request is not adequate.

Assign to Brian Hart.

Discussion:

On the Extended BSS Load:   Looking at REVmb, there are no interfaces or MIB variables supporting “BSS Load”.  I think the assumption is that the MLME determines values for the BSS load based on its own internal observations.   The same should apply for the Extended BSS Load.

This means that the Extended BSS Load should be removed from 19.62, but it it not necessary to add anything elsewhere.

On Extended Power Constraint:

Looking at REVmb usage for “Power Constraint”, it is present:

- In the Beacon frame

- In probe responses

- In timing advertisement frames

- In the TIMING ADVERTISEMENT sap primitives

- Not in the START.request

- Not in the MIB

- Not in the BSSDescription table

So it appears to be “magically known” by the MLME when transmitting

The same is, of course, true for the Extended Power Constraint.

So the question is whether we fix one or both of them.   The proposed resolutions does this.

Note, it also shows that these elements are “adopted” if present in an IBSS.

Proposed Resolution:

Revised.

The Extended BSS Load is generated internal to the MLME,  like the BSS Load.

Editor:  at 19.62,  remove the Extended BSS Load parameter.

The Extended Power Constraint and Power Constraint are both present in Beacons and Probe Response, and there is no interface through which they can be supplied.

Editor:  copy 6.3.11.2.2 (MLME-START.request) from REVmb D12, then insert Power Constraint and Extended Power Constraint parameters.

Add the following entry to the table in 6.3.11.2.2:

Power Constraint / Power Constraint element / as defined in 8.4.2.16 /  The Power Constraint element contains the information necessary to allow a STA to determine the local maximum transmit power in the current channel.  Present if

dot11SpectrumManagementRequired is true and is optionally present if dot11RadioMeasurementActivated is true.

Extended Power Constraint / Extended Power Constraint element / as defined in 8.4.2.165 /  The Extended Power Constraint element contains the information necessary to allow a STA to determine the local maximum transmit power in the current channel when the channel width is 80 MHz or more.  Present if dot11VHTOptionImplemented is true, the STA Channel Width subfield of the VHT Operation element indicates a channel width of 80 MHz or wider, and dot11SpectrumManagementRequired is true. Optionally present if dot11VHTOptionImplemented is true, the STA Channel Width subfield of the VHT Operation element indicates a channel width of 80 MHz or wider, and dot11RadioMeasurementActivated is true.

At 6.3.3.3.2  (BSSDescription table) add two entries:

Power Constraint / Power Constraint element / as defined in 8.4.2.16 /  The Power Constraint element contains the information necessary to allow a STA to determine the local maximum transmit power in the current channel.  Present if

dot11SpectrumManagementRequired is true and is optionally present if dot11RadioMeasurementActivated is true. / Adopt

Extended Power Constraint / Extended Power Constraint element / as defined in 8.4.2.165 /  The Extended Power Constraint element contains the information necessary to allow a STA to determine the local maximum transmit power in the current channel when the channel width is 80 MHz or more.  Present if dot11VHTOptionImplemented is true, the STA Channel Width subfield of the VHT Operation element indicates a channel width of 80 MHz or wider, and dot11SpectrumManagementRequired is true. Optionally present if dot11VHTOptionImplemented is true, the STA Channel Width subfield of the VHT Operation element indicates a channel width of 80 MHz or wider, and dot11RadioMeasurementActivated is true. / Adopt

| 4274 | Brian Hart | 20.34 | 6.3.11.2.2 | Power constraint is also optionally present if dot11RadioMeasurementActivated is true | Optionally allow if dot11RadioMeasurementActivated is true |
| --- | --- | --- | --- | --- | --- |

Status:  Assigned to Brian to resolve with 4273.

Discussion:

This is the case for the Power Constraint, so Extended Power Constraint should mirror.

Also note that the insertion in BSSDescription of Extended Power Constraint have already been adjusted to allow this.  So we only have to change existing instances in Clause 6.

Proposed resolution:

Revised.  At 20.34,  at the end of the Description add:  “Optionally present if dot11VHTOptionImplemented is true, the STA Channel Width subfield of the VHT Operation element indicates a channel width of 80 MHz or wider, and dot11RadioMeasurementActivated is true.”

| 4018 | Adrian Stephens | 19.64 | 6.3.11.2.2 | The inserted parameter "Extended BSS Load" does not have a table entry | Add a description of this parameter at 20.35, or remove it. |
| --- | --- | --- | --- | --- | --- |

| 5406 | Yusuke Asai | 20.35 | 6.3.11.2.2 | A row corresponding to "Extended BSS Load" is missed in the associated table. | "Add a row for ""Extended BSS Load"" with the following parameters:- Name: Extended BSS Load- Type: As defined in Extended BSS Load element- Valid range: As defined in 8.4.2.162 (Extended BSS Load element)- Description: Provide the information on band |
| --- | --- | --- | --- | --- | --- |

Discussion:

See CID 4273.

Proposed resolution:

Revised.  Delete cited parameter at 19.64.

(Note to editor, this is a subset of changes made by CID 4273)

| 4275 | Brian Hart | 20.36 | 6.3.11.2.2 | Allowed MCS values are actually more constrained than this, due to the more efficient encoding adopted in 11ac. And note a desire to crop the basic rates from below | Don't provide more flexibility at the interface than the MLME can deliver |
| --- | --- | --- | --- | --- | --- |

Discussion:

The issue arises because the MLME interface described MCSs as a “set” (which nicely matches the HT feature, but not the VHT feature).  Worse,   the type is given as a “set of integers”, which seems hardly applicable.

As to “note a desire to crop the basic rates from below”, I understand Brian intends to bring a presentation on this concept.   Assuming that this comment is not the entire “hook” for that presentation,  I don’t think we need to address this point in this comment resolution.   If this resolution is somehow inconsistent with what Brian want’s then he’ll need to revise it.

Context:   existing description:

Propose resolution:

Revised.   At 20.36,   replace “Set of integers” with,

“Set of (MCS, number of spatial stream) tuples, constrained so that the MCS values are expressable using the encoding described for the VHT Basic MCS Set field in 8.4.2.161.”

Make same change at 10.33

At 10.40, 11.15, and 20.41 replace “Set of integers” with,

“Set of (MCS, number of spatial stream) tuples, constrained so that the MCS values are expressable using the encoding described for the VHT Supported MCS Set field in 8.4.2.160.3.”

And replace:  “As defined for the VHT Basic MCS Set field in 8.4.2.161 (VHT Operation element)” with

“As defined in the Rx MCS Map and Rx Highest Supported Data Rate fields in the VHT Supported MCS field in 8.4.2.160.3.”

| 4516 | David Hunter | 20.4 | 6.3.11.2.2 | The last cell on this line and line 48 do not contain the usual text specifying when the related parameter is present in the primitive invocation. | On this line and line 48 include specifications of when these parameters are present. |
| --- | --- | --- | --- | --- | --- |

Proposed resolution:

Revised.   At the end of the descriptions at 20.40 and 20.48 add:  “Present when dot11VHTOptionImplemented is true; otherwise, this parameter is not present.”

| 5367 | Yongho Seok | 20.49 | 6.3.11 | Add Quiet Channel element into MLME-START.request primitive. | As per comment. |
| --- | --- | --- | --- | --- | --- |

Status:  Assigned to Brian Hart.

Discussion:

The quiet channel element is dynamic,  so the start.request is not adequate.

Admittedly, we don’t have an MLME interface that adequately describes there the Quiet Element comes from,  and in the IBSS case,  we can have a static Quiet Element.   But that doesn’t resolve the issue of where it comes from when it is dynamic,  and surely any interface that supports the dynamic infrastructure BSS case will also support the IBSS case.

| 5008 | Robert Stacey | 21.07 | 6.5.4.1 | This primitive needs an aCCAMidTime parameter | Add one |
| --- | --- | --- | --- | --- | --- |

Proposed Resolution:

Revised. At 21.25 add the following new row:

aCCAMidTime / integer / For Clause 22 PHYs,  the maximum time (in microseconds) the CCA mechanism has available to assess the medium to determine whether an IEEE 802.11 transmission is present on a non-primary channel.

| 4019 | Adrian Stephens | 21.14 | 6.5.4.1 | The description of a aCCAtime incorrectly quotes the baseline, which describes it as a minimum. I don't see why the definition needs to be changed for VHT. The VHT CCA section describes how CCA is performed, and there is no need to attempt to summarise it here. | Delete all changes to 6.5.4.1, or at least correctly quote the baseline. |
| --- | --- | --- | --- | --- | --- |

Discussion:

REVmb D12 399.12:

REVmb changed the description late in its life from “minimum” to “maximum”.

So TGac doesn’t have to create this distinction.

However the commenter’s point about “don’t see why it needs to be changed for VHT” is incorrect, as the timing of determination of CCA on non-primary channels is subject to different constraints.

Current text:

For Clause 14-21 PHYs, tThe minimum time (in microseconds) the CCA mechanism has available

to assess the medium within every time slot to determine whether the medium is busy or idle.;

otherwise the maximum time (in microseconds) that the CCA mechanism has available to detect

the start of a valid 802.11 transmission within the primary channel and to assess the energy on the

medium within the primary, secondary, secondary40 and secondary80 channels that fall

inside the operating channel, in order to determine the values of the STATE and channel-list

parameters of the PHY-CCA.indication primitive.

It is arguable that the description of energy detect applies also to 802.11n,  and therefore could be described in terms of “non-primary” or “secondary” channels.

However, the minimum change that satisfies the inconsistency is the following:

For Clause 14-21 PHYs, tThe maximum time (in microseconds) the CCA mechanism has available

to assess the medium within every time slot to determine whether the medium is busy or idle.;

otherwise the maximum time (in microseconds) that the CCA mechanism has available to detect

the start of a valid 802.11 transmission within the primary channel and to assess the energy on the

medium within the primary, secondary, secondary40 and secondary80 channels that fall

inside the operating channel, in order to determine the values of the STATE and channel-list

parameters of the PHY-CCA.indication primitive.

Proposed resolution:

Revised.  at 21.14 Change “minimum” to “maximum”.  Note this is a change without markup, because it corrects the quoting of the baseline.

| 4517 | David Hunter | 21.42 | 6.5.8.1 | If "user" here is not the same as "user" in "user priority", "remote authentication dial-in user service" and "methods for users to access emergency services" (all of which are in 11mb), then this new use of "user" needs to be defined. Is this "user" really referring to a person who sends and receives information? Is a "multiple user" someone we'll soon find walking down the street? (Or maybe just in dark alleys?) | Either define this new usage of "user" (which appears not to be found in 11mb), or, better, replace it with a more descriptive name. |
| --- | --- | --- | --- | --- | --- |

Proposed resolution:

Reject.  “User” here is used (albeit implicitly) in the context of “multi-user” and “single user”.

Google shows ~3M hits on “multi-user” MIMO and ~1M on “single-user MIMO”.

The .11ac draft has ~260 occurrences of “MU” standing for “multi-user” and 160 occurrences of SU standing for “single-user”.

The terminology is used extensively in this context both externally and within 802.11ac, so no change to the “user” terminology is warranted.

“User” in the context of SU and MU MIMO is also provided with a definition at 5.42.

To address commenter’s final points: “user” identifies a component part of a multi-user transmission.  At various points in the PHY receiver this is a group of related space-time streams, a group of related spatial streams,  or related octets that comprise a single PSDU.  Moving further up the 7-layer model, the model stops short of the human layer,  so it is out of scope of the ISO 7-layer model, and certainly out of scope of the P802.11ac to determine whether a person actually receives any information.  It is also outside the scope of P802.11ac to speculate on whether multiple-users will be found either shortly or at any future time walking in any location, such locations being either dark or not.

# Text boxes

Abstract

This submission contains proposed comment resolutions to comments received during WG letter ballot 187.

The 27 comments included are assigned to the Author, and cover topics in Clause 6.  They are:

5402,  5335,  5404,  4547,  5337,  4017,  5483,  5338,  4548,  5339,  5341,  5343,  5344,  5345,  5346,  4273,  4018,  5347,  5348,  4274,  5406,  4275,  4516,  5367,  5008,  4019,  4517

R1:  Reviewed with Mark Rison

R2: Updated during TGac ad-hoc Thursday pm session.