## Slide 1: Passive Scanning Enhancements
Date: 2012-02-28
Authors:

## Slide 2: Abstract
The presentation defines mechanisms to coordinate the total amount of scanning frames, i.e. consider both aperiodic and periodic scanning frame transmissions.
The cooperation mechanisms of the periodical scanning frames transmission are provided.
The target is to avoid too frequent transmissions of scanning frames and to reduce the amount of frames that are transmitted for passive scanning.

## Slide 3: Recap, scanning mechanisms as seen by a scanning STA
Passive scanning: The STA listens at a channel and detects the availability of the APs from the received frames
  Especially Beacons, Measurement Pilots and Probe Responses have a good set of information for the scanning STA
Active scanning: The STA requests for responses. The STA receives all frames, and it detects availability of the AP from the received frames
  A response to the request indicates that the request is received
  The same set of frames is used for AP availability detection as in the passive scanning. Especially at the idle channels, the active scanning discovers the available BSSs faster than the passive scanning

## Slide 4: Current assumptions of the passive scanning
The passive scanning relies on periodical transmissions of the Beacon and Measurement Pilot frames
  Both frames are transmitted according to precise transmission schedule, i.e. transmission is done at the target transmission time
The frequent transmission of Measurement Pilot (a subset of the Beacon frames) shortens the duration to obtain the operation parameters of the BSS
  On the other hand, the frequent transmissions of periodic messages create overhead

## Slide 5: Recap, beacon as an indication of BSS existence
Beaconing is a very profound operation to maintain the operation and existence of a BSS:
  Beacon communicates the operating parameters of the BSS
  Beacon provides information of the buffered traffic and indicates the availability of the BSS
Beacons should be transmitted periodically at the precise time
  The Beacon transmission should not be cancelled, because it may increase the stand-by power consumption of the power saving STAs

## Slide 6: Recap, Multiple BSSID Set
The Multiple BSSID Set element indicates that all APs reported in the Multiple BSSID Set element transmit using common class, channel and antenna connector
  These BSSs use the same HW (lower MAC and PHY)
The operation parameters of all BSSs in Multiple BSSID Set may be obtained from the same Beacon and Probe Response frame

## Slide 7: Recap, Measurement Pilot
Measurement Pilot frames are transmitted as ”small Beacon” frames
  Measurement Pilot frames may contain any information elements
The Measurement Pilot frames are transmitted periodically, typically more frequently than Beacons.
  Precise rules for selecting the periodicity are given in clause 10.11.5.2
  The Measurement Pilot is not transmitted, if:
  The BSSs in the Multiple BSSID Set may transmit own Beacons. These cancel Measurement Pilot transmissions as shown below

## Slide 8: Disadvantages of the Measurement Pilot
The Measurement Pilot does not consider transmission of Probe Response
  Measurement Pilot may be transmitted just after a Probe Response
Obtaining the periodicity may be difficult when many APs operate at the same coverage
  Why is the periodical interval needed for the Measurement Pilot?
The Measurement Pilot may contain only information of the APs in single Multiple BSSID Set
  When neighbor APs are located closely, the amount of overhead and/or delay for passive scanning increases
  The operating parameters of neighbor APs should be available in the Measurement Pilot to reduce the number of transmitted frames

## Slide 9: Recap, Passive scanning STAs benefit from Probe Responses
A Probe Request frame may be transmitted to solicit Probe Response frames from the BSSs within the range
The Probe Response frames may provide valid information to all scanning STAs
  These frames provide similar information to the Beacon and Mesurement Pilot frames
A Probe Response frame transmission should cancel Measurement Pilot frame transmission that is due very shortly
  Transmission of two very similar frames within a short time period is unnecessary overhead

## Slide 10: Improvements to passive scanning
An AP may transmit Measurement Pilot frame, if the AP has not transmitted a Beacon, Probe Response or Measurement Pilot frame within dot11MaxTXScanInterval
A Beacon is transmitted instead of the Measurement Pilot frame , if the TBTT of the AP is within dot11BeaconResponseDuration of the Measurement Pilot frame transmission time
Beacon
Time
Measurement Pilot
Probe Response
dot11MaxScan-TXInterval

## Slide 11: Benefits of dot11MaxTxScanInterval
The dot11MaxTxScanInterval avoids the Measurement Pilot transmission just after Probe Response
  Measurement Pilot frame is transmitted to fill the gaps between Beacon and Probe Response frames
The constant maximum interval between transmitted Measurement Pilot, Probe Response and Beacon frames is maintained
  This helps the scanning STAs to shorten the passive scanning duration

## Slide 12: Operation of FILS enhanced scanning
Two main scanning related tasks:
Reception of the BSS operating parameters
  Information of whether the scanning STA is allowed to associate with the AP
  Information of the congestion level and capabilities of the AP
Assessing the BSS radio link quality
  STA assesses the radio link quality between itself and the AP
All this information is needed, but it doesn’t need to be obtained from the same frame

## Slide 13: Collaboration to reduce the amount of scanning messages
Within the range there may be multiple APs
  The transmitted scanning related messages, Beacon, Probe Response and Measurement Pilot frames should contain neighboring BSSs information
The APs which are able to serve new associated STAs should be more discoverable than congested APs
  The discovery frames should be transmitted more often from available APs
    The transmission times of the passive scanning related messages may be varied to make a tradeoff between transmission overhead and discovery time
  The discovery frames should direct the STAs to associate to the best candidate AP

## Slide 14: Improvements to passive scanning
An AP may transmit Measurement Pilot frame, if it has not received or transmitted a Beacon, Probe Response or Measurement Pilot frame containing the information of the BSS within dot11MaxTXScanInterval
The collaboration between APs to transmit BSS information helps to further reduce the transmissions of Measurement Pilot frames
  See the example on the following slide

## Slide 15: Summary, two alternatives to reduce the amount of Measurement Pilot frames
When the AP ensures fast discovery for the whole coverage (as described in slides 10 & 11):
  An AP may transmit Measurement Pilot frame, if the AP has not transmitted a Beacon, Probe Response or Measurement Pilot frame within dot11MaxTXScanInterval
When the AP focuses on overhead reduction through collaboration (as described in slide 14):
  An AP may transmit Measurement Pilot frame, if the AP has not received or transmitted a Beacon, Probe Response or Measurement Pilot frame containing the information of the BSS within dot11MaxTXScanInterval
Both alternatives should be available to ensure flexibility for scanning frames transmission

## Slide 16: Appendix: calculation on number of Measurement Pilot transmissions
In the example, 4 APs are within the same coverage
  Each AP transmits a Beacon between 100ms
  APs transmit Measurement Pilots to enable a Beacon or Measurement Pilot frame transmission between 20 ms
The following slides introduce the scenarios in more details
Frame type | Size in octets | Transmission duration [micro seconds] @ 6 Mbit/s
Beacon, only transmitter’s information | 145 | 216
Measurement Pilot, only transmitter’s information | 87 | 136
Beacon, including parameters of two APs | 265 | 376
Measurement Pilot, including parameters of two APs | 207 | 296

## Slide 17: Appendix: Case 1, current Measurement Pilot transmission
  Each AP transmits a Beacon between 100ms
    A Beacon contains only parameters of the transmitting STA
    40 Beacons are transmitted in a second, 8.640 microseconds (0,864% of total time) is consumed for Beacon transmission
Each AP transmits a Measurement Pilot between 20 ms, Beacon cancels transmission of every fifth Measurement Pilot
  A Measurement Pilot contains only parameters of the transmitting STA
  160 Measurement Pilots are transmittted in a second, 21.760 microseconds (2,176% of the total time) is consumed for Measurement Pilot transmission

## Slide 18: Appendix: Case 1, current Measurement Pilot transmission
Totally 200 frames are transmitted and ~ 3% of total transmission time is consumed
A frame is transmitted between every 5ms
  The frequent transmission of small frames easily causes collisions and lowers the throughput
AP1
AP2
AP3
AP4
TBTT =100ms
TMPTT =20ms

## Slide 19: Appendix: Case 2, collaborative Measurement Pilot transmission
  Each AP transmits a Beacon between 100ms
    A Beacon contains only parameters of all four STAs
    40 Beacons are transmitted in a second, 15.040 microseconds (1,504% of total time) is consumed for Beacon transmission
Information of the AP is transmitted every 20ms. One Measurement Pilot per 100 ms is transmitted
  A Measurement Pilot contains parameters of all four STAs
  10 Measurement Pilots are transmittted in a second, microseconds, 2.960 microseconds (0,296 % of the total time) is consumed for Measurement Pilot transmission

## Slide 20: Appendix: Case 2, collaborative Measurement Pilot transmission
Totally 50 frames are transmitted and ~ 1,8 % of total transmission time is consumed
Especially the reduced number of transmitted frames avoids transmission collisions
AP1
AP2
AP3
AP4
TBTT =100ms
  dot11MaxTXScanInterval = 25ms
  The fastest AP transmits the Measurement Pilot, or different dot11MaxTXScanIntervals may be used in APs

## Slide 21: Appendix: Comparision between current and collaborative Measurement Pilot transmission schemes
Current scheme:
  Totally 200 frames are transmitted and ~ 3% of total transmission time is consumed
  On average a frame is transmitted between every 5ms
Cooperative scheme:
  Totally 50 frames are transmitted and ~ 1,8% of total transmission time is consumed
  On average a frame is transmitted between every 20 ms

## Slide 22: Motions for specification framework document (Voting at Hawaii F2F meeting)
Motion 1.
The FILS enhanced scanning mechanisms shall reduce overhead of the Measurement Pilot frames transmission.
Yes
No
Abstain

## Slide 23: Motions for specification framework document (Voting at Hawaii F2F meeting)
Motion 2.
The Measurement Pilot frame shall contain information of transmitting BSS and may contain information of neighbor BSSs.
Yes
No
Abstain

## Slide 24: Motions for specification framework document (Voting at Hawaii F2F meeting)
Motion 3.
When dot11MaxTXScanInterval is set, the AP may transmit Measurement Pilot frame according to following alternatives:
An AP may transmit Measurement Pilot frame, if the AP has not transmitted a Beacon, Probe Response or Measurement Pilot frame within dot11MaxTXScanInterval
  An AP may transmit Measurement Pilot frame, if the AP has not received or transmitted a Beacon, Probe Response or Measurement Pilot frame containing the information of the BSS within dot11MaxTXScanInterval
Yes
No
Abstain

## Slide 25: References
11-1619r3 Active Scanning
12-153r5 Active Scanning Requirements
12-42r0 FILS Beacon Proposal
12-206r0 Necessity of Probe reduction in FILS