## Slide 1: Passive Scanning Enhancements
Date: 2012-03-13
Authors:

## Slide 2: Abstract
The presentation defines mechanisms to coordinate the total amount of scanning frames, i.e. consider both aperiodic and periodic scanning frame transmissions.
The presentation explains different alternatives for periodically transmitted passive scanning frame (TBD).
The presentation explains, why the transmission mechanism for Measurement Pilot should not be changed.
The presentation enables cooperation mechanisms to add information of neighbor BSSs to any transmitted scanning frame.
This enables faster obtaining of the BSSs parameters.

## Slide 3: Recap, scanning mechanisms as seen by a scanning STA
Passive scanning: The STA listens at a channel and detects the availability of the APs from the received frames
  Especially Beacons, Measurement Pilots and Probe Responses have a good set of information for the scanning STA
Active scanning: The STA requests for responses. The STA receives all frames, and it detects availability of the AP from the received frames
  A response to the request indicates that the request is received
  The same set of frames is used for AP availability detection as in the passive scanning. Especially at the idle channels, the active scanning discovers the available BSSs faster than the passive scanning

## Slide 4: Currently available periodical frame transmissions for passive scanning
The passive scanning relies on periodical transmissions of the Beacon and Measurement Pilot frames
  Both frames are transmitted according to precise transmission schedule, i.e. transmission is done at the target transmission time
The frequent transmission of Measurement Pilot (a subset of the Beacon frames) shortens the duration to obtain the operation parameters of the BSS
  On the other hand, the frequent transmissions of periodic messages create overhead

## Slide 5: Recap, beacon as an indication of BSS existence
Beaconing is a very profound operation to maintain the operation and existence of a BSS:
  Beacon communicates the operating parameters of the BSS
  Beacon provides information of the buffered traffic and indicates the availability of the BSS
Beacons should be transmitted periodically at the TBTT
  The Beacon transmission should not be cancelled, because it may increase the stand-by power consumption of the power saving STAs
Open question: Does it harm to transmit Beacons more often without precise interval?

## Slide 6: Recap, Multiple BSSID Set
The Multiple BSSID Set element indicates that all APs reported in the Multiple BSSID Set element transmit using common class, channel and antenna connector
  These BSSs use the same HW (lower MAC and PHY)
The operation parameters of all BSSs in Multiple BSSID Set may be obtained from the same Beacon and Probe Response frame

## Slide 7: Recap, Measurement Pilot
Measurement Pilot frames are transmitted as ”small Beacon” frames
  Measurement Pilot frames may contain any information elements
The Measurement Pilot frames are transmitted periodically, typically more frequently than Beacons.
  Precise rules for selecting the periodicity are given in clause 10.11.5.2
  The Measurement Pilot is not transmitted, if:
  The BSSs in the Multiple BSSID Set may transmit own Beacons. These cancel Measurement Pilot transmissions as shown below

## Slide 8: Recap, Measurement Pilot
The Frame structure of Measurement Pilot frame is shown below

## Slide 9: Disadvantages of the Measurement Pilot
The Measurement Pilot does not consider transmission of Probe Response
  Measurement Pilot may be transmitted just after a Probe Response
Obtaining the Measurement Pilot transmission periodicity may be difficult when many APs operate at the same coverage
The Measurement Pilot may contain only information of the BSSs
  Multiple BSS indicates the number of BSSs in the AP
  The operating parameters of neighbor APs should be available in the Measurement Pilot to reduce the number of transmitted frames

## Slide 10: Recap, Measurement Pilot
The Measurement Pilot has been in 802.11 standards since 802.11k
  It has been available for many years
The precise transmission interval of the Measurement Pilot enables passive scanning STAs to switch the channel at precise time to get a transmission from the BSS
The frame structure of the Measurement Pilot frame is quite limited
  Subelements may be added to the Measurement Pilot frame, while elements may be added to Probe Response

## Slide 11: Recap, Passive scanning STAs benefit from Probe Responses
A Probe Request frame may be transmitted to solicit Probe Response frames from the BSSs within the range
    A STA may receive Probe Response at any time, i.e. The STA may not receive Probe Request prior to Probe Response
The Probe Response frames may provide valid information to all scanning STAs
  Broadcasted Probe Response provides similar set of information as Beacon
  Mesurement Pilot provides subset of the information
More discussion needed to select the optimal frame for passive scanning

## Slide 12: Improvement to passive scanning
An AP may transmit passive scanning frame (TBD), if the AP has not transmitted a Beacon, Probe Response or Measurement Pilot frame within dot11MaxTXScanInterval
Beacon
Time
Passive Scanning frame (TBD)
Probe Response
dot11MaxScan-TXInterval

## Slide 13: Filling the gaps vs. Measurement Pilot transmission mechanism
Measurement Pilot targets to maintain very precise transmission interval
  The Passive scanning frame (TBD) targets to fill gaps between the scanning messages
  Cancelling Measurement Pilot transmission due to recently received Probe Response may not be backward compatible
    The passive scanning STAs may switch the channel to receive the Measurement Pilot transmitted at precise time

## Slide 14: Benefits of dot11MaxTxScanInterval
The dot11MaxTxScanInterval avoids too frequent Probe Response
  Unsolicited Probe Response frame is transmitted to fill the gaps between any combination of Beacon, Measurement Pilot and/or Probe Response
The value of dot11MaxTxScanInterval is included to Measurement Pilot, Probe Response and Beacon
  The knowledge of the max transmission periodicity helps the scanning STAs to shorten the passive scanning duration
  The field indicates that BSS transmits Passive scanning frame (TBD)

## Slide 15: Operation of FILS enhanced scanning
Two main scanning related tasks:
Reception of the BSS operating parameters
  Information of whether the scanning STA is allowed to associate with the AP
  Information of the congestion level and capabilities of the AP
Assessing the BSS radio link quality
  STA assesses the radio link quality between itself and the AP
All this information is needed, but it doesn’t need to be obtained from the same frame

## Slide 16: Collaboration to reduce the amount of scanning messages
Within the range there may be multiple APs
  The transmitted scanning related messages, Beacon, Probe Response and Measurement Pilot frames should contain neighboring BSSs information
The APs which are able to serve new associated STAs should be more discoverable than congested APs
  The discovery frames should be transmitted more often from available APs
    The transmission times of the passive scanning related messages may be varied to make a tradeoff between transmission overhead and discovery time
  The discovery frames should direct the STAs to associate to the best candidate AP

## Slide 17: Improvements to passive scanning
An AP may transmit an passive scanning frame (TBD), if it has not received or transmitted a Beacon, Probe Response or Measurement Pilot frame containing the information of the BSS within dot11MaxTXScanInterval
The collaboration between APs to transmit BSS information helps to further reduce the transmissions of scanning frames
  The selection in cooperation is tradeoff between medium consumption vs. discoverability of the AP

## Slide 18: AP collaboration in passive scanning
The passive scanning frames are transmitted periodically without very strict real time requirements
  The APs learn the APs in their coverage
  The APs may setup rules for cooperating with passive scanning related frames transmission
The avoidance of too frequent passive scanning frame (TBD) transmission reduces medium time consumption
  The cancelation of the passive scanning frame transmission

## Slide 19: Summary, two alternatives to reduce the amount of scanning frames (TBD)
When the AP ensures fast discovery for the whole coverage (as described in slides 11 & 12):
  An AP may transmit unsolicited Probe Response, if the AP has not transmitted a Beacon, scanning frame (TBD), Probe Response or Measurement Pilot frame within dot11MaxTXScanInterval
When the AP focuses on overhead reduction through collaboration (as described in slide 17):
  An AP may transmit scanning frame (TBD), if the AP has not received or transmitted a Beacon, scanning frame (TBD), Probe Response or Measurement Pilot frame containing the information of the BSS within dot11MaxTXScanInterval
Both alternatives should be available to ensure flexibility for scanning frames transmission

## Slide 20: Appendix: calculation on number of scanning frame (TBD)
In the example, 4 APs are within the same coverage
  Each AP transmits a Beacon between 100ms
  APs transmit scanning frame (TBD) to enable a Beacon or scanning frame (TBD) transmission between 20 ms
The following slides introduce the scenarios in more details
Frame type | Size in octets | Transmission duration [micro seconds] @ 6 Mbit/s
Beacon or scanning frame (TBD), only transmitter’s information | 145 | 216
Beacon, or scanning frame (TBD) including parameters of four APs | 265 | 376
Only the TX ON time is calculated

## Slide 21: Appendix: Case 1, Each AP transmits own scanning frame (TBD)
  Each AP transmits a Beacon between 100ms
    A Beacon contains only parameters of the transmitting STA
    40 Beacons are transmitted in a second, 8.640 microseconds (0,864% of total time) is consumed for Beacon transmission
Each AP transmits a scanning frame (TBD) between 20 ms, Beacon cancels transmission of every fifth scanning frame (TBD)
  A scanning frame (TBD) contains only parameters of the transmitting STA
  160 Measurement Pilots are transmittted in a second, 34.560 microseconds (3,456% of the total time) is consumed for Measurement Pilot transmission

## Slide 22: Appendix: Case 1, Each AP transmits own scanning frame (TDB)
Totally 200 frames are transmitted and ~ 4,3% of total transmission time is consumed
A frame is transmitted between every 5ms
  The frequent transmission of small frames easily causes collisions and lowers the throughput
AP1
AP2
AP3
AP4
TBTT =100ms
dot11MaxTXScanInterval =20ms

## Slide 23: Appendix: Case 2, collaborative scanning frame (TDB) transmission
  Each AP transmits a Beacon between 100ms
    A Beacon contains only parameters of all four STAs
    40 Beacons are transmitted in a second, 15.040 microseconds (1,504% of total time) is consumed for Beacon transmission
Information of the AP is transmitted every 20ms. One unsolicited Probe Response per 100 ms is transmitted
  A Probe Response contains parameters of all four STAs
  10 Probe Responses are transmittted in a second, microseconds, 3.760 microseconds (0,376 % of the total time) is consumed for Probe Response transmission

## Slide 24: Appendix: Case 2, collaborative scanning frame (TDB) transmission
Totally 50 frames are transmitted and ~ 1,9 % of total transmission time is consumed
Especially the reduced number of transmitted frames avoids transmission collisions
AP1
AP2
AP3
AP4
TBTT =100ms
  dot11MaxTXScanInterval = 25ms
  The fastest AP transmits the unsolicited Probe Response, or different dot11MaxTXScanIntervals may be used in APs

## Slide 25: Appendix: Comparision between current and collaborative scanning frame (TDB) transmission schemes
Uncooperative scheme:
  Totally 200 frames are transmitted and ~ 3% of total transmission time is consumed
  On average a frame is transmitted between every 5ms
Cooperative scheme:
  Totally 50 frames are transmitted and ~ 1,8% of total transmission time is consumed
  On average a frame is transmitted between every 20 ms

## Slide 26: Motions for specification framework document
Motion 1) Add the following text to clause 5 of the Specification Framework document:
The Beacon frame shall contain information of transmitting BSS and may contain information of neighbor BSSs.
Moved:
Seconded:
Yes No Abstain

## Slide 27: Motions for specification framework document
Motion 2) Add the following text to clause 5 of the Specification Framework document:
The Measurement Pilot frame shall contain information of transmitting BSS and may contain information of neighbor BSSs.
Moved:
Seconded:
Yes No Abstain

## Slide 28: Motions for specification framework document
Motion 3) Add the following text to clause 5 of the Specification Framework document:
When dot11MaxTXScanInterval is set, the AP may transmit a passive scanning frame (TBD) according to following alternatives:
An AP may transmit a passive scanning frame (TBD), if the AP has not transmitted a Beacon, scanning frame (TBD), Probe Response or Measurement Pilot frame within dot11MaxTXScanInterval
  An AP may transmit a passive scanning frame (TBD), if the AP has not received or transmitted a Beacon, scanning frame (TBD), Probe Response or Measurement Pilot frame containing the information of the BSS within dot11MaxTXScanInterval
Moved: Seconded:
Yes No Abstain

## Slide 29: References
11-1619r3 Active Scanning
12-153r5 Active Scanning Requirements
12-42r0 FILS Beacon Proposal
12-206r0 Necessity of Probe reduction in FILS