## Slide 1: Fast Authentication in TGai
Name | Affiliations | Address | Phone | email
Kiseon Ryu | LG Electronics | 10225 Willow Creek Rd, San Diego, CA, 92131, USA | +1 (858)-635-5209 | kiseon.ryu@lge.com
Giwon Park | LG Electronics | LG R&D Complex 533, Hogye-1dong, Dongan-Gu, Anyang, Kyungki, 431-749, Korea | +82-31-450-1879 | giwon.park@lge.com
Jaehyung Song | LG Electronics | LG R&D Complex 533, Hogye-1dong, Dongan-Gu, Anyang, Kyungki, 431-749, Korea | +82-31-450-7898 | jaehyung.song@lge.com
Jinsam Kwak | LG Electronics | LG R&D Complex 533, Hogye-1dong, Dongan-Gu, Anyang, Kyungki, 431-749, Korea | +82-31-450-7902 | Jinsam.kwak@lge.com
George Cherian | Qualcomm | 5775 Morehouse Dr., San Diego, CA | 8586516645 | gcherian@qualcomm.com
Santosh Abraham | Qualcomm Inc | 5775 Morehouse Dr., San Diego, CA | 858 651 6107 | sabraham@qualcomm.com
Date: 2012-03-03
Authors:

## Slide 2: Abstract
This document proposes optimization of the EAP-RP based fast authentication for FILS.

## Slide 3: Conformance w/ TGai PAR & 5C
Conformance Question | Response
Does the proposal degrade the security offered by Robust Security Network Association (RSNA) already defined in 802.11? | No
Does the proposal change the MAC SAP interface? | No
Does the proposal require or introduce a change to the 802.1 architecture? | No
Does the proposal introduce a change in the channel access mechanism? | No
Does the proposal introduce a change in the PHY? | No
Which of the following link set-up phases is addressed by the proposal? (1) AP Discovery (2) Network Discovery (3) Link (re-)establishment / exchange of security related messages (4) Higher layer aspects, e.g. IP address assignment | 3

## Slide 4: Background
11/1160r6 has proposed using EAP framework for FILS
  Uses the EAP-RP for fast authentication by using a pre-established FILS context (i.e., EMSK, rRK, and rIK) to improve the authentication time during association.
STA can be disassociated with the AP due to several reasons (e.g., STA’s leaving the AP, STA’s inactivity, and etc.,)
However, STA should perform full EAP or EAP-RP procedure whenever coming back to the AP
  Full EAP and EAP-RP requires communication between the STA and the authentication server

## Slide 5: Proposal
STA/AP’s retaining the FILS context after disassociation for the specific time duration
When the time duration has not been expired (i.e., FILS context is retained at both the STA and the AP) and the STA attempts to be associated with the AP, EAP-RP procedure can be omitted during association by using retained FILS context
In this case, backbone signaling between AP and AS for EAP-RP is not necessary for re-authentication

## Slide 6: Optimization of EAP-RP based fast authentication
[step 1]. Full EAP authentication is performed between STA and AP1.
[step 2]. STA disassociates from AP.
[step 3]. STA/AP caches the STA/AP FILS contexts (i.e. PMK and rMSK, and etc.,) during specific time duration after STA’s disassociation/de-authentication.
[step 4]. STA acquires Anonce via Beacon or probe response message.
[step 5]. STA transmits the association request message with, MIC, EAPOL(Snonce, Anonce), If the STA is a previous associated STA and FILS contexts timer is not expired, AP re-use the STA’s FILS contexts (i.e., PMK, rMSK, and etc.,) and performs verification of association request message. If the association request message verification was failed, AP instructs STA to perform the full EAP authentication.
[step 6]. If the association request message verification was successful, AP transmits the association response message to STA. If the STA successfully completed the message verification, it can access AP otherwise, STA shall perform the full EAP authentication procedure with authentication server.

## Slide 7: Optimization of EAP-RP based fast authentication
EAP-RP based fast authentication procedure can be optimized when:
  STA comebacks to the AP with which it was previously associated
STA and AP retains the FILS contexts (e.g., PMK, rMSK, and etc.,) for the specific time duration (e.g., FILS context retain timer) after disassociation.
If the FILS contexts is retained at both STA and AP, EAP procedure can be omitted during re-association.

## Slide 8: Motion for specification framework document (Voting at Hawaii F2F meeting)
Motion
Adopt the proposed text of contribution 11-12-0252-00-00ai or latest version.
Yes
No
Abstain